## Slide 1: JCT3V-E0170: 3D-CE3 related: Motion data buffer reduction for 3D-HEVC
Yi-Wen Chen, Kazushi Sato, Jian-Liang Lin, Tzu-Der Chuang, Yu-Wen Huang, and Shawmin Lei.
Presented by Yi-Wen Chen
5nd JCT3V Meeting in Vienna
27 July – 2 Aug., 2013

## Slide 2: Overall Summary
Require buffers to store the motion data at full resolution when coding the pictures within the AU
Propose to store the motion data of each picture at smaller resolution during the coding within the AU
  Progressive scheme and Immediate scheme
  Reduce motion data buffer and memory access bandwidth
  Small BD-rate increase
The concept was already proposed in JCT3V-B0161
It is recommended that unified scheme be adopted both with SHVC and 3DVC
  In SHVC, the motion data of each picture is already stored at smaller resolution during the coding within the AU

## Slide 3: Motion Compression in HTM-7.0
Motion data of each picture is stored at full resolution during the coding of the pictures within the AU
After all the pictures within the same AU are coded, the 16:1 motion data compression is conducted

## Slide 4: Proposed Progressive Motion Compression
Motion data of each picture is stored at 1/4 resolution during the coding of the pictures within the AU
After all the pictures within the same AU are coded, a 4:1 motion data compression is conducted on the compressed motion data to produce the same results as conventional 16:1 motion compression

## Slide 5: Simulation Results
Anchor : HTM-7.0r1
Test : HTM-7.0r1 with progressive motion compression
Results crosschecked and confirmed in JCT3V-E0259

## Slide 6: Proposed Immediate Motion Compression
Motion data of each picture is directly stored at 1/16 resolution during the coding of the pictures within the AU

## Slide 7: Simulation Results
Anchor : HTM-7.0r1
Test : HTM-7.0r1 with immediate motion compression
Results crosschecked and confirmed in JCT3V-E0259

## Slide 8: Conclusion
Propose to store the motion data in smaller resolution when coding pictures within the AU
  The progressive scheme brings 0.0% BD-rate change
  The immediate scheme brings 0.4% BD-rate increase
Reduced motion data buffer
Reduced memory access bandwidth for r/w motion data
It is recommended that unified scheme be adopted both with SHVC and 3DVC.
  The progressive compression scheme is being investigated under CE in SHVC
  The immediate compression scheme has been already integrated into SHM-2.0

## Slide 9: Thank you for your attention!

## Slide 10: BackUp