## Slide 1: CE3.h related: Fast encoder decision for texture coding
Presented by Yi-Wen Chen
5th JCT-3V Meeting in Vienna
27 July – 2 Aug., 2013
Na Zhang, Yi-Wen Chen, Jian-Liang Lin, Jicheng An, Kai Zhang,Shawmin Lei, Siwei Ma, Debin Zhao, Wen Gao

## Slide 2: Overall Summary
A fast encoding algorithm to encode the texture pictures of dependent views
Two strategies
  Early merge mode decision
    No BD-rate change
    32% encoding time reduction
  Early CU splitting termination
    0.2% BD-rate saving
    39% encoding time reduction
  Combined
    0.1% BD-rate saving
    47% encoding time reduction

## Slide 3: The Proposed Fast Encoding Flow

## Slide 4: Early Merge Mode Decision
Principle: if the following two conditions are true, only merge modes are examined for all PUs within the current CU
  All the five inter-view neighbouring blocks are coded as merge modes.
  The RD performance of skip mode is better than 2Nx2N merge mode for the current CU.

## Slide 5: Results of Early Merge Mode Decision
Anchor : HTM-7.0r1
Test : HTM-7.0r1 with early merge mode decision
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | -0.1% | 0.1% | 0.1% | 0.0% | 71.3% | 104.3% | 100.0%
Kendo | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 71.2% | 98.2% | 100.7%
Newspaper_CC | 0.0% | -0.2% | 0.0% | 0.0% | 0.1% | 0.0% | 66.3% | 99.3% | 97.6%
GT_Fly | 0.0% | 0.2% | -0.1% | 0.1% | 0.1% | 0.0% | 73.5% | 98.5% | 100.5%
Poznan_Hall2 | 0.0% | 0.3% | 0.6% | 0.5% | 0.5% | 0.1% | 61.8% | 98.5% | 96.5%
Poznan_Street | 0.0% | -0.3% | -0.2% | 0.1% | 0.1% | 0.0% | 63.6% | 94.7% | 100.3%
Undo_Dancer | 0.0% | -0.2% | -0.2% | 0.1% | 0.1% | 0.0% | 67.4% | 101.2% | 98.5%
1024x768 | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 69.6% | 100.6% | 99.4%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.2% | 0.2% | 0.0% | 66.5% | 98.2% | 99.0%
average | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 67.9% | 99.2% | 99.2%

## Slide 6: Early CU Splitting Termination
Principle: if the following two conditions are true, no further CU splitting is needed for the current CU.
  The CU splitting depth of the current CU is equal to or larger than the maximum CU splitting depths of the five inter-view neighboring blocks.
  Skip mode is selected as the best prediction mode for the current CU after checking all the possible prediction modes.

## Slide 7: Results of Early CU Splitting Termination
Anchor : HTM-7.0r1
Test : HTM-7.0r1 with early CU splitting termination
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.2% | -0.3% | 0.2% | 0.2% | -0.1% | 62.3% | 103.3% | 101.3%
Kendo | 0.0% | -0.1% | -0.3% | 0.2% | 0.3% | 0.0% | 63.5% | 100.9% | 100.1%
Newspaper_CC | 0.0% | -0.3% | -0.5% | 0.0% | 0.1% | 0.1% | 60.4% | 95.2% | 98.6%
GT_Fly | 0.0% | -1.8% | -2.1% | -0.1% | -0.2% | -0.3% | 64.8% | 96.9% | 99.4%
Poznan_Hall2 | 0.0% | -1.5% | -1.3% | -0.3% | -0.2% | -0.4% | 53.4% | 95.3% | 98.6%
Poznan_Street | 0.0% | -0.9% | -1.0% | -0.1% | -0.1% | -0.2% | 57.9% | 104.5% | 100.6%
Undo_Dancer | 0.0% | -0.8% | -1.0% | 0.0% | 0.0% | -0.1% | 62.8% | 105.7% | 99.3%
1024x768 | 0.0% | -0.2% | -0.3% | 0.1% | 0.2% | 0.0% | 62.0% | 99.8% | 100.0%
1920x1088 | 0.0% | -1.2% | -1.3% | -0.1% | -0.1% | -0.3% | 59.7% | 100.6% | 99.5%
average | 0.0% | -0.8% | -0.9% | 0.0% | 0.0% | -0.2% | 60.7% | 100.2% | 99.7%

## Slide 8: Combined Results
Anchor : HTM-7.0r1
Test : HTM-7.0r1 with the following modifications
  Early merge mode decision
  Early CU splitting termination
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.2% | -0.3% | 0.3% | 0.4% | -0.1% | 54.8% | 101.2% | 99.5%
Kendo | 0.0% | -0.1% | -0.3% | 0.3% | 0.4% | 0.1% | 56.5% | 97.5% | 100.5%
Newspaper_CC | 0.0% | -0.4% | -0.5% | 0.1% | 0.2% | 0.1% | 51.9% | 93.2% | 100.0%
GT_Fly | 0.0% | -1.8% | -2.2% | -0.1% | -0.1% | -0.3% | 57.7% | 99.1% | 98.4%
Poznan_Hall2 | 0.0% | -1.1% | -1.0% | 0.3% | 0.3% | -0.3% | 45.1% | 91.8% | 97.0%
Poznan_Street | 0.0% | -0.9% | -1.0% | 0.0% | 0.1% | -0.2% | 49.0% | 93.9% | 100.0%
Undo_Dancer | 0.0% | -1.0% | -1.2% | 0.1% | 0.1% | -0.1% | 53.8% | 104.4% | 99.8%
1024x768 | 0.0% | -0.2% | -0.4% | 0.2% | 0.3% | 0.0% | 54.4% | 97.3% | 100.0%
1920x1088 | 0.0% | -1.2% | -1.3% | 0.1% | 0.1% | -0.2% | 51.4% | 97.3% | 98.8%
average | 0.0% | -0.8% | -0.9% | 0.1% | 0.2% | -0.1% | 52.7% | 97.3% | 99.3%

## Slide 9: Conclusion
Early merge mode decision
  No BD-rate change
  32% encoding time reduction
Early CU splitting termination
  0.2% BD-rate saving
  39% encoding time reduction
Combined
  0.1% BD-rate saving
  47% encoding time reduction

## Slide 10: Thank you for your attention!