## Slide 1: JCT3V-E0174 3D-CE3.h related: A disparity derived depth coding method in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  Depth values are used to predict disparity vectors.
  Can we use disparity vectors to predict depth values?
Proposed
  A disparity derived depth (DDD) coding method is proposed to improve the coding efficiency for the depth component.
  Utilize the disparity vector in the collocated texture block to derive a depth prediction value for the current depth block
Results
  Achieve 0.22% BD-rate saving for the synthesized views

## Slide 3: The problem
Samples in the depth component are used to derive disparity vectors for texture component coding. (BVSP)
  A disparity vector (DVx, 0) can be derived from its corresponding depth value (dep) by a linear relationship as
  where w and b are two camera parameters
Equ. (1) is implemented in an integer form so w and b can be transmitted from the encoder to the decoder as integers.
Can we use disparity vectors to predict depth values?
(1)

## Slide 4: Proposed
  A disparity derived depth (DDD) coding method is proposed.
  A depth value can also be derived from its corresponding disparity vector (DVx, DVy) as
  When the collocated texture block of the current depth block is predicted by disparity-compensated prediction (DCP)
    A DDD candidate will be inserted into the merging candidate list right after the texture candidate.
    In a DDD candidate, all prediction samples in the current block are set as dep calculated by Equ. (2)
    Equ (2) is implemented in an integer form. The division operation, i.e., 1/w, is calculated only once for a picture.
(2)

## Slide 5: Proposed (Cont.)

## Slide 6: Results
Achieve 0.22% BD-rate saving for the synthesized views
Cross-checked by JCT3V-Exxxx (Thank LG)
CTC

## Slide 7: Conclusion
A disparity derived depth coding method is proposed.
0.22% BD-rate saving for the synthesized views
Suggest to be adopted

## Slide 8: Thank you for your attention!