## Slide 1: JCT3V-E0176 AHG7: An efficient coding method for DLT in 3D-HEVC
Kai Zhang, Fabian Jäger, Jicheng An, Shawmin Lei
A joint proposal by MediaTek Inc. and RWTH Aachen University

## Slide 2: Overall Summary
Problem definition
  Depth lookup table (DLT) is coded in Exp-Golomb code in SPS
  It is inefficient so the size of SPS becomes very large
The proposed DLT coding method
  Enhanced range constrained bit map (ERCBM) for coding DLT
    The DLT is represented by a range constrained bit-map (RCBM) as proposed in JCT3V-C0142 and JCT3V-D0151.
    Differential run-length coding is utilized on RCBM.
    The delta-DLT approach proposed in JCT3V-D0054 is applied on dependent views.
Results
  Reduce more than 90% of the original DLT size

## Slide 3: Problem Definition
DLT is coded in Exp-Golomb code in SPS
DLT requires a large amount of bits
  Statistics on the four sequences enabling DLT, average DLT size is 557.33 bits, and accounts for more than 65% bits in SPS
The worst case of current DLT coding
  If values from 128 to 255 are in DLT, DLT requires 1937 bits
  If values from 0 to 255 are all in DLT, DLT requires 3365 bits
The DLT size of the worst case determines the buffer size

## Slide 4: The Proposed DLT Coding Method (1/3)
An enhanced range constrained bit-map (ERCBM) method
  DLT is represented by a range constrained bit-map as proposed in JCT3V-C0142 and JCT3V-D0151
    The value range [MinDltValue, MaxDltValue] of DLT is signaled
    Values in DLT between (MinDltValue, MaxDltValue) can be represented by a bit-map BM[i]. If BM[i] = 1, the value (i + MinDltValue + 1) is in DLT.
  Use a differential run-length coding approach to code the bit-map
    A minimum 0-run-length is coded firstly
    Differences between 0-run-lengths and the minimum 0-run-length are coded sequentially
    For example: The minimum 0-run-length 2 is coded first. Then 1, 0, 0, and 1 are coded in order

## Slide 5: The Proposed DLT Coding Method (2/3)
The encoder can choose to code the RCBM directly.
  Guarantee an acceptable bits number in the worst case
  A DLT is coded with 265 bits in the worst case for 8-bit samples.
  A conformable encoder never codes a DLT with more than 265 bits.
dlt_flag | u(1)
if( dlt_flag){ | 
diff_max_dlt_value | u(v)
min_dlt_value | u(v)
if(!DLTDeduced){ | 
run_length_coding_flag | u(1)
if(run_length_coding_flag){ | 
min_run_length | u(3)
run_length_bits_minus1 | u(3)
for(j = MinDltV+1; j< MaxDltV; j+=Run[j]+1){ | 
run_length_diff[j] | u(v)
if(run_length_diff[j]==RunBoundary) | 
run_length_diff_rem[j] | ue(v)
} | 
} | 
else{ | 
for(j = MinDltV+1; j< MaxDltV; j++) | 
bit_map_flag[j] | u(1)
} | 
} | 
} | 

## Slide 6: The Proposed DLT Coding Method (3/3)
The delta-DLT method proposed in JCT3V-D0054 is used on the dependent view
  DLT0 and DLT1 are DLTs on the base view and on the dependent view respectively, represented in a full bit-map form
  A delta-DLT DLT1’ is calculated as DLT1’ = DLT0⊕DLT1
  DLT1’ instead of DLT1 is passed to the DLT coder.
  After DLT1’ is decoded, DLT1 = DLT0⊕DLT1’
No parsing issue in the delta-DLT approach
  Inter-view information is only utilized at the reconstruction step
  No matter DLTs are coded in VPS, SPS, PPS, or slice header.

## Slide 7: The Comparison of DLT size
On average, the proposed method generates only 9.4% bits of the anchor to code DLT.
 |  | DLT Size (bits) |  | 
 |  | Anchor | Proposed | P/A (%)
Balloons | V0_depth | 555 | 70 | 12.61%
 | V1_depth | 641 | 40 | 6.24%
 | V2_depth | 617 | 38 | 6.16%
Kendo | V0_depth | 485 | 65 | 13.40%
 | V1_depth | 637 | 50 | 7.85%
 | V2_depth | 649 | 51 | 7.86%
Newspapercc | V0_depth | 606 | 101 | 16.67%
 | V1_depth | 621 | 16 | 2.58%
 | V2_depth | 696 | 31 | 4.45%
PoznanHall2 | V0_depth | 420 | 80 | 19.05%
 | V1_depth | 380 | 40 | 10.53%
 | V2_depth | 381 | 21 | 5.51%
Average |  | 557.33 | 50.25 | 9.41%

## Slide 8: Results (Cont.)
Anchor: HTM-7.0r1 under common test condition
The coding performance is similar to the anchor
  Crosschecked by E0295 (Thanks to ZTE)

## Slide 9: Conclusion
An efficient coding method for the depth lookup table (DLT) is proposed
  Reduce more than 90% of the original DLT size
  Guarantee an acceptable bits number in the worst case
  No Parsing dependency issue

## Slide 10: Thank you for your attention!