## Slide 1: JCT3V-E0179 3D-CE5.h related: A simplified DMM prediction method in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
Problem definition
  DMM prediction is conducted differently in different cases.
    Two samples of the top reference sample row or the left reference sample column may be chosen to generate a DC predictor for different partition patterns.
    Four cases are identified to generate the DC predictors
The proposed simplification
  Unify two cases among the four cases due to its similarity
Results
  0.1% BD-rate saving for the synthesized views

## Slide 3: Problem Definition
DMM prediction is conducted differently in different cases
  Four cases are identified to generate the DC predictor
  Also applied to chain-coding

## Slide 4: Problem Definition (Cont.)
The difference between case 1 and case 2 is minor.
Case 1
Case 2

## Slide 5: Proposed Simplification
  Unify case 1 and case 2 as a single case for predicting the DC values
    (X+Y)>>1 is used to replace (S+T)>>1 or 128
    No change to bandwidth since X Y are already accessed in the padding and filtering process before prediction.
T
S
X
Y

## Slide 6: Results
Anchor: HTM-7.0r1 under common test condition
The simplification does not cause a BD-rate loss.
Cross-checked by JCT3V-E0265 (Thanks to Hisilicon)

## Slide 7: Results (Cont.)
Anchor: HTM-7.0r1 All Intra case

## Slide 8: Conclusion
  Propose to simplify the DMM prediction by unifying two prediction cases in the DMM prediction
  4 prediction cases are reduced to 3.
0.1% BD-rate savings for the synthesized views

## Slide 9: Thank you for your attention!