## Slide 1: 3D-CE3.h related: Sub-PU level inter-view motion prediction
Jicheng An, Kai Zhang, Jian-Liang Lin, and Shawmin Lei

## Slide 2: Overall Summary
Sub-PU level inter-view motion prediction is proposed for the temporal inter-view merge candidate.
Significant BD-rate reduction and modest complexity increase can be achieved.
  Three sub-PU sizes were tested.
<number>

## Slide 3: Current Design in HTM
Current temporal inter-view merge candidate (TIVMC)
  Add a DV (by DoNBDV) to the current PU to obtain a reference block
  If the reference block is coded using MCP, the associated motion parameters can be used as TIVMC for the current PU.
Drawback
The corresponding area in the ref view may contain plentiful motion info., but only motion info. in the middle position of the area is used for the current PU.
<number>

## Slide 4: Proposed Method
Sub-PU level inter-view motion prediction (SPIVMP) for temporal inter-view merge candidate (TIVMC)
  Divide the current PU into sub-PUs
  Add a DV to each sub-PU to obtain each reference block
  For each reference block, the associated motion parameters (MP) can be utilized for the sub-PU.
<number>

## Slide 5: Proposed Syntax Change
Add one flag in SPS to signal the sub-PU size, which can be one of the following values:
  4x4
  8x8 (PU size <= 8x8 will not be divided)
  16x16 (PU size <= 16x16 will not be divided)
  32x32 (PU size <= 32x32 will not be divided)
  64x64 (PU are always not divided, same as anchor)
<number>

## Slide 6: Results for Sub-PU Size = 4x4
Implemented on HTM7.0r1
<number>

## Slide 7: Results for Sub-PU Size = 8x8
Implemented on HTM7.0r1
PU size <= 8x8 will not be divided
<number>

## Slide 8: Results for Sub-PU Size = 16x16
Implemented on HTM7.0r1
PU size <= 16x16 will not be divided
<number>

## Slide 9: Conclusion
Sub-PU level inter-view motion prediction is proposed for the temporal inter-view merge candidate
Significant BD-rate reduction and modest complexity increase can be achieved.
Sub-PU size is signaled in SPS for flexibility.
<number>

## Slide 10: Thank you!