## Slide 1
CE3.h related : AMVP candidate list construction for DCP blocks
(JCT3V-E0189)
July 2013
LG Electronics
Sunmi Yoo (sunmi.yoo@lge.com)
Taesup Kim (taesup.kim@lge.com)
Junghak Nam (junghak.nam@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Introduction
Two prediction modes for inter coding in 3D-HEVC
  Merge : Additional candidates for inter-view prediction
    Inter-view motion vector candidate (IvMC)
    Depth-refined inter-view disparity candidate (IvDC)
    VSP candidate
  AMVP
    IvMC used to be one of candidates
    Currently no inter-view candidate
But we still have a chance to improve the AMVP for inter-view prediction, for DCP blocks.

## Slide 3: Proposed method
The proposed method is to reuse DoNBDV and NBDV used in merge process for AMVP DCP blocks.
  If a current reference picture is an inter-view picture and the number of candidates is not sufficient, DoNBDV is added as one of candidates.
  If none of candidates is available, DoNBDV and NBDV are inserted into the candidate list.
Current
PU
A2
A1
B1
B2
B3
T
AMVP Candidates :
Final AMVP Candidates :
DoNBDV
NBDV
Final AMVP Candidate in HTM7.0r1 :
0
Current
PU
A2
A1
B1
B2
B3
T
AMVP Candidates :
Final AMVP Candidates :
A1
DoNBDV
Final AMVP Candidate in HTM7.0r1 :
A1
A1
0

## Slide 4: Complexity analysis
HTM7.0 | Method Proposed in E0189
A0, A1, B0, B1, B2 (spatial candidates) | A0, A1, B0, B1, B2 (spatial candidates)
Temporal candidate | Temporal candidate
Zero candidate | DoNBDV / NBDV candidate
Method Proposed in E0189 | Note
Additional comparisons : 1 redundancy check | Num. of redundancy checks in current 3D-HEVC: 1 redundancy check
Additional memory accesses: 1 access for DoNBDV/NBDV (could be loaded in one time) | Depending on implementation, DoNBDV/NDBV is available without memory access

## Slide 5: Experimental results
Experimental result shows that the coding efficiency can be improved by the proposed method.
  For video 1 and video 2, 0.14% and 0.19% of coding gains can be achieved.
  0.02% gain is achieved from synthesized result.
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.30% | -0.20% | -0.12% | -0.12% | -0.12% | 101.4% | 100.0% | 101.3%
Kendo | 0.00% | -0.23% | -0.31% | -0.14% | -0.12% | -0.05% | 103.7% | 96.3% | 103.6%
Newspaper_CC | 0.00% | -0.09% | -0.22% | -0.08% | -0.06% | -0.19% | 103.4% | 99.8% | 103.3%
GT_Fly | 0.00% | 0.17% | -0.10% | -0.02% | -0.01% | -0.01% | 101.0% | 98.7% | 105.6%
Poznan_Hall2 | 0.00% | -0.22% | 0.03% | -0.10% | -0.11% | 0.04% | 102.0% | 99.8% | 103.7%
Poznan_Street | 0.00% | -0.34% | -0.33% | -0.14% | -0.13% | -0.09% | 101.5% | 99.1% | 106.6%
Undo_Dancer | 0.00% | 0.01% | -0.17% | -0.06% | -0.06% | 0.28% | 100.8% | 105.2% | 106.1%
1024x768 | 0.00% | -0.21% | -0.24% | -0.11% | -0.10% | -0.12% | 102.8% | 98.7% | 102.7%
1920x1088 | 0.00% | -0.09% | -0.14% | -0.08% | -0.08% | 0.05% | 101.3% | 100.7% | 105.5%
average | 0.00% | -0.14% | -0.19% | -0.09% | -0.09% | -0.02% | 102.0% | 99.8% | 104.3%

## Slide 6: Conclusion
The proposed method is to reuse DoNBDV and NBDV as supplements if the number of AMVP candidates for the inter-view reference is not maximal.
Since the DoNBDV and the NBDV are obtained at CU-level,
  Additional refined disparity calculation for DCP AMVP is not necessary.
  It is free from the memory cost issue.
We recommend this proposal is adopted for the next version.