## Slide 1
1. Problem of current method
2. Proposed method
3. Experimental results
4. Complexity analysis
5. Conclusion
Contents
JCT3V-E0191
CE4.h: The results on illumination compensation using offset model
2013-07
Jiwook Jung
(LG Electronics)

## Slide 2: Problems of Current Method
Current Method
  Estimation of scale & offset (linear least square solution)
    Where, , are left and top neighbor pixels by , , respectively.
    Division can substituted by multiplication and shift.
    cross-correlation of arbitrary samples
    32 bit operations to deal with multiplications

## Slide 3: Problems of Current Method
Complexity of linear least square solution
  The complexity reduction is necessary with respect to applying IC on Y/U/V/Depth.
  Multiplication between arbitrary values
  Bit operation range
MR-SAD(Mean Removed SAD) of the encoder ME metric is not matched with current compensation model, conceptually.

## Slide 4: Proposed Offset Model Method
Proposed Method
  Apply simple offset
  Offset is estimated by the difference of neighbor pixels’ mean

## Slide 5: Experimental results
HTM-7.0rc1 IC OffsetModel

## Slide 6: Complexity analysis
Complexity analysis
  Number of operations
    Anchor (HTM-7.0r1, Linear Model)
    Proposed (Offset Model)
  Multiplication-free (between arbitrary sample values)
  Number of addition/shift : reduced by 1/3
  No need to have LUT for division
  Reduce operation bit range (3216)

## Slide 7: Conclusion
Proposed method
  Offset compensation model for IC
Complexity
  Multiplication-free
  Numbers of Addition/shift can be reduced by 1/3.
  16 bit range operation
  encoding time : 100.3%, decoding time : 97.4%
Performance
  Total : 0.0%, V1 : 0.2% and v2: -0.3%, (Poznan_Hall2 v2 : -2.4%)