## Slide 1
Shinya Shimizu, Shiori Sugimoto/ NTT
JCT3V-D0207
3D-CE1.h: Adaptive block partitioning for VSP

## Slide 2: Proposal
Adaptive partition for sub-PU level DCP
  For each 8x8 block, either 4x8 or 8x4 is decided by checking 4 corners of corresponding virtual depth map
TL
TR
BR
BL
Virtual depth map

## Slide 3: Simulations
Implemented on HTM v7.0r1
Follow the common test condition (JCT3V-D1100)

## Slide 4: Simulation results
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.00% | 0.09% | -0.07% | 0.01% | 0.01% | -0.04% | 99.4% | 101.0%
Kendo | 0.00% | 0.06% | -0.05% | 0.00% | 0.02% | -0.02% | 99.4% | 101.1%
Newspapercc | 0.00% | 0.00% | -0.11% | -0.02% | -0.01% | -0.06% | 99.4% | 100.9%
GhostTownFly | 0.00% | 0.44% | 0.17% | 0.06% | 0.06% | 0.07% | 99.4% | 98.1%
PoznanHall2 | 0.00% | 0.06% | 0.13% | 0.02% | -0.01% | 0.07% | 99.2% | 101.5%
PoznanStreet | 0.00% | 0.08% | 0.18% | 0.02% | 0.02% | 0.02% | 99.1% | 100.8%
UndoDancer | 0.00% | 0.84% | 0.72% | 0.20% | 0.19% | 0.16% | 99.2% | 100.0%
1024x768 | 0.00% | 0.05% | -0.08% | 0.00% | 0.01% | -0.04% | 99.4% | 101.0%
1920x1088 | 0.00% | 0.36% | 0.30% | 0.07% | 0.07% | 0.08% | 99.2% | 100.1%
average | 0.00% | 0.23% | 0.14% | 0.04% | 0.04% | 0.03% | 99.3% | 100.5%

## Slide 5: Complexity
Required operation to decide block partitioning
  2 comparisons
 | # of operations Add/Sub/Comp (ratio to anchor) | Data storage (ratio to anchor) | Data transfer rate (ratio to anchor) | # of storage accessing (ratio to anchor)
Worst | 98.42% | 100.53% | 100.00% | 57.14%
Average |  |  | 90.38% | 51.18%
Best |  |  | 80.77% | 50.07%

## Slide 6: Conclusions
Adaptive block size on 2nd DCP in VSP
  Decision based on virtual depth map
  4x8 or 8x4
Experiments
  Small coding loss (< 0.03% on average)
  Complexity reduction with better alignment with HEVC
Recommendation
  Adopt to the next version of 3D-HEVC