## Slide 1: AHG7 Related: Differential coding method for DLT in 3D-HEVC (JCT3V-E0211)
Ming LI, Ping WU, Hongwei LI
Guoqiang SHANG, Yutang XIE

## Slide 2: Summary
As tested on HTM7.0 (CTC), DLT related syntax elements take about 66% of the coding bits of SPS.
To reduce the coding bits of DLT, differential coding is proposed to perform lossless compression on the DLT elements in JCT3V-D0172.
The method in JCT3V-D0172 was implemented on HTM7.0. Compared with the HTM7.0 CTC anchors, using this method, the coding bits for DLT are reduced by about 75% (taking an average of 32% in the SPS coding bits), while the bits for SPS are saved by 49%.
In addition, with the proposed method, the coding performance is very slightly improved by 0.02% and 0.01% on average for 1280x768 and 1920x1088 sequences, respectively, under CTC configurations.

## Slide 3: Introduction
In HTM7.0, DLT for every view is constructed by pre-analyzing an intra period of original depth pictures associated with given layer_id. The syntax structure in HTM7.0 for DLT is given in the table below.
seq_parameter_set_rbsp( ) { | Descriptor
…… | 
if ( DepthFlag ) { | 
dlt_flag | u(1)
if (dlt_flag) { | 
num_depth_values_in_dlt | ue(v)
for ( i = 0; i < num_depth_values_in_dlt ; i++ ) { | 
dlt_depth_value[ i ] | ue(v)
} | 
} | 
} | 
…… | 
} | 

## Slide 4: Motivation
As tested on HTM7.0 (CTC), DLT related syntax elements take about 65% of the coding bits of SPS.
Sequence | View | DLT bits (D0) | SPS bits (S0) | D0/S0 (%)
Balloon | 3 | 556 | 846 | 65.72
 | 1 | 642 | 938 | 68.44
 | 5 | 618 | 916 | 67.47
Kendo | 3 | 486 | 776 | 62.63
 | 1 | 638 | 934 | 68.31
 | 5 | 650 | 948 | 68.57
Newspaper | 4 | 607 | 897 | 67.67
 | 2 | 622 | 918 | 67.76
 | 6 | 697 | 995 | 70.05
Poznan_hall2 | 6 | 421 | 713 | 59.05
 | 7 | 381 | 679 | 56.11
 | 5 | 382 | 682 | 56.01
Average |  | 558.33 | 853.50 | 65.42

## Slide 5: Proposed syntax
To reduce the coding bits for DLT, a differential coding method is proposed. The modified syntax on HTM7.0 is as below.
seq_parameter_set_rbsp( ) { | Descriptor
…… | 
if (dlt_flag) { | 
num_depth_values_in_dlt | ue(v)
dlt_depth_value[0] | ue(v)
for ( i = 0; i < num_depth_values_in_dlt ; i++ ) { | 
dlt_depth_diff_minus1_less_than_4_flag[ i ] | u(1)
if (dlt_depth_diff_minus1_less_than_4_flag[ i ]) | 
dlt_depth_diff_minus1[ i ] // shall not be negative | u(2)
else | 
dlt_depth_diff_minus1_minus4[ i ] // shall not be negative | ue(v)
} | 
…… | 
} | 

## Slide 6: Proposed semantics
num_depth_values_in_dlt specifies the number of elements in the depth lookup table for depth view components.
dlt_depth_value[ 0 ] specifies the 0-th entry in the depth lookup table for depth view components.
dlt_depth_diff_minus1_less_than_4_flag[ i ] equal to 1 specifies that the value of dlt_depth_diff_minus1[ i ] is presented. Otherwise, dlt_depth_diff_minus1_less_than_4_flag[ i ] equal to 0 specifies that the value of dlt_depth_diff_minus1_minus4[ i ] is presented.
dlt_depth_diff_minus1[ i ] specifies the i-th entry for deriving the i-th entry in depth lookup table for depth view components. The value of dlt_depth_diff_value_minus1[i] shall not be negative. The value of the i-th entry in depth lookup table is derived as dlt_depth_value[i] = dlt_depth_value[i – 1] + dlt_depth_diff_minus1[i] + 1, for i from 1 to num_depth_values_in_dlt – 1. NOTE: dlt_depth_value[0] is the smallest depth value in depth lookup table.
dlt_depth_diff_minus1_minus4[ i ] specifies the i-th entry for deriving the i-th entry in depth lookup table for depth view component. The value of dlt_depth_diff_value_minus1_minus4[ i ] shall not be negative. The value of the i-th entry in depth lookup table is derived as dlt_depth_value[ i ] = dlt_depth_value[ i – 1 ] + dlt_depth_diff_value_minus1_minus4[ i ] + 1 + 4, for i from 1 to num_depth_values_in_dlt – 1.

## Slide 7: Proposed encoding
According to the proposed syntax and semantics, DLT is encoded in the following steps:
  Step 1: Presenting the depth values into DLT array (e.g. dlt_depth_value[ ]) in ascending order.
  Step 2: Encoding the number of depth values in DLT array and the first element dlt_depth_value[0].
  Step 3: Calculating diff_minus1 = dlt_depth_value[i] – dlt_depth_value[i – 1] – 1.
  Step 4: If diff < 4 holds, encoding ‘1’ using u(1) and diff_minus1 value using u(2); otherwise, encoding ‘0’ using u(1) and (diff_minus1 – 4) value using ue(v).

## Slide 8: Experimental results
HTM7.0, CTC. Comparisons between HTM7.0 anchors and proposed on DLT and SPS coding bits. No performance loss was observed.
Sequence | View | HTM7.0 Anchor |  |  | HTM7.0 + proposed |  |  | Comparisons | 
 |  | DLT bits (D0) | SPS bits (S0) | D0/S0 (%) | DLT bits (D1) | SPS bits (S1) | D1/S1 (%) | D1/D0 (%) | S1/S0 (%)
Balloon | 3 | 556 | 846 | 65.72 | 121 | 411 | 29.44 | 21.76 | 48.58
 | 1 | 642 | 938 | 68.44 | 141 | 437 | 32.27 | 21.96 | 46.59
 | 5 | 618 | 916 | 67.47 | 141 | 439 | 32.12 | 22.82 | 47.93
Kendo | 3 | 486 | 776 | 62.63 | 109 | 399 | 27.32 | 22.43 | 51.42
 | 1 | 638 | 934 | 68.31 | 139 | 435 | 31.95 | 21.79 | 46.57
 | 5 | 650 | 948 | 68.57 | 141 | 439 | 32.12 | 21.69 | 46.31
News- paper | 4 | 607 | 897 | 67.67 | 157 | 447 | 35.12 | 25.86 | 49.83
 | 2 | 622 | 918 | 67.76 | 160 | 456 | 35.09 | 25.72 | 49.67
 | 6 | 697 | 995 | 70.05 | 175 | 473 | 37.00 | 25.11 | 47.54
Poznan _hall2 | 6 | 421 | 713 | 59.05 | 127 | 419 | 30.31 | 30.17 | 58.77
 | 7 | 381 | 679 | 56.11 | 119 | 417 | 28.54 | 31.23 | 61.41
 | 5 | 382 | 682 | 56.01 | 118 | 418 | 28.23 | 30.89 | 61.29
Average |  | 558.33 | 853.50 | 65.42 | 137.33 | 432.50 | 31.75 | 24.60 | 50.67

## Slide 9
HTM7.0, CTC. Performance comparisons between HTM7.0 anchor and proposed (3 view test case)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.00% | -0.03% | -0.03% | 117.9% | 93.9% | 90.7%
Kendo | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.02% | 109.0% | 105.1% | 111.1%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.02% | 88.5% | 108.6% | 85.7%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 0.00% | 104.9% | 98.6% | 93.9%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.00% | -0.03% | -0.03% | 90.5% | 101.6% | 99.5%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 0.00% | 97.0% | 112.2% | 97.8%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.00% | 0.00% | 0.00% | 90.9% | 105.2% | 103.1%
1024x768 | 0.0% | 0.0% | 0.0% | 0.00% | -0.02% | -0.02% | 105.1% | 102.5% | 95.8%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.01% | 95.8% | 104.4% | 98.6%
average | 0.0% | 0.0% | 0.0% | 0.00% | -0.01% | -0.01% | 99.8% | 103.6% | 97.4%

## Slide 10
HTM7.0, CTC. Performance comparisons between HTM7.0 anchor and proposed (2 view test case)
 | video 0 | video 1 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | 0.0% | 0.00% | -0.02% | -0.02%
Kendo | 0.0% | 0.0% | 0.00% | -0.02% | -0.02%
Newspaper_CC | 0.0% | 0.0% | 0.00% | -0.02% | -0.02%
GT_Fly | 0.0% | 0.0% | 0.00% | 0.00% | 0.00%
Poznan_Hall2 | 0.0% | 0.0% | 0.00% | -0.02% | -0.02%
Poznan_Street | 0.0% | 0.0% | 0.00% | 0.00% | 0.00%
Undo_Dancer | 0.0% | 0.0% | 0.00% | 0.00% | 0.00%
1024x768 | 0.0% | 0.0% | 0.00% | -0.02% | -0.02%
1920x1088 | 0.0% | 0.0% | 0.00% | -0.01% | -0.01%
average | 0.0% | 0.0% | 0.00% | -0.01% | -0.01%

## Slide 11: Modified WD
The proposed differential coding method on DLT is integrated into VPS extension syntax in WD.
vps_extension2( ) { | Descriptor
...... | 
dlt_flag[ layerId ] | u(1)
if( dlt_flag[ layerId ] ) { | 
num_depth_values_in_dlt[ layerId ] | ue(v)
dlt_depth_value[ layerId ][ 0 ] | ue(v)
for ( j = 0; j < num_depth_values_in_dlt[ layerId ] ; j++) { | 
dlt_depth_value[ layerId ][ j ] | ue(v)
dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ] | u(1)
if (dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ]) | 
dlt_depth_diff_minus1[ layerId ][ j ] // shall not be negative | u(2)
else | 
dlt_depth_diff_minus1_minus4[ layerId ][ j ] // shall not be negative | ue(v)
} | 
} | 
...... | 
} | 

## Slide 12
The semantics of the proposed syntax elements are listed below.
dlt_depth_value[ layerId ][ 0 ] specifies the 0-th entry in the depth lookup table for depth view components with layer_id equal to layerId.
dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ] equal to 1 specifies that the value of dlt_depth_diff_minus1[ layerId ][ j ] is presented. Otherwise, dlt_depth_diff_minus1_less_than_4_flag[ layerId ][ j ] equal to 0 specifies that the value of dlt_depth_diff_minus1_minus4[ layerId ][ j ] is presented.
dlt_depth_diff_minus1[ layerId ][ j ] specifies the j-th entry for deriving the j-th entry in depth lookup table for depth view components with layer_id equal to layerId. The value of dlt_depth_diff_value_minus1[ layerId ][ j ] shall not be negative. The value of the j-th entry in depth lookup table is derived as dlt_depth_value[ layerId ][ j ] = dlt_depth_value[ layerId ][ j – 1] + dlt_depth_diff_minus1[ layerId ][ j ] + 1, for j from 1 to num_depth_values_in_dlt[ layerId ] – 1. NOTE: dlt_depth_value[layerId][0] is the smallest depth value in depth lookup table for depth view components with layer_id equal to layerId.
dlt_depth_diff_minus1_minus4[ layerId ][ j ] specifies the j-th entry for deriving the j-th entry in depth lookup table for depth view components with layer_id equal to layerId. The value of dlt_depth_diff_minus1_minus4[ layerId ][ j ] shall not be negative. The value of the j-th entry in depth lookup table is derived as dlt_depth_value[ layerId ][ j ] = dlt_depth_value[ layerId ][ j – 1 ] + dlt_depth_diff_minus1_minus4[ layerId ][ j ] + 1 + 4, for j from 1 to num_depth_values_in_dlt[ layerId ] – 1.

## Slide 13: Conclusions
A differential coding method for DLT is proposed.
Proposed method saves the DLT coding bits by an average of 75%, and SPS coding bits by 49%.
Additionally, the CTC test results show that the proposed method provides almost the same coding performance as that of HTM7.0 anchor.
Therefore, it is recommended to adopt this method into 3D-HEVC.