## Slide 1: JCT3V-E0213 3D-CE3.h related: Simple merge candidate list construction for 3DV (Cross-checked by JCT3V-E0278)
ETRI & Kyung Hee University
G. Bang, Y.S. Heo, K.Y. Kim, G.H. Park,
G.S. Lee, and N. Hur
Notes: <number>

## Slide 2: Motivation of proposal
The current 3D-HEVC
  Designed for high coding-efficiency on the 3D videos
  But, the current design may be un-suitable in terms of H/W implementation, since the chip for 3D-HEVC module should be re-designed and re-implemented.
    3D-HEVC module has been more complex than the original HEVC module.
    It significantly increases the computational complexity and H/W implementation complexity.

## Slide 3: Problem on MCL construction
There exist two kinds of construction processes of merging candidate list (MCL).
  For the independent (base) texture view
  For the dependent views and depth map
The MCL construction process for the dependent views and depth map is more complexly-combined than the MCL construction process for the independent texture view.
<number>
Current MCL construction process for the current 3D-HEVC

## Slide 4: Problem on MCL construction of 3D-HEVC
The inserting processes for extra candidates (green-squared) are added.
In addition, traditional processes (yellow-squared) in HEVC are changed.
Therefore, redundant implementation should be carried out for traditional candidates in 3D-HEVC.
  Redundant design.
<number>
Current MCL construction process in 3D-HEVC

## Slide 5: Proposed method
We propose a low-complexity way to implement the MCL construction process for the 3D-HEVC by re-using existing MCL construction module in the HEVC.
This design is suitable for implementing the new MCL processes, since the existing MCL construction module in the HEVC can be re-used.
<number>
Proposed MCL construction process

## Slide 6: Proposed method
For dependent views, the MCL construction process in HEVC is used without any changes.
Then, the additional MCL construction processes are carried out with the MCL1 and AvailableFlagN as inputs (with N being replaced by A0, A1, B0, B1 or B2).
<number>
MCL construction process in HEVC
Proposed inserting process for extra candidates for dependent view
Notes: AvailableFlagN 은 HEVC의 MCL process 중에 생성되는 플래그 들이다.
Spatial candidate의 availability를 의미하며 N은 A1, B1, B0, A0, B2로 대체 된다.
<number>

## Slide 7: Proposed method
For dependent view or depth, the order of candidates is identical to the current 3D-HEVC.
<number>
Inserting process for extra candidates for dependent views
Notes: AvailableFlagN 은 spatial candidate의 availability를 의미하며 N은 A1, B1, B0, A0, B2로 대체 된다.
<number>

## Slide 8: Simulation Results
Cross-checked by LG (JCT3V-E0278).
For the proposed MCL construction process,
  The process in HM 10.0rc1 was used.
  Therefore, the simulation results of the ‘video 0’ are slightly different from the anchor.
Very Small Coding Loss : ONLY 0.07% (Almost the same with the Anchor)
<number>
Simulation results of the proposed method

## Slide 9
<number>

## Slide 10: Conclusion
Proposed MCL construction process significantly decrease the complexity for hardware implementation.
  Very Small Coding Loss provided : ONLY 0.07%
  Seriously Simplified WD text.
  We recommend to adopt the proposed MCL construction process for the next 3D-HTM.
The modules redundancies between 3D-HEVC and HEVC can be removed to reduce H/W implementation complexity.
  Further study to be required to investigate the other redundancies between 3D-HEVC and HEVC in terms of H/W implementation design.
<number>

## Slide 11: Proposed method
Example>
  AvailableFlagN is used to understand the condition of spatial merging candidates in the MCL.
<number>
Proposed MCL construction process
MCL1
, AvailableFlagN
MCL2
T
IvMC
N VSP
Zero
IvDC
VSP
0 | A1
1 | B0
2 | A0
3 | Col
4 | Combined B
5 | 
0 | A1(VSP)
1 | B0
2 | A0(VSP)
3 | Col
4 | Combined B
5 | 
0 | IvMC
1 | A1
2 | B0
3 | A0
4 | Col
5 | Combined B
0 | IvMC
1 | A1
2 | B0
3 | VSP
4 | A0
5 | Col
MCL1
Not available
Not available
List is full
Available
Available
Notes: <number>

## Slide 12: Proposed method
Example>
  Step 1> Check candidate N in the input MCL1 has VSP flag or not. Then, set the VSP flag of N.
<number>
Proposed MCL construction process
MCL1
, AvailableFlagN
MCL2
T
IvMC
N VSP
Zero
IvDC
VSP
0 | A1
1 | B0
2 | A0
3 | Col
4 | Combined B
5 | 
0 | A1(VSP)
1 | B0
2 | A0(VSP)
3 | Col
4 | Combined B
5 | 
0 | IvMC
1 | A1
2 | B0
3 | A0
4 | Col
5 | Combined B
0 | IvMC
1 | A1
2 | B0
3 | VSP
4 | A0
5 | Col
MCL1
Not available
Not available
List is full
Available
Available
Notes: <number>

## Slide 13: Proposed method
Example>
  Step 2> Texture candidate is not available: go to the next step.
<number>
Proposed MCL construction process
MCL1
, AvailableFlagN
MCL2
T
IvMC
N VSP
Zero
IvDC
VSP
0 | A1
1 | B0
2 | A0
3 | Col
4 | Combined B
5 | 
0 | A1(VSP)
1 | B0
2 | A0(VSP)
3 | Col
4 | Combined B
5 | 
0 | IvMC
1 | A1
2 | B0
3 | A0
4 | Col
5 | Combined B
0 | IvMC
1 | A1
2 | B0
3 | VSP
4 | A0
5 | Col
MCL1
Not available
Not available
List is full
Available
Available
Notes: <number>

## Slide 14: Proposed method
Example>
  Step 3> IvMC candidate is available: Shift right all valid candidates and insert the Temporal Inter-view candidate to the first space of the MCL.
<number>
Proposed MCL construction process
MCL1
, AvailableFlagN
MCL2
T
IvMC
N VSP
Zero
IvDC
VSP
0 | A1
1 | B0
2 | A0
3 | Col
4 | Combined B
5 | 
0 | A1(VSP)
1 | B0
2 | A0(VSP)
3 | Col
4 | Combined B
5 | 
0 | IvMC
1 | A1
2 | B0
3 | A0
4 | Col
5 | Combined B
0 | IvMC
1 | A1
2 | B0
3 | VSP
4 | A0
5 | Col
MCL1
Not available
Not available
List is full
Available
Available
Notes: <number>

## Slide 15: Proposed method
Example>
  Step 4> IvDC candidate is not available: go to the next step.
<number>
Proposed MCL construction process
MCL1
, AvailableFlagN
MCL2
T
IvMC
N VSP
Zero
IvDC
VSP
0 | A1
1 | B0
2 | A0
3 | Col
4 | Combined B
5 | 
0 | A1(VSP)
1 | B0
2 | A0(VSP)
3 | Col
4 | Combined B
5 | 
0 | IvMC
1 | A1
2 | B0
3 | A0
4 | Col
5 | Combined B
0 | IvMC
1 | A1
2 | B0
3 | VSP
4 | A0
5 | Col
MCL1
Not available
Not available
List is full
Available
Available
Notes: <number>

## Slide 16: Proposed method
Example>
  Step 5> VSP candidate is available: Shift right and ranges from the A0 to the last valid candidate and insert the VSP candidate to after the IVDC candidate.
<number>
Proposed MCL construction process
MCL1
, AvailableFlagN
MCL2
T
IvMC
N VSP
Zero
IvDC
VSP
0 | A1
1 | B0
2 | A0
3 | Col
4 | Combined B
5 | 
0 | A1(VSP)
1 | B0
2 | A0(VSP)
3 | Col
4 | Combined B
5 | 
0 | IvMC
1 | A1
2 | B0
3 | A0
4 | Col
5 | Combined B
0 | IvMC
1 | A1
2 | B0
3 | VSP
4 | A0
5 | Col
MCL1
Not available
Not available
List is full
Available
Available
Notes: <number>

## Slide 17: Proposed method
Example>
  Step 6> List is full: Skip adding zero vector.
  Then MCL2 is constructed as an output.
<number>
Proposed MCL construction process
MCL1
, AvailableFlagN
MCL2
T
IvMC
N VSP
Zero
IvDC
VSP
0 | A1
1 | B0
2 | A0
3 | Col
4 | Combined B
5 | 
0 | A1(VSP)
1 | B0
2 | A0(VSP)
3 | Col
4 | Combined B
5 | 
0 | IvMC
1 | A1
2 | B0
3 | A0
4 | Col
5 | Combined B
0 | IvMC
1 | A1
2 | B0
3 | VSP
4 | A0
5 | Col
MCL1
Not available
Not available
List is full
Available
Available
Notes: <number>

## Slide 18: Draft Text
<number>
Notes: HEVC의 모듈 수정 없이 그대로 사용.
<number>

## Slide 19: Draft Text
<number>

## Slide 20: Draft Text
<number>

## Slide 21
<number>