## Slide 1
Page <number>
JCT3V-E0226: Modification of Binaryzation for Depth Intra Mode
Xu Chen
Notes: 26/7/31
<number>

## Slide 2: Summary
Page <number>
A follow-up of JCT3V-D0195 with the following modification
  Reduce bits for signaling depth intra mode 0, 1 and 2 in 8×8-32×32 without complexity improvement.
  Reduce bits for signaling depth intra mode 3 in 4×4 without complexity improvement.

## Slide 3: Motivation
9 depth intra modes are applied for 4×4 and 8×8-32×32,which are list depth modeling table semantics as follow.
Page <number>
depth_intra_mode | DepthIntraMode
0 | SDCM_Planar
1 | HEVC intra (HEVC_INTRA_PRED)
2 | SDCM_DMM_1
3 | DMM_1 (MODE_DMM_WFULL)
4 | DMM_4 (MODE_DMM_CPREDTEX)
5 | DMM_3 (MODE_DMM_WPREDTEX)
6 | SDCM_DC
7 | DMM_2 (MODE_DMM_WPREDDIR)
8 | CCM
Name of depth_intra_mode | Bin String | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN
INTRA_DEP_SDC_PLANAR | 00 | -
INTRA_DEP_NONE | 010 | 0
INTRA_DEP_SDC_DMM_WFULL | 011 | -
INTRA_DEP_DMM_WFULL | 100 | 10
INTRA_DEP_DMM_CPREDTEX) | 101 | -
INTRA_DEP_DMM_WPREDTEX) | 110 | 110
INTRA_DEP_SDC_DC | 1110 | -
INTRA_DEP_DMM_WPREDDIR) | 11111 | -
INTRA_DEP_CHAIN | 11110 | 111

## Slide 4: Motivation
Modify the syntax table of 8×8-32×32, fewer bits for signalling depth intra mode 1 and 2, which can bring greater impact than other modes behind.
Page <number>
Name of depth_intra_mode | Bin String | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN
INTRA_DEP_SDC_PLANAR | 00 | -
INTRA_DEP_NONE | 01 | 0
INTRA_DEP_SDC_DMM_WFULL | 10 | -
INTRA_DEP_DMM_WFULL | 1100 | 10
INTRA_DEP_DMM_CPREDTEX) | 1101 | -
INTRA_DEP_DMM_WPREDTEX) | 1110 | 110
INTRA_DEP_SDC_DC | 11110 | -
INTRA_DEP_DMM_WPREDDIR) | 111110 | -
INTRA_DEP_CHAIN | 111111 | 111

## Slide 5: Motivation
Page <number>
Solution1
Modify the syntax table of 4×4 with syntax flag sig_intramode_det0, which for signaling weather mode 5 or 8 applied in detecting unit(64×64).
sig_intramode_det0 only exist once in detecting unit(64×64) that with 4×4 inside and the flag determine the signaling depth intra mode way of all 4×4s inside detecting unit.

## Slide 6: Proposed solution
Page <number>
Name of depth_intra_mode | Bin String |  | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN | intramode_det0
INTRA_DEP_SDC_PLANAR | 00 | - | 1
INTRA_DEP_NONE | 01 | 0 | 
INTRA_DEP_SDC_DMM_WFULL | 10 | - | 
INTRA_DEP_DMM_WFULL | 1100 | 10 | 
INTRA_DEP_DMM_CPREDTEX) | 1101 | - | 
INTRA_DEP_DMM_WPREDTEX) | 1110 | 110 | 
INTRA_DEP_SDC_DC | 11110 | - | 
INTRA_DEP_DMM_WPREDDIR) | 111110 | - | 
INTRA_DEP_CHAIN | 111111 | 111 | 
Name of depth_intra_mode | Bin String |  | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN | intramode_det0
INTRA_DEP_SDC_PLANAR | 00 | - | 0
INTRA_DEP_NONE | 01 | 0 | 
INTRA_DEP_SDC_DMM_WFULL | 10 | - | 
INTRA_DEP_DMM_WFULL | 1100 | 1 | 
INTRA_DEP_DMM_CPREDTEX) | 1101 | - | 
INTRA_DEP_DMM_WPREDTEX) | 1110 | - | 
INTRA_DEP_SDC_DC | 11110 | - | 
INTRA_DEP_DMM_WPREDDIR) | 111110 | - | 
INTRA_DEP_CHAIN | 111111 | - | 
mode 5 or 8 applied in detecting unit(64×64)
Without mode 5 or 8 in detecting unit(64×64)

## Slide 7: Proposed solution
Further modify the syntax table of 8×8-32×32 with syntax flag sig_intramode_det1, which for signaling weather mode 3-8 applied in detecting unit(64×64).
sig_intramode_det1 only exist once in detecting unit(64×64) that with 8×8-32×32 inside and the flag determine the signaling depth intra mode way of all 8×8-32×32s inside detecting unit.
Page <number>
Solution2

## Slide 8: Proposed solution
Page <number>
Name of depth_intra_mode | Bin String |  | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN | intramode_det1
INTRA_DEP_SDC_PLANAR | 00 | - | 1
INTRA_DEP_NONE | 01 | 0 | 
INTRA_DEP_SDC_DMM_WFULL | 10 | - | 
INTRA_DEP_DMM_WFULL | 1100 | 10 | 
INTRA_DEP_DMM_CPREDTEX) | 1101 | - | 
INTRA_DEP_DMM_WPREDTEX) | 1110 | 110 | 
INTRA_DEP_SDC_DC | 11110 | - | 
INTRA_DEP_DMM_WPREDDIR) | 111110 | - | 
INTRA_DEP_CHAIN | 111111 | 111 | 
Name of depth_intra_mode | Bin String |  | 
 | ( cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_2Nx2N ) ¦ ¦ ( cLog2CbSize > 3 && cLog2CbSize < 6 ) | cLog2CbSize = = 3 && PartMode[ xC ][ yC ] = = PART_NxN | intramode_det1
INTRA_DEP_SDC_PLANAR | 0 | - | 0
INTRA_DEP_NONE | 10 | 0 | 
INTRA_DEP_SDC_DMM_WFULL | 11 | - | 
INTRA_DEP_DMM_WFULL | - | 10 | 
INTRA_DEP_DMM_CPREDTEX) | - | - | 
INTRA_DEP_DMM_WPREDTEX) | - | 110 | 
INTRA_DEP_SDC_DC | - | - | 
INTRA_DEP_DMM_WPREDDIR) | - | - | 
INTRA_DEP_CHAIN | - | 111 | 
mode 3-8 applied in detecting unit(64×64)
Without mode 3-8 in detecting unit(64×64)

## Slide 9: Experimental results
Page <number>
Solution (CTC) (anchor is HTM7.0r1) (modify on HTM7.01)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.00% | -0.05% | 0.03% | -0.01% | 0.00% | 0.00%
Kendo | 0.00% | 0.06% | -0.20% | -0.02% | 0.02% | -0.05%
Newspaper_CC | 0.00% | 0.10% | -0.13% | -0.01% | -0.01% | -0.31%
GT_Fly | 0.00% | 0.73% | 0.59% | 0.09% | 0.08% | 0.04%
Poznan_Hall2 | 0.00% | 0.10% | 0.12% | 0.02% | -0.01% | 0.04%
Poznan_Street | 0.00% | 0.14% | 0.10% | 0.02% | 0.03% | 0.03%
Undo_Dancer | 0.00% | -0.84% | -0.98% | -0.31% | -0.31% | -0.11%
1024x768 | 0.00% | 0.04% | -0.10% | -0.01% | 0.00% | -0.12%
1920x1088 | 0.00% | 0.03% | -0.04% | -0.04% | -0.05% | 0.00%
average | 0.00% | 0.04% | -0.07% | -0.03% | -0.03% | -0.05%
Solution1

## Slide 10: Experimental results
Page <number>
Solution (CTC) (anchor is HTM7.0r1) (modify on HTM7.0r1)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.00% | -0.02% | 0.02% | 0.00% | 0.00% | 0.00%
Kendo | 0.00% | 0.06% | -0.07% | 0.00% | 0.03% | 0.01%
Newspaper_CC | 0.00% | 0.08% | -0.03% | 0.01% | 0.03% | -0.22%
GT_Fly | 0.00% | 0.21% | 0.02% | 0.02% | 0.02% | 0.01%
Poznan_Hall2 | 0.00% | 0.10% | -0.36% | -0.07% | -0.04% | -0.06%
Poznan_Street | 0.00% | -0.28% | -0.05% | -0.05% | -0.04% | -0.06%
Undo_Dancer | 0.00% | -0.10% | -0.08% | -0.03% | -0.04% | 0.03%
1024x768 | 0.00% | 0.04% | -0.03% | 0.00% | 0.02% | -0.07%
1920x1088 | 0.00% | -0.02% | -0.12% | -0.03% | -0.03% | -0.02%
average | 0.00% | 0.01% | -0.08% | -0.02% | 0.00% | -0.04%
Solution1

## Slide 11: Experimental results
Page <number>
Solution (CTC) (anchor is HTM7.0r1) (modify on HTM7.0r1)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.0% | -0.2% | -0.1% | -0.05% | 0.02% | -0.01%
Kendo | 0.0% | 0.1% | 0.0% | 0.01% | 0.10% | 0.06%
Newspaper_CC | 0.0% | 0.0% | -0.1% | -0.01% | 0.09% | -0.14%
GT_Fly | 0.0% | 0.3% | 0.1% | 0.03% | 0.07% | 0.04%
Poznan_Hall2 | 0.0% | 0.2% | -0.1% | 0.01% | 0.05% | -0.04%
Poznan_Street | 0.0% | 0.0% | 0.0% | -0.01% | 0.06% | -0.01%
Undo_Dancer | 0.0% | -0.2% | -0.2% | -0.05% | -0.02% | 0.02%
1024x768 | 0.0% | 0.0% | -0.1% | -0.02% | 0.07% | -0.03%
1920x1088 | 0.0% | 0.1% | 0.0% | 0.00% | 0.04% | 0.00%
average | 0.0% | 0.0% | -0.1% | -0.01% | 0.05% | -0.01%
Solution2

## Slide 12: Experimental results
Page <number>
Solution (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.04%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.01%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | 0.02% | 0.05%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | 0.03% | 0.02%
Poznan_Hall2 | Support later |  |  | Support later |  | 
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.02%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.01% | 0.03%
1920x1088 | Support later |  |  | Support later |  | 
average | Support later |  |  | Support later |  | 
Solution1

## Slide 13: Experimental results
Page <number>
Solution (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | 0.08% | -0.01%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | 0.10% | 0.01%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | 0.11% | 0.01%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | 0.09% | 0.00%
Poznan_Hall2 | Support later |  |  | Support later |  | 
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | 0.06% | 0.00%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.05% | -0.02%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | 0.10% | 0.00%
1920x1088 | Support later |  |  | Support later |  | 
average | Support later |  |  | Support later |  | 
Solution2

## Slide 14: Conclusions
Page <number>
Modify syntax table for depth intra mode without complexity improve
Solution1: 0.04%(modify on HTM7.0r1) or 0.05%(modify on HTM7.01) coding gain on synthesized view
0.03%(modify on HTM7.01) coding gain on Video total bitrate
0.03%(modify on HTM7.01) or 0.02%(modify on HTM7.0r1) coding gain on Video bitrate
Solution2: 0.01% coding gain on synthesized view and 0.05% lost on video
Suggest adopting the proposed solutions
Thanks for cross-check by Qualcomm

## Slide 15
Page <number>
Thank you!
www.hisilicon.com