## Slide 1: JCT3V-E0227 Inter-view MAD prediction for rate control of 3D multi-view video coding
W. Lim, H. Jo, J. Yoo, I.V. Bajić and D. Sim
KWU and SFU
<number>
Notes: <number>

## Slide 2: Introduction
Multi-view video coding
  Compression of multiple videos acquired by cameras with translated position at the same time
  The base view is compatible to the single-view video coding
  The extended views are with the inter-view prediction to exploit high correlation between views
  Can provide view scalability
Rate control for 3D multi-view video coding
  Rate control is important in the practical use of video coding
  URQ (Unified Rate-Distortion) model-based rate control and R-lambda model-based rate control in HEVC reference software
  For multi-view extension of HEVC, no implementation of rate control
    Before the last meeting in Incheon, HTM_DEV0.3 with rate control was released
    However, there is no rate control in current HTM7.0_r1 yet
<number>

## Slide 3: The previous research
URQ model-based rate control
  H. Choi, J. Nam, J. Yoo, D. Sim, and I. V. Bajić, “Rate control based on unified RQ model for HEVC,” JCT-VC of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JCT-VC H0213 (m23088), San José, CA, USA, Feb. 2012.
  H. Choi, J. Nam, J. Yoo, D. Sim, and I. V. Bajić, “Improvement of the rate control based on pixel-based URQ model for HEVC,” JCT-VC of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JCTVC-I0094 (m24333), Geneva, Switzerland, Apr.-May 2012.
Multi-view rate control
  W. Lim, H. Choi, J. Nam, H. Jo, D. Sim and I. Bajić, “Rate control for 3D multi-view video coding,” JCT3V of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JCT3V-A0151, Stockholm, Sweden, Jul. 2012.
  W. Lim, H. Choi, J. Nam, H. Jo, D. Sim and I. Bajić, “Improvement of the rate control for 3D multi-view video coding,” JCT3V of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JCT3V-B0030, Shanghai, China, Oct. 2012.
  W. Lim, D. Sim and I. Bajić, “Improvement of the rate control for 3D multi-view video coding,” JCT3V of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JCT3V-C0090, Geneva, CH, Jan. 2013.
  W. Lim, H. Jo, D. Sim and I. Bajić, “The rate control schemes for 3D multi-view video coding,” JCT3V of ITU-T SG16 WP3 and ISO/IEC JTC1/SC29/WG11, JCT3V-D0111, Incheon, KR, Apr. 2013.
<number>

## Slide 4: The proposed methods
View-wise target bitrate allocation
  Better to be configured for the various applications of multi-view video coding
    E.g. multi-view video services for the clients not only with multi-view display but also with single-view display
    With consideration of the diverse display, the quality of the base view is important and it must be controlled
Inter-view MAD prediction
  The base view among the multiple views is compatible to HEVC
    The conventional rate control algorithms are suitable
  The extended views
    Coded not only with the intra and temporal prediction in HEVC but also with the inter-view prediction
    In case of fast motion or scene change, temporal correlation will be decreased but inter-view correlation won’t be decreased
<number>

## Slide 5: The proposed rate control for HEVC-based multi-view coding
To improve the rate control performance, we propose
  View-wise target bitrate allocation
  Depth map-based inter-view MAD prediction
<number>
HEVC with
rate control
(extended view)
Target bitrate
HEVC with
rate control
(Base view)
MAD
MAD
Amount of bits
Amount of bits
Target bitrate

## Slide 6: View-wise target bitrate allocation
View-wise target bitrate allocation
  Provides a function to configure the target bitrate for each view
  Can be enabled or disabled as an encoding issue
  Still can use the conventional URQ and R-lambda model-based rate control algorithms
  ‘TargetBitAssign’ : If the value is equal to 1, view-wise target bitrate allocation is enabled. If the value is equal to 0, view-wise target bitrate allocation is disabled
  ‘ViewWiseTargetBits’ : If view-wise target bitrate allocation is on, values are target bitrate for each view along the coding order (the units are bps for R-lambda model-based rate control and Kbps for URQ model-based rate control)
<number>
TargetBitAssign : 1 # Manual assignment of target bit-rate
ViewWiseTargetBits : 934 356 366 # View-wise target bit-rate setting

## Slide 7: Depth map-based inter-view MAD prediction
In order to select a QP value for the current CTU
  a rate control algorithm needs to predict the MAD value of the current CTU using previously encoded information
  In single-view rate control, this is done by using the MAD of a collocated block in the reference frame (temporal MAD prediction)
  While this may work well in the case of low motion
  Temporal MAD prediction is less accurate as the motion level increases, and becomes completely unreliable in case of scene changes
<number>

## Slide 8: Depth map-based inter-view MAD prediction
Inter-view MAD prediction
  The conventional rate control algorithms
  If the temporal distance becomes further, the temporal correlation will be decreased not only in case of moving objects but also in case of camera panning
…
…
MAD from temporally
collocated block
MAD from inter-view
corresponding block
Extended view
Base view
view
t
The current unit

## Slide 9: Depth map-based inter-view MAD prediction
<number>

## Slide 10: Experimental results
Percentage error in the actual bitrate (%) in R-lambda model-based rate control case
<number>
Sequence | R-lambda model-based rate control |  |  |  | R-lambda model-based rate control + the proposed methods |  |  | 
 | Average view0 | Average view1 | Average view2 | total | Average view0 | Average view1 | Average view2 | total
Balloons | 0.79 | 1.10 | 1.05 | 0.89 | 0.79 | 1.60 | 1.59 | 1.08
Kendo | 0.25 | 0.89 | 0.82 | 0.47 | 0.25 | 0.96 | 0.91 | 0.50
Newspaper | 1.00 | 1.04 | 0.99 | 1.01 | 1.00 | 1.37 | 1.27 | 1.12
GTFly | 0.48 | 0.90 | 0.96 | 0.50 | 0.48 | 3.80 | 4.26 | 1.20
Poznanhall2 | 0.45 | 1.31 | 1.01 | 0.49 | 0.45 | 1.34 | 1.52 | 0.50
Poznanstreet | 2.73 | 1.58 | 1.58 | 2.40 | 2.73 | 3.63 | 4.02 | 3.00
Dancer | 0.58 | 0.44 | 0.45 | 0.53 | 0.58 | 0.81 | 0.82 | 0.59
Average | 0.90 | 1.04 | 0.98 | 0.90 | 0.90 | 1.93 | 2.06 | 1.14

## Slide 11: Experimental results
Compression performance in R-lambda model-based rate control case
<number>
Sequence | Bdrate of R-lambda only vs. R-lambda + the proposed | 
 | average view1 | average view2
Balloons | -4.12 | -3.78
Kendo | -2.75 | -2.71
Newspaper | -6.79 | -8.10
GTFly | 4.36 | 4.77
Poznanhall2 | -5.50 | -6.49
Poznanstreet | -2.44 | -2.69
Dancer | -1.47 | -1.38
Average | -2.67 | -2.91

## Slide 12: Experimental results
Percentage error in the actual bitrate (%) in URQ model-based rate control case
<number>
Sequence | URQ model-based rate control |  |  |  | URQ model-based rate control + the proposed methods |  |  | 
 | Average view0 | Average view1 | Average view2 | total | Average view0 | Average view1 | Average view2 | total
Balloons | 0.79 | 0.54 | 0.68 | 0.71 | 0.79 | 0.54 | 0.53 | 0.67
Kendo | 0.67 | 0.51 | 0.49 | 0.56 | 0.67 | 0.51 | 0.49 | 0.56
Newspaper | 1.68 | 2.14 | 1.74 | 1.77 | 1.68 | 2.22 | 2.05 | 1.84
GTFly | 0.50 | 0.95 | 6.25 | 0.50 | 0.50 | 0.48 | 6.66 | 0.48
Poznanhall2 | 0.76 | 2.45 | 2.76 | 0.67 | 0.76 | 1.39 | 2.73 | 0.78
Poznanstreet | 0.46 | 1.43 | 4.95 | 0.73 | 0.46 | 1.13 | 3.32 | 0.64
Dancer | 0.54 | 0.55 | 0.73 | 0.45 | 0.54 | 0.45 | 0.82 | 0.44
Average | 0.77 | 1.22 | 2.51 | 0.77 | 0.77 | 0.96 | 2.37 | 0.77

## Slide 13: Experimental results
Compression performance in URQ model-based rate control case
<number>
Sequence | Bdrate of URQ only vs. URQ+ the proposed | 
 | average view1 | average view2
Balloons | 0.30 | -0.31
Kendo | 1.70 | 1.35
Newspaper | 1.12 | 3.19
GTFly | -0.80 | -0.34
Poznanhall2 | -0.83 | -0.13
Poznanstreet | 4.03 | -3.60
Dancer | -0.18 | 0.35
Average | 0.76 | 0.07

## Slide 14: Experimental results
Frame-wise accumulated virtual buffer occupancy in R-lambda model-based rate control case
  Anchor (black) : only R-lambda or URQ model-based rate control is used
  Proposed (red) : R-lambda or URQ model-based rate control is used with the proposed inter-view MAD prediction
<number>

## Slide 15: Experimental results
Ex) R-lambda / Dancer / extended views / Random Access / R2
<number>

## Slide 16: Experimental results
Ex) URQ / Dancer / extended views / Random Access / R2
<number>

## Slide 17: Conclusion
We proposed two methods to improve rate control of extended views in multi-view video coding based on HEVC
  View-wise target bitrate allocation
  Inter-view MAD prediction for the extended view
The proposed methods can be used with any rate control algorithms that relies on the prediction of to-be-generated bits from MAD or other error metrics, including the newly adopted R-lambda model-based algorithm
All the experimental results are crosschecked by KHU
In the 3rd meeting in Geneva, we proposed the same algorithms
  A few supports, no objection
  The reason why it is not adopted is there was no implementation of rate control in reference software
  The current proposed algorithms are implemented in HTM7.0_r1 based on HTM-DEV0.3 and our previous implementation
  We can provide the source code
We recommend the proposed methods to be adopted to the current rate control for multi-view video coding
<number>