## Slide 1: On DMM Simplification
Zhouye Gu (Santa Clara University)
Jianhua Zheng (HiSilicon)
Nam Ling (Santa Clara University)
JCT3V-E0242

## Slide 2: Introduction
Motivation: simplification for DMM4 to remove division in the depth wedgelet Pattern derivation.
Experimental results based on HTM7.0r1: no impact on coding performance
Thanks NTT for crosscheck (JCT3V-E0298)

## Slide 3: Introduction
At current DMM4 design, a threshold value is set as the average of the sample values inside a texture intra block and is used for derivation of the binary depth wedgelet Pattern.
The division are shown as follows:
– The variable sumTextPicVals is set equal to 0.
– For x = 0..nT−1 the following applies
– For y = 0..nT−1 the following applies
sumTextPicVals += recTextPic[ xB + x ][ yB + y ] (H 38)
– The variable textThresh = sumTextPicVals / ( nT * nT )

## Slide 4: Our Solution
For DMM4, the candidate block can only have size 8x8, 16x16 and 32x32
In a CU, different size corresponds to different coding tree depth as show in Table 1
Table 1 Block size and partition depth correspondence
Propose to use codingTree_depth, ctDepth, as an indicator of block size for average value calculation
textThresh = sumTextPicVals >> (6 - ctDepth)*2 (1)
Block size | 8x8 | 16x16 | 32x32
codingTree_depth (ctDepth) | 3 | 2 | 1

## Slide 5
All Intra test result
Random Access (CTC) test result

## Slide 6: Text Changes

## Slide 7: Summary
Simplification for DMM4 to remove division is proposed.
Simplify hardware implementation with no impact on the coding performance
Suggest to adopt the proposed solution

## Slide 8: Thank you!