## Slide 1: MV-HEVC/SHVC HLS: Skipped slice and use case (JCTVC-O0055, JCT3V-F0032)
JCT-VC 15th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
JCT-3V 6th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
Tomoyuki Yamamoto, Tomohiro Ikai, Takeshi Tsukuba
SHARP Corporation

## Slide 2: Summary
This contribution includes
  Introduction of ROI-capable scalable video application
  Proposals relating skipped slices to support the application
Proposed changes:
  Indication syntax whether all tiles included in CVS are motion constrained.
  Slice-level non-significant slice indication flag
  Slice-level syntax for the number of skipped CTUs in skipped slice based on max number of CTUs included in the tile
  Bitstream constraint on conformance cropping window to include only non-skipped tiles.

## Slide 3: ROI application using SHVC
BL
EL 00
S. Ha QB Field 3/9
EL: Enhancement Layer
BL: Base Layer
EL00
SHVC encoder
Intelligent network element
BL
EL 21
EL 22
BL
EL 30
EL 20
EL 31
EL 21
EL 10
EL 00
EL 11
EL 01
EL 32
EL 22
EL 33
EL 23
EL 12
EL 02
EL 13
EL 03
BL
EL 21
BL
EL 11
BL
EL 22
BL
EL 30
EL 20
EL 31
EL 21
EL 10
EL 00
EL 11
EL 01
EL 32
EL 22
EL 33
EL 23
EL 12
EL 02
EL 13
EL 03
SHVC bitstream

## Slide 4: System components and data requirements
SHVC encoder / SHVC bitstream
  Part of EL bitstream need to be decoded independent of rest parts of EL. When encoding such EL tile, non-collocated part of BL region could be referenced via inter-layer prediction.
Intelligent Network Element (INE)
  INE receives ROI requests from a user.
  INE extracts the sub bitstream corresponding to the requested ROI from the whole bitstreams.
    Extraction process should be easy. INE could discard NAL units based on NAL unit header, VPS, and SPSs. INE overwrite syntax values in VPS, SPS and PPS parameters. INE might overwrite some slice header syntax corresponding to the ROI but should not modify slice data corresponding to the non-ROI. INE should not use information acquired by decoding slice data (e.g. decoded picture, syntax elements below slice data, etc.).
Client terminal
  Client terminal shall have SHVC decoder to decode sub bitstream corresponding to ROI.

## Slide 5: Codec support
To support ROI-capable scalable video application with SHVC, combination of “Skipped slices” and “Motion constrained tile set” are useful.
It is proposed to support those tools. Details are described in following slides.

## Slide 6: Proposed changes
A flag to indicate independent decodability of tiles
sps_extension ( ) { | Descriptor
… | 
all_tiles_decoding_dependency_flag | u(1)
} | 
all_tiles_decoding_dependency_flag equal to 1 specifies that all tiles in CVS are motion constrained. all_tiles_decoding_dependency_flag equal to 0 specifies that all tiles in CVS may not be motion constrained.

## Slide 7: Proposed changes
Skipped slice indication / number of CTBs in skipped slice
  skipped slice indication flag is signalled when multiple tiles are used and tiles are motion constrained
slice_segment_header( ) { | Descriptor
… | 
… | 
if( slice_segment_header_extension_present_flag ) { | 
slice_segment_header_extension_length | ue(v)
if ( tiles_enabled_flag && all_tiles_decoding_dependency_flag ) | 
{ | 
non_significant_tile_flag | u(1)
if( non_significant_tile _flag ) | 
num_ctu_in_slice_segment_minus1 | ue(v)
} | 
… | 
} | 
non_significant_tile_flag equal to 1 specifies that the tile containing the slice is the non-significant tile. non_significant_tile_flag equal to 0 specifies that the tile containing the slice is not non-significant tile. When not present, non_significant_tile_flag is inferred to be equal to 0.
num_ctb_in_slice_segment_minus1 plus 1 specifies the number of CTUs in the current slice segment. The length of the num_ctu_in_slice_segment_minus1 syntax element is Ceil( Log2( ColWidth[tileIdx] * RowHeight[tileIdx] ) bits, where tileIdx is equal to TileId[ CtbAddrRsToTs[ slice_segment_address ] ].

## Slide 8: Proposed changes
Slice segment data
Reconstruction
slice_segment_layer_rbsp( ) { | Descriptor
slice_segment_header( ) | 
if (!non_significant_slice_segment_flag) | 
slice_segment_data( ) | 
rbsp_slice_segment_trailing_bits( ) | 
} | 
All pixels in all CTU in a non-significant slice segment are not required to be decoded. When they are decoded, they shall have the value of 0.

## Slide 9: Proposed changes
Loop filter
  When nuh_layer_id associated with the PPS is greater than 0 and non-significant slice exists in the current CVS, loop_filter_across_tiles_enabled_flag shall be equal to 0.
Conformance window
  Conformance window shall not include non-significant slice.

## Slide 10: Conclusion
This contribution includes
  Introduction of ROI-capable scalable video application
  Proposals relating skipped slices to support the application
    Indication syntax whether all tiles included in CVS are motion constrained.
    Slice-level non-significant slice indication flag
    Slice-level syntax for the number of skipped CTUs in skipped slice based on max number of CTUs included in the tile
    Bitstream constraint on conformance cropping window to include only non-skipped tiles.
It is recommended to adopt proposed modifications to support ROI-capable scalable video application.