## Slide 1: MV-HEVC/SHVC HLS: On profile, tier, and level information (JCTVC-O0058, JCT3V-F0035)
JCT-VC 15th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
JCT-3V 6th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
Takeshi Tsukuba, Tomoyuki Yamamoto, Tomohiro Ikai
SHARP Corporation

## Slide 2: Summary
Problem
  It is not useful that “Profile_ref_minus1[i]” constantly sues 6 bits and in many case, the information can be inferred from the previous one since encoder can arrange elements of a list of profile_tier_level().
  profile_tier_level() can be not present. It is very confusing that there are unknown values that can be referred by output layer set with profile_level_tier_idx[].
  profile_tier_level() in VPS extension is not byte-aligned, while In HEVC ver.1, profile_tiler_level() is byte-aligned.
  Proposal
      For issue A, remove profile_ref_minus1.
      For issue B, add inference rules for sub-layer profile and level information.
      For issue C, add byte-alignment for prfile_teir_level() in VPS extension.
  Benefits
      Reduce bit amount of profile_ref_minus1[i] ( and easy to byte-aligned).
      Avoid confusing undefined value handling of profile_tier_level().
      Easy to decode profile_tier_level() of layer set, which is important when negotiation.
Notes:   Avoid the improper removal of sharing parameter set in bitstream extraction.
  Enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
  Enhance SPS sharing capability for Extended Spatial Scalability.

## Slide 3: Introduction
The profile_tier_level() for layer sets are decoded as follows:
  Decode a list of profile_tier_level() with vps_profile_present_flag/profile_ref_minus1
  Select decoded profile_tier_level() by profile_level_tier_level_idx[i] for the layer set
However, there exits several issues, called issue A to issue C.
  It is not useful that “Profile_ref_minus1[i]” constantly sues 6 bits and in many case, the information can be inferred from the previous one since encoder can arrange elements of a list of profile_tier_level().
  profile_tier_level(), which is referred by profile_level_tier_idx, can be not present. It is very confusing that there are unknown values that can be referred by output layer set with profile_level_tier_idx[].
  profile_tier_level() in VPS extension is not byte-aligned, while In HEVC ver.1, profile_tiler_level() is byte-aligned.

## Slide 4: Solution A for issue A
    Remove profile_ref_minus1
    Use vps_present_flag equal to 0 as substitute for profile_ref_minus1 to refer the profile_tier_level()
      Solution A can reduce bit amount of profile_ref_minus1[i].
      Note that encoder can arrange elements of a list of profile_tier_level()
      See next page on text changes for Solution A.
Notes: The proposal adds the following restriction.
F.7.4.2.4 Order of VPS, SPS and PPS RBSPs and their activation
It is a requirement of bitstream conformance that, when an SPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.
It is a requirement of bitstream conformance that, when a PPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.

## Slide 5: Text changes on Solution A
vps_extension( ) { | Descriptor
…snipped… | 
vps_number_layer_sets_minus1 | u(10)
vps_num_profile_tier_level_minus1 | u(6)
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
if( !vps_profile_present_flag[ i ] ) | 
profile_ref_minus1[ i ] | u(6)
profile_tier_level( vps_profile_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
} | 
…snipped… | 
} | 
Notes: The proposal adds the following restriction.
F.7.4.2.4 Order of VPS, SPS and PPS RBSPs and their activation
It is a requirement of bitstream conformance that, when an SPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.
It is a requirement of bitstream conformance that, when a PPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.

## Slide 6: Solution B for issue B
    In addition to solution 1,
    Add a inference rule which indicates that, - When the level information is not present for the i-th sub-layer, - Inferred to be equal to the (i+1)-th sub-layer’s or general level information
    Add a inference rule which indicates that, - When vps_profile_present_flag is equal to 1 and the profile information is not present for the i-th sub-layer - Inferred to be equal to the (i+1)-th sub-layer’s or general profile information.
      Solution B can solve confusing undefined value handling of profile_tier_level().
      See next page on text changes for Solution B.
Notes: In addition to the above changes of issue A, the following changes are applied;
Add inference rule which indicates that, when the level information is not present for the i-th sub-layer, it is inferred to be equal to the (i+1)-th sub-layer’s or general level information.
Add inference rule which indicates that, when the profile information is not present for the i-th sub-layer, it is inferred to be equal to the (i+1)-th sub-layer’s or general profile information.

## Slide 7: Text changes on Solution B
Notes: The proposal adds the following restriction.
F.7.4.2.4 Order of VPS, SPS and PPS RBSPs and their activation
It is a requirement of bitstream conformance that, when an SPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.
It is a requirement of bitstream conformance that, when a PPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.

## Slide 8: Solution C for issue C
    Rearrange the syntax elements (e.g. splitting_flag to vps_vui_present_flag) on top part on VPS extension.
    Option A) Add a syntax vps_ptr_info_offset indicating byte-offset from starting of VPS NAL to the syntax(e.g. vps_num_layer_sets_minus1) related to profile_tier_level()
    Option B) Move syntaxes related to profile_tier_level() after scalability_mask_flag
    In addition above changes,
      Option 1) add byte-alignment bits between those syntaxes, with signaling vps_profile_present_flag[i] and profile_tier_level() separately.
      Option 2) Extend bit-length of profile_ref_minus1[i] from 6 bits to 8bits
      Solution C can enable decoder to easily access profile_tier_level() of layer set, which is important when negotiation.
      See next page on text changes for Solution C.
Notes: In addition to the above changes of issue A, the following changes are applied;
Add inference rule which indicates that, when the level information is not present for the i-th sub-layer, it is inferred to be equal to the (i+1)-th sub-layer’s or general level information.
Add inference rule which indicates that, when the profile information is not present for the i-th sub-layer, it is inferred to be equal to the (i+1)-th sub-layer’s or general profile information.

## Slide 9: Text changes on Solution C (Option A)
Option A:changes are highlighted in cyan and yellow and removals are stroke through in red.
F.7.4.3.1.1 Video parameter set extension semantics
vps_ reserved_zero_6bits shall be equal to 0 in bitstreams conforming to this version of this Specification. Other values for vps_ reserved_zero_6bits are reserved for future use by ITU-T | ISO/IEC. Although the value of vps_ reserved_zero_6bits is required to be equal to 0 in this version of this Specification, decoders shall allow other values of vps_ reserved_zero_6bits to appear in the syntax.
vps_ptr_info_offset specifies the byte offset, starting from the beginning of the VPS NAL unit, of the set of fixed-length coded information starting from vps_number_layer_sets_minus1, in the VPS NAL unit. Emulation prevention bytes that appear in the VPS NAL unit are counted for purposes of byte offset identification.

## Slide 10: Text changes on Solution C (option A)
vps_extension( ) { // Option A | Descriptor
avc_base_layer_flag | u(1)
splitting_flag | u(1)
vps_nuh_layer_id_present_flag | u(1)
max_tid_ref_present_flag | u(1)
all_ref_layers_active_flag | u(1)
rep_format_idx_present_flag | u(1)
max_one_active_ref_layer_flag | u(1)
cross_layer_irap_aligned_flag | u(1)
single_layer_for_non_irap_flag | u(1)
vps_vui_present_flag | u(1)
vps_reserved_6bits | u(6)
vps_vui_offset | u(16)
vps_ptr_info_offset | u(16)
splitting_flag | u(1)
… | 
vps_nuh_layer_id_present_flag | u(1)
… | 
max_tid_ref_present_flag | u(1)
… | 
all_ref_layers_active_flag | u(1)
… | 
// option 2) | 
while (!byte_aligned()) | 
vps_alignment_bit_equal_to_one | u(1)
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
if( !vps_profile_present_flag[ i ] ) | 
profile_ref_minus1[ i ] | u(6) u(8)
profile_tier_level( vps_profile_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
} | 
// option 1) | 
while(!byte_aligned() ) | 
vps_aliginment_bit_equal_to_one | u(1)
vps_number_layer_sets_minus1 | u(10)
vps_num_profile_tier_level_minus1 | u(6)
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
} | 
for( i = ((8-(vps_num_profile_tier_level_minus1 + 1)%8)%8); i >0 ;i-- ) { | 
vps_reseved_zero_bit[ i ] | u(1)
} | 
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
if( !vps_profile_present_flag[ i ] ) | 
profile_ref_minus1[ i ] | u(6)
profile_tier_level( vps_profile_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
} | 
… | 
rep_format_idx_present_flag | u(1)
… | 
max_one_active_ref_layer_flag | u(1)
cross_layer_irap_aligned_flag | u(1)
… | 
single_layer_for_non_irap_flag | u(1)
vps_vui_present_flag | u(1)
… | 
} | 
Byte-aligned
Byte-aligned
Byte-aligned

## Slide 11: Text changes on Solution C (option B)
vps_extension( ) { // Option A | Descriptor
avc_base_layer_flag | u(1)
splitting_flag | u(1)
vps_nuh_layer_id_present_flag | u(1)
max_tid_ref_present_flag | u(1)
all_ref_layers_active_flag | u(1)
rep_format_idx_present_flag | u(1)
max_one_active_ref_layer_flag | u(1)
cross_layer_irap_aligned_flag | u(1)
single_layer_for_non_irap_flag | u(1)
vps_vui_present_flag | u(1)
vps_reserved_6bits | u(6)
vps_vui_offset | u(16)
splitting_flag | u(1)
…// scalaibility mask flag | 
vps_nuh_layer_id_present_flag | u(1)
… | 
max_tid_ref_present_flag | u(1)
… | 
all_ref_layers_active_flag | u(1)
…. | 
rep_format_idx_present_flag | u(1)
… | 
max_one_active_ref_layer_flag | u(1)
cross_layer_irap_aligned_flag | u(1)
… | 
single_layer_for_non_irap_flag | u(1)
vps_vui_present_flag | u(1)
… | 
} | 
// option 2) | 
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
if( !vps_profile_present_flag[ i ] ) | 
profile_ref_minus1[ i ] | u(6) u(8)
profile_tier_level( vps_profile_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
} | 
// option 1) | 
vps_number_layer_sets_minus1 | u(10)
vps_num_profile_tier_level_minus1 | u(6)
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
} | 
for( i = ((8-(vps_num_profile_tier_level_minus1 + 1)%8)%8); i >0 ;i-- ) { | 
vps_reseved_zero_bit[ i ] | u(1)
} | 
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
if( !vps_profile_present_flag[ i ] ) | 
profile_ref_minus1[ i ] | u(6)
profile_tier_level( vps_profile_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
} | 
Byte-aligned
Byte-aligned
Byte-aligned

## Slide 12: Conclusion
  Proposal
      For issue A, remove profile_ref_minus1.
      For issue B, add inference rules for sub-layer profile and level information.
      For issue C, add byte-alignment for prfile_teir_level() in VPS extension.
  Benefits
      Reduce bit amount of profile_ref_minus1[i] ( and easy to byte-aligned).
      Avoid confusing undefined value handling of profile_tier_level().
      Easy to decode profile_tier_level() of layer set, which is important when negotiation.
      It is recommended to adopt proposals to next SHVC/MV-HEVC.
Notes:   Avoid the improper removal of sharing parameter set in bitstream extraction.
  Enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
  Enhance SPS sharing capability for Extended Spatial Scalability.

## Slide 13
Thank you!