## Slide 1: On independent layer (JCTVC-O0062, JCT3V-F0039)
JCT-VC 15th Meeting in Geneva, CH, 23 Oct. - 2 Nov. 2013
JCT-3V 6th Meeting in Geneva, CH, 25 Oct. - 2 Nov. 2013
Tomohiro Ikai , Takeshi Tsukuba, Tomoyuki Yamamoto
SHARP Corporation

## Slide 2: Summary
Motivation
    Independent layer, where direct_dependency_flag[] of the layer is 0, is used for cases such as supplementary video which is synchronized with the main video but is not correlated
    Simple decoder (multiple HEVC version1 decoder) should be enough to manage the abobe pattern.
    Independent layer should be decordable with HEVC version 1 if nal_layer_id is ignored but current syntax doesn’t allow it because a couple of syntax changes are incorporated when nal_layer_id > 0.
  Proposal
    Option1
      strictly disallowing syntax change for independent layers
    Option2
      allow syntax changes only if that is indicated in VPS
  Benefits
    HEVC version 1 decoder can decode independent layers (nuh_layer_id aside)
    Note: Independent layers are determined by VPS, so with this proposal, the dependency between SPS/PPS and VPS appears. If we truly need to avoid that dependency, it might be needed to conceive SPS/PPS syntax change.

## Slide 3: Introduction
Several syntax changes are incorporated in SHVC / MV-HEVC
  Representing format (SPS)
  Scaling list prediction (SPS / PPS)
  POC alignment (slice segment header)
No longer possible that simple HEVC version 1 decoder decode independent layers although independent layer doesn’t use new prediction tool at all

## Slide 4: Exsamples of the syntax change
seq_parameter_set_rbsp( ) { | Descriptor
sps_video_parameter_set_id | u(4)
if(nuh_layer_id = = 0 ) { [1] | 
sps_max_sub_layers_minus1[M1007] | u(3)
sps_temporal_id_nesting_flag [K0276][M1007] | u(1)
profile_tier_level( 1, sps_max_sub_layers_minus1 ) | 
} | 
sps_seq_parameter_set_id | ue(v)
if(nuh_layer_id > 0 ) [2] | 
update_rep_format_flag | u(1)
pic_parameter_set_rbsp( ) { | Descriptor
… | 
if(nuh_layer_id > 0 ) [3] | 
pps_infer_scaling_list_flag | u(1)
if( pps_infer_scaling_list_flag ) | 
pps_scaling_list_ref_layer_id | u(6)
else { | 
pps_scaling_list_data_present_flag | u(1)
if( pps_scaling_list_data_present_flag ) | 
scaling_list_data( ) | 
} | 
… | 
} | 
slice_segment_header( ) { | Descriptor
… | 
if( !dependent_slice_segment_flag ) { | 
… | 
if(nuh_layer_id > 0 ¦ [4]¦ ( nal_unit_type != IDR_W_RADL && nal_unit_type != IDR_N_LP ) ) { | 
slice_pic_order_cnt_lsb | u(v)
SPS
PPS
slice segment header

## Slide 5: Proposal
  Option1
    strictly disallowing syntax change for independent layers
  Option2
    allowing syntax changes only if that is indicated in VPS

## Slide 6: WD change
    Option1 and Option2 (common)

## Slide 7: WD change
    Option1
seq_parameter_set_rbsp( ) { | Descriptor
sps_video_parameter_set_id | u(4)
if( IndependentLayerFlag [nuh_layer_id] ¦¦ nuh_layer_id = = 0 ) { | 
sps_max_sub_layers_minus1 | u(3)
sps_temporal_id_nesting_flag | u(1)
profile_tier_level( 1, sps_max_sub_layers_minus1 ) | 
} | 
sps_seq_parameter_set_id | ue(v)
if(! IndependentLayerFlag [nuh_layer_id] && nuh_layer_id > 0 ) | 
update_rep_format_flag | u(1)
… | 
if( scaling_list_enabled_flag ) { | 
if(! IndependentLayerFlag [nuh_layer_id] && nuh_layer_id > 0 ) | 
sps_infer_scaling_list_flag | u(1)
… | 
} | 
pic_parameter_set_rbsp( ) { | Descriptor
… | 
if(! IndependentLayerFlag [nuh_layer_id] && nuh_layer_id > 0 ) | 
pps_infer_scaling_list_flag | u(1)
… | 
} | 
slice_segment_header( ) { | Descriptor
… | 
if( !dependent_slice_segment_flag ) { | 
… | 
if(! IndependentLayerFlag [nuh_layer_id] && nuh_layer_id > 0 ¦ ¦ ( nal_unit_type != IDR_W_RADL && nal_unit_type != IDR_N_LP ) ) { | 
slice_pic_order_cnt_lsb | u(v)

## Slide 8: WD change
    Option2
vps_extension( ) { | Descriptor
… | 
rep_format_idx_present_flag | u(1)
if( rep_format_idx_present_flag ) | 
vps_num_rep_formats_minus1 | u(4)
for( i = 0; i <= vps_num_rep_formats_minus1; i++ ) | 
rep_format( ) | 
if( rep_format_idx_present_flag ) | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) | 
if( vps_num_rep_formats_minus1 > 0 ) | 
vps_rep_format_idx[ i ] | u(4)
vps_syntax_change_by_layer_id_flag | v(1)
max_one_active_ref_layer_flag | u(1)
… | 
} | 

## Slide 9: WD change
    Option2
seq_parameter_set_rbsp( ) { | Descriptor
sps_video_parameter_set_id | u(4)
if( !vps_syntax_change_by_layer_id_flag ¦¦ nuh_layer_id = = 0 ) { | 
sps_max_sub_layers_minus1 | u(3)
sps_temporal_id_nesting_flag | u(1)
profile_tier_level( 1, sps_max_sub_layers_minus1 ) | 
} | 
sps_seq_parameter_set_id | ue(v)
if(vps_syntax_change_by_layer_id_flag && nuh_layer_id > 0 ) | 
update_rep_format_flag | u(1)
… | 
if( scaling_list_enabled_flag ) { | 
if(vps_syntax_change_by_layer_id_flag && nuh_layer_id > 0 ) | 
sps_infer_scaling_list_flag | u(1)
… | 
} | 
pic_parameter_set_rbsp( ) { | Descriptor
… | 
if(vps_syntax_change_by_layer_id_flag && nuh_layer_id > 0 ) | 
pps_infer_scaling_list_flag | u(1)
… | 
} | 
slice_segment_header( ) { | Descriptor
… | 
if( !dependent_slice_segment_flag ) { | 
if( vps_syntax_change_by_layer_id_flag && nuh_layer_id > 0 ¦ ¦ ( nal_unit_type != IDR_W_RADL && nal_unit_type != IDR_N_LP ) ) { | 
slice_pic_order_cnt_lsb | u(v)

## Slide 10: Conclusion
  Proposal
    Option1
      strictly disallowing syntax change for independent layers
    Option2
      allow syntax changes only if that is indicated in VPS.
  Benefits
    HEVC version 1 decoder can decode independent layers (nuh_layer_id aside)
Recommend to adopt this simple method in SHVC and MV-HEVC

## Slide 11
Thank you!