## Slide 1: JCT3V-F0045 3D-HEVC HLS: Constraints on Camera Parameter Signaling
Yu-Lin Chang, Yi-Wen Chen, Jian-Liang Lin, Yu-Pao Tsai, Shawmin Lei
Presented by Yu-Lin Chang
6th JCT3V Meeting in Geneva
25 Oct. – 1 Nov., 2013

## Slide 2: Overall Summary
In current 3D-HEVC, camera parameters of a texture layer can be replaced with those of a depth layer of the same view, which may cause wrong depth-to-disparity conversion
Two methods are proposed to solve the ambiguity problem of the camera parameter signaling for layers with the same view order index.
  Allow at most one layer per view with its cp_present_flag equal to 1 and to transmit camera parameters in the slice segment header extension only when cp_present_flag of the layer and cp_in_slice_segment_header_flag are both equal to 1
  Force the camera parameters to be the consistent for all layers of the same view
Notes:     Problem and proposeVSP off, finding inter-view reference without warping

## Slide 3: Current Camera Parameter Signaling in 3D-HEVC
Camera parameter signaling depends on the cp_present_flag for each layer
VPS_header_extension2( ) { | Descriptor
… | 
if ( layerId ! = 0 ) { | 
cp_present_flag[ layerId ] | u(1)
… | 
cp_precision | ue(v)
cp_in_slice_segment_header_flag | u(1)
if( !cp_in_slice_segment_header_flag ) | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
layerId = layer_id_in_nuh[ i ] | 
if( cp_present_flag[ layerId ] ) { | 
viewIdx = ViewOrderIdx[ layerId ] | 
for( j = 0; j < viewIdx; j++ ) { | 
vps_cp_scale[ viewIdx ][ j ] | se(v)
vps_cp_off[ viewIdx ][ j ] | se(v)
vps_cp_inv_scale_plus_scale[ viewIdx ][ j ] | se(v)
vps_cp_inv_off_plus_off[ viewIdx ][ j ] | se(v)
} | 
} | 
} | 

## Slide 4: Current Camera Parameter Signaling in 3D-HEVC (2/2)
The camera parameters are stored for each view order index whereas the camera parameters could be signaling for each layer
The camera parameters of a layer can be overwritten by those of another layer with a larger layer index when the two layers have the same view order index.

## Slide 5: Proposed Bug-fix For the Missing Braces
A pair of missing braces is added.
VPS_header_extension2( ) { | Descriptor
… | 
if ( layerId ! = 0 ) { | 
cp_present_flag[ layerId ] | u(1)
… | 
cp_precision | ue(v)
cp_in_slice_segment_header_flag | u(1)
if( !cp_in_slice_segment_header_flag ) | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
layerId = layer_id_in_nuh[ i ] | 
if( cp_present_flag[ layerId ] ) { | 
viewIdx = ViewOrderIdx[ layerId ] | 
for( j = 0; j < viewIdx; j++ ) { | 
vps_cp_scale[ viewIdx ][ j ] | se(v)
vps_cp_off[ viewIdx ][ j ] | se(v)
vps_cp_inv_scale_plus_scale[ viewIdx ][ j ] | se(v)
vps_cp_inv_off_plus_off[ viewIdx ][ j ] | se(v)
} | 
} | 
} | 

## Slide 6: Proposed Method 1 – Restrict cp_present_flag to Prevent Overwriting
Add a constraint on cp_present_flag to allow only up to one layer of a view to signal camera parameters in the VPS
Allow camera parameters coded in the slice segment header extension only when both cp_in_slice_segment_header_flag and cp_present_flag[ nuh_layer_id ] are equal to 1.

## Slide 7: Working Draft Changes for Method 1
Proposed constraint on cp_present_flag
Proposed change on slice segment header extension
slice_segment_header_extension( ) { | Descriptor
if( cp_in_slice_segment_header_flag && cp_present_flag[ nuh_layer_id ] ) { | 
for ( i = 0; i < ViewIdx; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 

## Slide 8: Proposed Method 2 – Force Using the Same Camera Parameters
Add a normative constraint saying that camera parameters with the same view shall be the consistent.

## Slide 9: Working Draft Changes for Method 2
Proposed constraint on camera parameters

## Slide 10: Conclusions
One bug-fix for VPS is first provided
Two methods are proposed to solve the conflict when camera parameters are inconsistent between two layers of the same view
  Allow up to only one layer with cp_present_flag equal to 1 for each view, and allow camera parameters coded in the slice segment header extension only when cp_present_flag of the layer and cp_in_slice_segment_header_flag are both equal to 1
  Force the camera parameters to be consistent for all layers of the same view

## Slide 11: Thanks for your attention!
www.mediatek.com