## Slide 1
Carriage of auxiliary pictures (JCTVC-O0135/JCT3V-F0048)
Byeongdoo Choi
Samsung Electronics Co., Ltd
Oct., 2013
Notes: <number>

## Slide 2: Outline
Needs of carriage of auxiliary picture were discussed. One promising solution is proposed by JCTVC-O0041(Nokia).
Two alternative solutions of carriage of auxiliary pictures
  With new NAL unit type (proposed): Option-1
  With new scalability dimension (Nokia, JCTVC-O0041): Option-2
Improvements of options 1&2
  Indication of used auxiliary pictures for each layer : for Option-1
  Grouped signalling of layer dependencies : for Option-2
Constraints for Options 1&2
Modification of default_one_target_output_layer_flag for Option-2
<number>

## Slide 3: Solution-1
A nal_unit_type, namely AUX_NUT, is assigned to indicate auxiliary pictures. The types of auxiliary pictures are signalled in slice headers of VCL NAL units.
<number>
Table 7‑1 – NAL unit type codes and NAL unit type classes
aux_id specifies the type of auxiliary pictures.
aux_id | auxiliary picture type
0 | Primary picture
1 | Depth map
2 | Alpha map
3 | Enhanced chroma

## Slide 4: Solution-1 (alternative)
Multiple NAL unit types can be allocated for indicating various auxiliary picture types.
<number>
if( nal_unit_type > 40 && nal_unit_type < 44) AuxId = nal_unit_type – 40
else AuxId = 0

## Slide 5: Comparison of two alternative methods
Our suggestion is the first option (NAL unit type indication), but both are applicable to carry auxiliary pictures.
On option-1: NAL unit type
  Pros: 1) From a nuh_layer_id without mapping to scalability dimensions, the corresponding auxiliary pictures of a primary picture can be identified.
  Pros: 2) The layer dependency information is more efficiently represented by signalling only dependencies between primary pictures.
  Pros: 3) Auxiliary pictures with the corresponding primary picture in DPB are synchronously handled.
  Pros: 4) Many NAL unit types are reserved, while nuh_layer_id (6 bits) is not enough to represent multiple scalability dimensions.
  Pros: 5) A single layer bitstream with auxiliary pictures is available.
On option-2: Scalability dimension (same as described in JCTVC-O0041)
  Pros: 1) Easy bitstream extraction is possible with nuh_layer_id.
  Pros: 2) The presence of auxiliary pictures are indicated in VPS.
  Pros: 3) No NAL unit type is burned.
  Pros: 4) Decoders can choose the CPB HRD parameters with or without auxiliary pictures.
<number>

## Slide 6: Indication of auxiliary picture types for each layer in VPS (for options-1)
<number>

## Slide 7: Grouped signalling of layer dependencies in VPS (for option-2)
<number>

## Slide 8: Grouped signalling of layer dependencies in VPS (for option-2)
<number>

## Slide 9: Grouped signalling of layer dependencies in VPS (for option-2)
<number>
vps_aux_picture_use_flag equal to 1 specifies that an auxiliary picture is present in a bitstream, and aux_mask_flag[i] is present in VPS. vps_aux_picture_use_flag equal to 0 specifiest hat an auxiliary picture is not present in a bitstream, and aux_mask_flag is inferred equal to 0.
aux_mask_flag [ i ] equal to 1 indicates that auxiliary pictures with the i-th auxiliay picture type are present in a bitstream. aux_mask_flag [ i ] equal to 0 indicates that auxiliary pictures with the i-th auxialiary picture type are not present in a bitstream.
vps_aux_picture_grouped_flag equal to 1 specifies that the nuh_layer_id of the i-th auxiliary pictures associated with a primary picture with nuh_layer_id equal to k is equal to (k+i). The auxiliary pictures have the same layer dependencies as the corresponding primary pictures. vps_aux_picture_grouped_flag equal to 0 specifies that the above restriction may or may not apply. If not present, vps_aux_picture_grouped_flag is inferred to be equal to 0.
The variables NumDirectRefLayers[ i ],and RefLayerId[ i ][ j ]SamplePredEnabledFlag[ i ][ j ], MotionPredEnabledFlag[ i ][ j ] and DirectRefLayerIdx[ i ][ j ]are derived as follows:
  for( i = 0; i <= vps_max_layers_minus1; i += NumGroupLayers ) { for( k = 0; k < NumGroupLayers; k++ ) { iNuhLId = layer_id_in_nuh[ i ] + k NumDirectRefLayers[ iNuhLId ] = 0 for( j = 0; j < i; j++ ) if( direct_dependency_flag[ i ][ j ] ){ RefLayerId[ iNuhLId ][ NumDirectRefLayers[ iNuhLId ]++ ] = layer_id_in_nuh[ j ] + k SamplePredEnabledFlag[ iNuhLId ][ j ] = (( direct_dependency_type[ i ][ j ] + 1 ) & 1 ) MotionPredEnabledFlag[ iNuhLId ][ j ] = ((( direct_dependency_type[ i ][ j ] + 1 ) & 2 ) >> 1 ) DirectRefLayerIdx[ iNuhLid ][ layer_id_in_nuh[ j ]+k] = NumDirectRefLayers[ iNuhLId ] – 1 } }

## Slide 10: Proposed constraints for options 1&2
<number>

## Slide 11: Proposed constraints for options 1&2
<number>

## Slide 12: Modifications of default_one_target_output_layer_flag semantics (for Option-2)
<number>

## Slide 13
Thank you !
<number>