## Slide 1
Extended layer identifier (JCTVC-O0137/JCT3V-F0050)
Byeongdoo Choi
Samsung Electronics Co., Ltd
Oct., 2013
Notes: <number>

## Slide 2: Motivation
The needs of the feature to increase the maximum number of layers was agreed at the last meetings.
  Extending nuh_layer_id (6bits) to represent more than 64 layers is desirable to cope with Super multi-views.
The basic idea of the previous proposals (N0135/E0115 and N0355/E0092) is to signal the extra bits to be used as LSB bits of nuh_layer_id.
<number>

## Slide 3: Proposals
Two alternative solutions are proposed.
Solution-1: Signaling extra LSB bits of nuh_layer_id
Solution-2: Replacement of nuh_layer_id with ext_layer_id
<number>

## Slide 4: Solution-1
Extra LSB bits (ext_layer_id) of nuh_layer_id are signalled in slice headers, parameter set (SPS, PPS), and SEI messages.
If vps_layer_id_extension_flag is equal to 1
Otherwise
<number>
nuh_layer_id (6bits)
ext_layer_id (x bits)
nuh_layer_id (6bits)
LayerId (6+x bits)
LayerId (6 bits)

## Slide 5: VPS in Solution-1
<number>
vps_layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers. vps_layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used. If not present, vps_layer_id_extension_flag is inferred to be equal to 0.
num_layer_id_extension_bits_minus1 plus1 specifies the number of extra bit to identify layers more than 64.
ext_max_layers_minus1 plus1 specifies the variable MaxNumLayers.
if(layer_id_extension_flag) MaxNumLayers = ext_max_layers_minus1 + 1 else MaxNumLayers = vps_max_layers_minus1 + 1
ext_max_layer_id specifies the maximum allowed value of the extended layer identifier of all NAL units in the CVS. If not present, ext_max_layer_id is inferred to be equal to vps_max_layer_id.

## Slide 6: Slice in Solution-1
<number>
slice_ext_layer_id specifies the variable LayerId, when vps_layer_id_extension_flag is equal to 1. If not present, slice_ext_layer_id is inferred to be equal to 0.
if ( nuh_unit_type < 32 ) { if ( vps_layer_id_extension_flag ) LayerId = nuh_layer_id << (num_layer_id_extension_bits_minus1 + 1) + slice_ext_layer_id else LayerId = nuh_layer_id
}

## Slide 7: SPS in Solution-1
<number>
sps_layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers for sequence parameter set. sps_layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used for sequence parameter set. If not present, sps_layer_id_extension_flag is inferred to be equal to 0.
sps_ext_layer_id specifies the variable LayerId, when sps_layer_id_extension_flag is equal to 1. If not present, sps_ext_layer_id is inferred to be equal to 0.
if ( nuh_unit_type == SPS_NUT ) { if ( sps_layer_id_extension_flag ) LayerId = nuh_layer_id << (num_layer_id_extension_bits_minus1 + 1) + sps_ext_layer_id else LayerId = nuh_layer_id

## Slide 8: PPS in Solution-1
<number>
pps_layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers for picture parameter set. pps_layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used for picture parameter set. If not present, pps_layer_id_extension_flag is inferred to be equal to 0.
pps_ext_layer_id specifies the variable LayerId, when pps_layer_id_extension_flag is equal to 1. If not present, pps_ext_layer_id is inferred to be equal to 0.
if ( nuh_unit_type == PPS_NUT ) { if ( pps_layer_id_extension_flag ) LayerId = nuh_layer_id << (num_layer_id_extension_bits_minus1 + 1) + pps_ext_layer_id else LayerId = nuh_layer_id

## Slide 9: SEI message in Solution-1
<number>
sei_layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers for SEI message. sei_layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used for SEI message. If not present, sei_layer_id_extension_flag is inferred to be equal to 0.
sei_ext_layer_id specifies the variable LayerId, when sei_layer_id_extension_flag is equal to 1. If not present, sei_ext_layer_id is inferred to be equal to 0.
if ( nuh_unit_type == PREFIX_SEI_NUT || nuh_unit_type == SUFFIX_SEI_NUT ) { if (sei_layer_id_extension_flag ) LayerId = nuh_layer_id << (num_layer_id_extension_bits_minus1 + 1) + sei_ext_layer_id else LayerId = nuh_layer_id

## Slide 10: Solution-2
nuh_layer_id (6bits) is replaced with ext_layer_id having more than 6bits, when layer_id_extension_flag in VPS is equal to 1
If layer_id_extension_flag is equal to 1 and nuh_layer_id is equal to 63
Otherwise
<number>
ext_layer_id (x bits)
nuh_layer_id (6bits)
LayerId (x bits)
LayerId (6 bits)

## Slide 11: VPS in Solution-2
<number>
layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers. layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used. If not present, layer_id_extension_flag is inferred to be equal to 0.
ext_layer_id_len_minis1 plus1 specifies the number of bits to identify the extended layer identifiers.
ext_max_layers_minus1 plus1 specifies the variable MaxNumLayers.
if(layer_id_extension_flag) MaxNumLayers = ext_max_layers_minus1 + 1 else MaxNumLayers = vps_max_layers_minus1 + 1
ext_max_layer_id specifies the maximum allowed value of the extended layer identifier of all NAL units in the CVS. If not present, ext_max_layer_id is inferred to be equal to vps_max_layer_id.

## Slide 12: Slice in Solution-2
<number>
slice_ext_layer_id specifies the variable LayerId, when layer_id_extension_flag is equal to 1. If not present, slice_ext_layer_id is inferred to be equal to nuh_layer_id.
if ( nuh_unit_type < 32 ) { if (layer_id_extension_flag ) LayerId = slice_ext_layer_id else LayerId = nuh_layer_id
}

## Slide 13: SPS in Solution-2
<number>
sps_layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers for sequence parameter set. sps_layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used for sequence parameter set. If not present, sps_layer_id_extension_flag is inferred to be equal to 0.
sps_ext_layer_id specifies the variable LayerId, when sps_layer_id_extension_flag is equal to 1. If not present, sps_ext_layer_id is inferred to be equal to nuh_layer_id.
if ( nuh_unit_type == SPS_NUT ) { if ( sps_layer_id_extension_flag ) LayerId = sps_ext_layer_id else LayerId = nuh_layer_id
}

## Slide 14: PPS in Solution-2
<number>
pps_layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers for picture parameter set. pps_layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used for picture parameter set. If not present, pps_layer_id_extension_flag is inferred to be equal to 0.
pps_ext_layer_id specifies the variable LayerId, when pps_layer_id_extension_flag is equal to 1. If not present, pps_ext_layer_id is inferred to be equal to nuh_layer_id.
if ( nuh_unit_type == PPS_NUT ) { if ( pps_layer_id_extension_flag ) LayerId = pps_ext_layer_id else LayerId = nuh_layer_id
}

## Slide 15: SEI message in Solution-2
<number>
sei_layer_id_extension_flag equal to 1 indicates that the extra bits are assigned for layer identifiers to increase the maximum number of layers for SEI message. sei_layer_id_extension_flag equal to 0 indicates that the layer identifier extension is not used for SEI message. If not present, sei_layer_id_extension_flag is inferred to be equal to nuh_layer_id.
sei_ext_layer_id specifies the variable LayerId, when sei_layer_id_extension_flag is equal to 1. If not present, sei_ext_layer_id is inferred to be equal to 0.
if ( nuh_unit_type == PREFIX_SEI_NUT || nuh_unit_type == SUFFIX_SEI_NUT ) { if (sei_layer_id_extension_flag ) LayerId = sei_ext_layer_id else LayerId = nuh_layer_id
}

## Slide 16: Conclusion
Two alternative solutions are proposed.
Solution-1: Signaling extra LSB bits of nuh_layer_id
Solution-2: Replacement of nuh_layer_id with ext_layer_id
Solution-1 is preferable, because nuh_layer_id can indicate group of layers (GOL), when adjacent layers are grouped into a GOL.
The concept of GOL is applicable for carriage of auxiliary pictures.
  A GOL consists of a primary picture and the auxiliary pictures associated with the primary picture.
  When solution-1 is used, nuh_layer_id indicates each GOL, while ext_layer_id indicates the type of auxiliary pictures.
For super multiviews, adjacent views can be grouped into a group of views (GOV).
  A GOV can be identified by nuh_layer_id
<number>

## Slide 17
Thank you !
<number>