## Slide 1
Alignment of picture order counts (JCTVC-O0140/JCT3V-F0053) for AHG10 teleconferences
Byeongdoo Choi
Samsung Electronics Co., Ltd
Nov., 2013
Notes: <number>

## Slide 2: Motivation
For POC value alignments across layers
The following features are considered.
  Compatibility with HEVC ver.1
  Error robustness
  Independent derivation of POC values within each layer
<number>

## Slide 3: Proposal-1
We propose that poc_reset_flag is replaced with poc_msb_reset_flag.
When this flag is equal to 1, the POC MSB value of the current picture is set to 0, in addition, the POC values of the pictures in DPB belonging to the same layer are changed accordingly to maintain the POC differences to the current picture.
poc_msb_reset_flag equal to 1 specifies that the PicOrderCntMsb for the current picture is equal to 0. poc_msb_reset_flag equal to 0 specifies that the derived PicOrderCntMsb for the current picture may or may not be equal to 0. It is a requirement of bitstream conformance that when cross_layer_irap_aligned_flag is equal to 1, the value of poc_msb_reset_flag shall be equal to 0. When not present, the value of poc_msb_reset_flag is inferred to be equal to 0.
<number>

## Slide 4: Problems with poc_reset_flag
When poc_reset_flag is equal to 1 in a base layer, the base layer bitstream is not compatible with HEVC ver.1 decoder, due to the POC LSB mismatch.
poc_reset_flag cannot ensure the POC value alignment, when only POC MSB is reset in a BLA.
When a picture with poc_reset_flag equal to 1 is lost, POC values cannot be correctly derived in the following pictures.
POC LSB is only reset when a base layer is IDR, but then slice_pic_order_cnt_lsb will be equal to 0 in non-base layers. Hence, POC LSB reset indication is not actually needed.
<number>

## Slide 5: Benefits with poc_msb_reset_flag
When poc_msb_reset_flag is equal to 1 in a base layer, the base layer bitstream is compatible with HEVC ver.1 decoder, without POC LSB mismatch.
poc_msb_reset_flag can ensure the POC value alignment, when only POC MSB is reset in a BLA.
poc_msb_reset_flag equal to 1 can indicated in multiple pictures from the reset points to POC MSB incrementing point. Even though a picture with poc_msb_reset_flag equal to 1 is lost, POC MSB reset can be done by the follow pictures.
POC LSB reset indication is not needed. (base-layer IDR reset POC to 0)
<number>

## Slide 6: For error robustness
poc_msb_reset_flag equal to 1 can be indicated in multiple pictures before POC MSB increases for improving error robustness.
Even though a picture with poc_msb_reset_flag equal to 1 is lost, the correct POC MSB value can be derived from the following pictures.
POC LSB values will be always correctly signalled.
<number>
LayerId = 0
LayerId = 1
P POC MSB = 0
poc_msb_reset_flag = 1
IDR (or BLA) POC MSB = 0
poc_msb_reset_flag = 1
P POC MSB = 16
poc_msb_reset_flag = 0
P POC MSB = 16
poc_msb_reset_flag = 0
P POC MSB = 0
poc_msb_reset_flag = 1
P POC MSB = 0
poc_msb_reset_flag = 1
P POC MSB = 0
poc_msb_reset_flag = 1
P POC MSB = 0
poc_msb_reset_flag = 1

## Slide 7: Questions on JCTVC-O0275
Why should Ordinary POC and Layer POC be separated?.
  In the proposed text of JCTVC-O0275, can the alignment of the ordinary POC values be ensured? (It seems not)
  If ensured?, why do we need Layer POC?
<number>

## Slide 8: General comments
The feature that POC values is derived within a layer is important.
  For simulcast
  For error robustness
  For hybrid framework (AVC + HEVC)
  For minimizing inter-operations across layers
<number>

## Slide 9
Thank you !
<number>