## Slide 1
3D/MV-HEVC HLS: Study and proposal of methods for extending the supported number of layers (JCT3V-F0071)
Karsten Sühring, Gerhard Tech, Robert Skupin, Yago Sanchez, Thomas Schierl

## Slide 2: Introduction
  In the current draft the number of scalable layers, views and depths is constrained by the range of nuh_layer_id to a total of 64.
  Use cases that require a higher amount of views exist:
    360° camera arrays
    Holographic projection
    Light field camera arrays
    Future ideas
    See also JCT3V-F0099 and JCT3V-F0100

## Slide 3: Examples
3dragon holo table
Stanford camera array

## Slide 4: Commercial products
Holographika 3D display
Lytro lightfield camera

## Slide 5: Introduction
  Mandate of the JCT-3V and the JCT-VC HLS AHGs:
    Study different methods for extending the supported number of layers in 3D- and MV-HEVC.
  In this contribution methods for signalling the extended number of layers and the extended layer id values are discussed and compared.
  The evaluated methods are based on
    methods that have been presented at the 4th and 5th JCT-3V meeting (as e.g. JCT3V-E0092 and JCT3V-D0211)
    or on alternative suggestions made by participants of the last meeting.

## Slide 6: Introduction
In particular following methods are discussed:
    A Layer Id extension for nuh_layer_id values greater than 0.
    B Layer Id extension for a nuh_layer_id value of 63.
    C Layer Id extension for a reserved nuh_layer_id value of 63 plus additional VPS extension

## Slide 7: Communalities between all methods
  A syntax element layer_id_ext_len it is signalled in the VPS indicating whether the layer id extension is used.
  When layer_id_ext_len is greater than 0
     layer id extension is enabled
     layer_id_ext_len indicates the length in bit of a new layer_id_ext syntax element that might be present in the NAL units.
  Instead of nuh_layer_id, a LayerId variable is used to identify layers:
    If layer id extension is disabled  LayerId is equal to nuh_layer_id.
    If layer id extension is enabled  LayerId is derived from the nuh_layer_id and layer_id_ext.

## Slide 8: Overview methods
  Method A
    When nuh_layer_id is greater than 0, layer_id_ext present in NALUs
    And LayerId is derived by
    ( ( nuh_layer_id << layer_id_ext_len ) + layer_id_ext )
  Method B
    When nuh_layer_id is in the range of 0 to 62 the LayerId variable is equal to nuh_layer_id and the layer_id_ext value is not present
    When nuh_layer_id is equal to 63, layer_id_ext present in NALUs
    And LayerId is set equal to ( 63 + layer_id_ext ).

## Slide 9: Overview methods
  Method C
    nuh_layer_id value equal to 63 can be associated with multiple layers as described for method B.
    The VPS extension of the current MV-HEVC draft is not modified,
    Syntax elements needed for layer id extension mechanism are signalled in additional VPS extension.
    Correspond to a scenario, in that an inclusion of the a layer id extension mechanism would be postponed to a later HEVC extension.

## Slide 10: Comparison of methods Additional syntax
syntax structure | Layer Id ext. disabled | A | B | C | Layer Id ext. enabled | A | B | C
VPS | layer_id_ext_len, u(4) | x | x |  | layer_id_ext_len, u(4) | x | x | x
 |  |  |  |  | max_layer_id_ext, u(v) | x | x | x
 | Enabling of additional syntax extension |  |  | x | Enabling of additional syntax extension |  |  | x
 |  |  |  |  | Additional syntax extension, (including layer_id_ext_len and max_layer_id_ext) |  |  | x
SPS, PPS, SEI | layer_id_ext_len, u(4) | x |  |  | layer_id_ext_len, u(4) | x | x | x
 |  |  |  |  | layer_id_ext, u(v) | x | x | x
Slice segment header |  |  |  |  | layer_id_ext, u(v) | x | x | x

## Slide 11: Comparison of methods Syntax design
  Methods A and B
    the range of layer ids is extended in a straight forward way.
    existing loops in the VPS extension over layer dependent syntax elements can also be used for the extension layers (e.g. dimension_id, max_tid_il_ref_pic_plus1, vps_rep_format_idx and direct_dependency_type
     unified clear design.
  Method C
    Needs compatibility to a legacy "Multi-view" profile
    Layer dependent syntax elements have to be signalled in additional VPS extension,
    Syntax elements sharing the same semantics are signalled in different syntax structures.
     distributed and undesired design

## Slide 12: Comparison of methods Bitstream extraction
  Method B and C
    All extension layers are associated with a value of nuh_layer_id of 63
    Based on nuh_layer_id a network device is only able to identify and extract all extension layers at once.
    not possible to select a subset of extension layers based nuh_layer_id.
  Method A
    All nuh_layer_id values >0 can be associated with multiple layers.
    Layers associated with one nuh_layer_id value are a "layer cluster".
    Within a cluster the layers are identified by their layer_id_ext values.
     Extracting different clusters based on nuh_layer_id values possible
Highest flexibility is given by method A.

## Slide 13: Comparison of methods Bitstream extraction
  When the layer id extension mechanism is enabled, additional bits in the slice header are required for layer_id_ext
  In method B and C layer_id_ext indicates an offset to the nuh_layer_id value of 63,
  In method A layer_id_ext indicates the LSB of the LayerId variable.
 Therefore number of bits required for the layer_id_ext syntax element can be chosen significantly lower for method A than for methods B and C.

## Slide 14: Comparison of methods Bits in the slice segment header
  This can be illustrated by the following example assuming a total of 127 layers:
    For method A the maximum number of layers is given by 63 * ( 1 << layer_id_ext_len ) + 1.
     Therefore layer_id_ext_len needs to be at least 1.
    For method B and C the maximum number of layers is given by 63 + ( 1 << layer_id_ext_len ).
    Therefore layer_id_ext_len needs to be at least 6.

## Slide 15: Comparison of methods Overview
 | Method A (layer clustering) | Method B (escape code 63) | Method C (escape code 63 + reserved)
Additional syntax elements in VPS | yes (minimal) | yes (minimal) | yes (at least to enable VPS extension)
Additional extension section in VPS | no | no | yes
Additional syntax elements in SPS/PPS/SEI | yes (minimal) | yes (minimal) | yes (minimal, reserved)
Additional syntax in slice segment header | yes | yes | yes
Number of additional bits in slice header | low | high | high
Clearness of syntax | straight forward | straight forward | duplication of syntax in additional extension (duplicates loops over all layers)

## Slide 16: Comparison of methods Overview
 | Method A (layer clustering) | Method B (escape code 63) | Method C (escape code 63 + reserved)
Additional layers associated with nuh_layer_id | any nuh_layer_id > 0 | 63 | 63
"Legacy" devices have useful extraction information | yes | yes | no
"clustering" of additional layers | yes | no | no
pre-selection of layer clusters based on nuh_layer_id | yes | no | no
Number of usable layers when layer id extension is disabled | full | reduced | reduced

## Slide 17: Conclusion
  Different solutions for signalling an extended number of layers in MV-HEVC and 3D-HEVC have been discussed.
  It has been shown that using reserved values in MV-HEVC and postponing the inclusion of a mechanism to a later profile/extension (method C) leads to an suboptimal complicated solution.
  The inclusion of a simple method (A or B) for extending the number of layers at the current stage avoids duplication of syntax elements in an additional extension structure and provides to a clean unified design.
  Overhead of methods A and B are negligible and a minimum number of additional syntax elements are required.
  Compare to method B methods A enables a more flexible way to extraction clusters based on nuh_layer_id values and requires a lower amount of additional bits in slice segment header.
  It is recommend to adopt solution A to the MV-HEVC specification