## Slide 1: JCT3V-F0082 3D-HEVC HLS: On slice-level camera parameter signaling
Yu-Lin Chang, Yi-Wen Chen, Jian-Liang Lin, Yu-Pao Tsai, Shawmin Lei
Presented by Yu-Lin Chang
6th JCT3V Meeting in Geneva
25 Oct. – 1 Nov., 2013

## Slide 2: Overall Summary
In current 3D-HEVC, conflict between cp_present_flag[ layerId ] and cp_in_slice_segment_header_flag might happen because these two flags are independent
Proposed method 1:
  Signal camera parameters in the slice segment header extension only when both cp_present_flag[ nuh_layer_id ] and cp_in_slice_segment_header_flag are equal to 1.
Proposed method 2:
  Extend cp_in_slice_segment_header_flag to an array of flags, where each array element represents a flag for a layer.
  Send camera parameters of the layer with the layer index equal to layerId in VPS only when cp_present_flag[ layerId ] is equal to 1 and cp_in_slice_segment_header_flag[ layerId ] is equal to 0
Notes:     Problem and proposeVSP off, finding inter-view reference without warping

## Slide 3: Current Camera Parameter Signaling in 3D-HEVC (1/2)
Camera parameter signaling depends on the cp_present_flag for each layer
VPS_header_extension2( ) { | Descriptor
… | 
if ( layerId ! = 0 ) { | 
cp_present_flag[ layerId ] | u(1)
… | 
cp_precision | ue(v)
cp_in_slice_segment_header_flag | u(1)
if( !cp_in_slice_segment_header_flag ) | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
layerId = layer_id_in_nuh[ i ] | 
if( cp_present_flag[ layerId ] ) { | 
viewIdx = ViewOrderIdx[ layerId ] | 
for( j = 0; j < viewIdx; j++ ) { | 
vps_cp_scale[ viewIdx ][ j ] | se(v)
vps_cp_off[ viewIdx ][ j ] | se(v)
vps_cp_inv_scale_plus_scale[ viewIdx ][ j ] | se(v)
vps_cp_inv_off_plus_off[ viewIdx ][ j ] | se(v)
} | 
} | 
} | 

## Slide 4: Current Camera Parameter Signaling in 3D-HEVC (2/2)
In slice segment header extension, camera parameter signaling only depends on cp_in_slice_segment_header_flag
For a certain layer, the camera parameter might not be presented. But if cp_in_slice_segment_header_flag is enabled, the camera parameters are still signaled for each slice
slice_segment_header_extension( ) { | Descriptor
if( cp_in_slice_segment_header_flag ) { | 
for ( i = 0; i < ViewIdx; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 

## Slide 5: Proposed Bug-fix For the Missing Braces
A pair of missing braces is added.
VPS_header_extension2( ) { | Descriptor
… | 
if ( layerId ! = 0 ) { | 
cp_present_flag[ layerId ] | u(1)
… | 
cp_precision | ue(v)
cp_in_slice_segment_header_flag | u(1)
if( !cp_in_slice_segment_header_flag ) | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
layerId = layer_id_in_nuh[ i ] | 
if( cp_present_flag[ layerId ] ) { | 
viewIdx = ViewOrderIdx[ layerId ] | 
for( j = 0; j < viewIdx; j++ ) { | 
vps_cp_scale[ viewIdx ][ j ] | se(v)
vps_cp_off[ viewIdx ][ j ] | se(v)
vps_cp_inv_scale_plus_scale[ viewIdx ][ j ] | se(v)
vps_cp_inv_off_plus_off[ viewIdx ][ j ] | se(v)
} | 
} | 
} | 

## Slide 6: Proposed Method 1 – Check cp_present_flag in Slice Segment Header Extension
Propose to code camera parameters in the slice segment header extension only when both cp_in_slice_segment_header_flag and cp_present_flag[ nuh_layer_id ] are equal to 1
slice_segment_header_extension( ) { | Descriptor
if( cp_in_slice_segment_header_flag && cp_present_flag[ nuh_layer_id ] ) { | 
for ( i = 0; i < ViewIdx; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 

## Slide 7: Proposed Method 2 – Extend cp_in_slice_segment_header_flag to an Array
Propose to extend cp_in_slice_segment_header_flag to an array of flags, where each array element represents a flag for a layer.
In VPS, if cp_present_flag[ layerId ] is equal to 1, cp_in_slice_segment_header_flag[ layerId ] is coded; otherwise, it is not coded and inferred to be 0.
Camera parameters of a layer with a layer index equal to layerId are coded in VPS only when cp_present_flag[ layerId ] is equal to 1 and cp_in_slice_segment_header_flag[ layerId ] is equal to 0
The camera parameters could be signaled more efficiently

## Slide 8: Working Draft Changes for Method 2 (1/3)
Proposed change on VPS
vps_extension2( ) { | Descriptor
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
layerId = layer_id_in_nuh[ i ] | 
if ( layerId ! = 0 ) { | 
cp_present_flag[ layerId ] | 
if ( cp_present_flag[ layerId ] ) | 
cp_in_slice_segment_header_flag[ layerId ] | ue(v)
… | 
cp_precision | ue(v)
cp_in_slice_segment_header_flag | u(1)
if( !cp_in_slice_segment_header_flag ) | 
for( i = 0; i <= vps_max_layers_minus1; i++ ) { | 
layerId = layer_id_in_nuh[ i ] | 
if( cp_present_flag[ layerId ] && !cp_in_slice_segment_header_flag[ layerId ] ) { | 
viewIdx = ViewOrderIdx[ layerId ] | 
for( j = 0; j < viewIdx; j++ ) { | 
vps_cp_scale[ viewIdx ][ j ] | se(v)
vps_cp_off[ viewIdx ][ j ] | se(v)
vps_cp_inv_scale_plus_scale[ viewIdx ][ j ] | se(v)
vps_cp_inv_off_plus_off[ viewIdx ][ j ] | se(v)
} | 
} | 
} | 
iv_mv_scaling_flag | u(1)
} | 
Further cleanup

## Slide 9: Working Draft Changes for Method 2(2/3)
Proposed change on VPS

## Slide 10: Working Draft Changes for Method 2(3/3)
Proposed change on slice segment header extension
slice_segment_header_extension( ) { | Descriptor
if( cp_in_slice_segment_header_flag[ nuh_layer_id ] ) { | 
for ( i = 0; i < ViewIdx; i++ ) { | 
cp_scale[ i ] | se(v)
cp_off[ i ] | se(v)
cp_inv_scale_plus_scale[ i ] | se(v)
cp_inv_off_plus_off[ i ] | se(v)
} | 
} | 
} | 

## Slide 11: Conclusions
One bug-fix for VPS is first provided
Two methods are proposed to solve the conflict of camera parameter signaling between VPS and slice segment header extension.
  Add the checking of cp_present_flag in slice segment header extension
  Extend cp_in_slice_segment_header_flag to an array of flags, where each array element is for a layer, to better support the case when camera parameters of one or more layers are time variant and those of the rest layer(s) are time invariant.
    Send camera parameters of a layer with a layer index equal to layerId in VPS only when cp_present_flag[ layerId ] is equal to 1 and cp_in_slice_segment_header_flag[ layerId ] is equal to 0

## Slide 12: Thanks for your attention!
www.mediatek.com