## Slide 1: JCT3V-F0107 3D-CE3: Results on additional merging candidates for depth coding
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
Background
  In texture coding
    Depth values are used to predict disparity vectors.
    An additional inter-view merging candidates are adopted.
Proposed
  A disparity derived depth (DDD) coding method
  An additional texture merging candidate
Results
  Achieve 0.3% BD-rate saving for the synthesized views

## Slide 3: Background
Samples in the depth component are used to derive disparity vectors for texture coding. (BVSP)
  A disparity vector (DVx, 0) can be derived from its corresponding depth value (dep) by a linear relationship as
  where w and b are two camera parameters
Equ. (1) is implemented in an integer form so w and b can be transmitted from the encoder to the decoder as integers.
Can we use disparity vectors to predict depth values?
(1)

## Slide 4: Background
Two inter-view merging candidates are adopted into the merging candidate list at the first position and the position before TMVP candidate in texture coding
  Inherit motion parameters from the center position and the below-right position
Only one texture merging candidate in depth coding
  Inherit motion parameters from the center position only
  Can we also use the below-right position in depth coding?

## Slide 5: Proposed
  A disparity derived depth (DDD) coding method is proposed.
  A depth value can also be derived from its corresponding disparity vector (DVx, DVy) as
  When the collocated texture block of the current depth block is predicted by disparity-compensated prediction (DCP)
    A DDD candidate will be inserted into the merging candidate list right after the texture candidate.
    In a DDD candidate, all prediction samples in the current block are set as dep calculated by Equ. (2)
    Equ (2) is implemented in an integer form. The division operation, i.e., 1/w, is calculated only once for a picture.
(2)

## Slide 6: Proposed

## Slide 7: Proposed
  Similar to texture coding, an additional texture merging candidate is proposed in depth coding
    Inherits motion parameters from the right bottom position of the collocated PU in the reference texture picture
    The additional texture merging candidate is also inserted into the merging candidate list before TMVP
      pruning with the first merging candidate

## Slide 8: Results
Only the DDD candidate

## Slide 9: Results
Only the additional texture candidate

## Slide 10: Results
The combination of DDD and the additional texture candidate

## Slide 11: Results
The combination with more pruning
  The additional texture merging candidate can be pruned with all previous merging candidates

## Slide 12: Conclusion
Two additional merging candidates are proposed
  A disparity derived depth coding candidate
  An additional texture merging candidate
The combination achieves an average BD-rate saving of 0.3% for the synthesized views
Suggest to be adopted

## Slide 13: Thank you for your attention!