## Slide 1: JCT3V-F0108 3D-CE4: Results on improved advanced residual prediction
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  In ARP, NBDV is not an estimated DV accurate enough
  ARP only handles the MCP case, not the DCP case
Proposed
  JCT3V-E0175: Adaptive disparity vector derivation (ADVD)
  JCT3V-E0185: Advanced temporal residual prediction (ATRP)
Results
  Achieve 0.6% BD-rate saving for the synthesized views

## Slide 3: The problem
In ARP, NBDV as the estimated DV is not accurate enough.
  NBDV is the first encountered DV from a neighbouring block.
  The first encountered may not be the best.
ARP only works when the current reference picture is not an inter-view picture
  The ARP flag is redundant in this case.

## Slide 4: Proposed
  Adaptive disparity vector derivation (ADVD)
    3 DV candidates are derived from neighbouring blocks.
    The encoder can find the best DV candidate in ARP according to RDO criterion and signal the index to the decoder.
  For further improvement, aligned temporal DV (ATDV) is proposed as a new DV candidate
    ATDV is obtained from the aligned block, which is located by a scaled MV to the collocated picture.
    Two collocated pictures are utilized, as in the NBDV derivation.
    ATDV is put into the candidate list first when it is used

## Slide 5: Proposed
ATDV

## Slide 6: Proposed
Advanced temporal residual prediction (ATRP)
  Works when the current reference picture is an inter-view picture
  The current DV is applied to a corresponding block in a temporal reference picture to generate the pseudo residual
  The corresponding block in the temporal reference picture is located by a derived motion vector (DMV).
  DMV is the MV of the block which the current DV is pointing to in the reference view

## Slide 7: Proposed
The combination of ADVD and ATRP
  Three MV candidates are derived for ATRP just like three DV candidates are derived for ARP in ADVD.
  DMV is put into the MV candidate list first if it can be found.
  Then spatial/temporal neighbouring blocks are checked to find more MV candidates.
  An encoder can find the best MV candidate used in ATRP according to RDO criterion, and signal the index to the decoder, similar to what is done in ADVD for ARP.

## Slide 8: Results
ADVD only

## Slide 9: Results
ADVD without ½ weighting
  ½ weighting introduces additional overhead bits.
  But it is not so useful when the estimated DV is accurate enough.

## Slide 10: Results
ATRP only

## Slide 11: Results
ADVD+ ATDV without ½ weighting

## Slide 12: Results
ADVD+ ATDV+ATRP without ½ weighting

## Slide 13: Conclusion
ADVD and ATRP are proposed to improve ARP
0.6% BD-rate saving for the synthesized views
Recommend to be adopted

## Slide 14: Thank you for your attention!