## Slide 1: JCT3V-F0111: CE1.h : Simplified view synthesis prediction
Presented by Yu-Lin Chang
6th JCT3V Meeting in Geneva
25 Oct. – 1 Nov., 2013
Yi-Wen Chen, Jian-Liang Lin, Na Zhang, Jicheng An, Shawmin Lei

## Slide 2: Overall Summary
Two simplifications for view synthesis prediction (VSP) are proposed
  Unify the depth data accessed by DoNBDV and VSP
    No overall BD-rate change
    The bandwidth of accessing depth data is reduced by 50%
  Remove the line buffer for NBDV and VSP flag
    No overall BD-rate change
    Line buffers (~9Kbits) for NBDV and VSP flag are removed

## Slide 3: Depth Data Accessed by DoNBDV and VSP
  In HTM-8.0
VSP
DoNBDV
The inherited DV may locate different depth blocks

## Slide 4: Proposed Unification of the Depth Data Accessed by DoNBDV and VSP
  The inherited VSP mode also uses the derived NBDV of the current CU to fetch a depth block in the reference view
  The worst case memory access bandwidth for accessing depth data is reduced by 50%

## Slide 5: Simulation Results
Anchor : HTM-8.0
  Test : HTM-8.0 + Using NBDV derived for current CU for the inherited VSP block

## Slide 6: Remove the Line Buffer for NBDV and VSP Flag
Disallow inheritance of the VSP modes from neighbors belonging to the upper coding tree unit (CTU) row.
The VSP coded blocks at upper CTU row are viewed as normal DCP blocks
The line buffer for NBDV and VSP flag (~ 9K Bits) could be removed

## Slide 7: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 + disallowing inheriting VSP mode from upper CTU row

## Slide 8: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with the both simplifications

## Slide 9: Conclusion
Unify the depth data accessed by DoNBDV and VSP
  No overall BD-rate change
  The overhead of accessing depth data is reduced by 50%
  Depth data accessed by DoNBDV and VSP are unified
Remove line buffer for NBDV and VSP mode flag
  No overall BD-rate change
  Line buffer (9K bits) for NBDV and VSP mode flag are removed

## Slide 10: Thank you for your attention!