## Slide 1: JCT3V-F0112: 3D-CE4 related: On complexity reduction of bi-prediction for advanced residual prediction
Yi-Wen Chen, Jian-Liang Lin, Yu-Wen Huang, Shawmin Lei
Presented by Yu-Lin Chang
6th JCT3V Meeting in Geneva
25 Oct. – 1 Nov., 2013

## Slide 2: Overall Summary
Bi-prediction of identical motion
  HTM-8.0 changes bi-prediction to uni-prediction
  Generated bitstreams may not conform to the 3D-HEVC text when ARP is enabled due to unequal operations between uni-prediction and bi-prediction
  The same issue has been resolved in Illumination Compensation
Propose to align the operations between uni-prediction and bi-prediction when ARP is enabled
  Introduce no overall BD-rate increase
  Allowing decoder change Bi-prediction with identical motion to uni-prediction could save 5% decoding time

## Slide 3: Issues of ARP with Identical Motion Checking
Issue 1: Unequal clipping operations are applied to uni-prediction and bi-prediction of a ARP enabled PU
Issue 2: Different predicting residual signal for List0 and List1 when List0/List1 motion are identical
  L0: select the base-view reference picture with ref. idx =0 in List0
  L1: select the base-view reference picture with ref. idx =0 in List1
L0MV ≠ L1MV
L0MV = L1MV

## Slide 4: Proposed Solution for The Issue 1
Unify the clipping operations for uni-prediction and bi-prediction
Always applying clipping after the predicting residual signal is added to the MCP signal no mater current PU is uni-prediction or bi-prediction
No overall BD-rate increase

## Slide 5: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with equal clippings for uni- and bi- prediction when ARP is enabled

## Slide 6: Proposed Solution for The Issue 2
Modify the selection of base-view reference picture
  Original : L0: select the base-view reference picture with ref. idx =0 in List0
  L1: select the base-view reference picture with ref. idx =0 in List1
  Modify : Among the two base view reference pictures in the original scheme,
  L0: select the one which is closer to the L0 reference picture of
  current CU in terms of POC distance
  L1: select the one which is closer to the L1 reference picture of
  current CU in terms of POC distance
No coding loss

## Slide 7: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with modified ref. picture selection

## Slide 8: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with equal clipping operations and modified ref. picture selection
  Results crosschecked and confirmed in JCT3V-F0209

## Slide 9: Additional Results
Anchor : HTM-8.0 with the proposed fix without identical motion checking
Test : HTM-8.0 with the proposed fix with identical motion checking

## Slide 10: Conclusions
Align the operations between uni-prediction and bi-prediction for ARP
  Unify the clipping operations
  Modify the selection of base-view reference picture
Negligible coding loss while the unnecessary bi-prediction could be avoided when ARP is enabled
The decoder which enables the non-normative fast bi-prediction could save 5% decoding time

## Slide 11: Thank you for your attention!