## Slide 1: 3D-CE5 related: Bin reduction for SDC residual coding
Yi-Wen Chen, Jian-Liang Lin, Yu-Wen Huang, Shawmin Lei
Presented by Jian-Liang Lin
6th JCT3V Meeting in Geneva
25 Oct. – 1 Nov., 2013

## Slide 2: Overall Summary
Binary codeword for the SDC residual magnitude could be very long (e.g. around 200 bins for the worst case)
  Increase the latency for CABAC processing
  Increase the overhead for hardware design
Proposed to constrain the residual magnitude of intra SDC within a predefined range
  Introduce no overall BD-rate increase
  The number of the context coded bins is significantly reduced

## Slide 3: Residual Coding for SDC in HTM-8.0
Intra SDC-coded depth block is intra predicted by Planar prediction (1 segment) or DMM (2 segments)
A residual value is signaled for each segment
The binary codeword for the residual magnitude could be very long
  The codeword when the number of depth values in DLT is 256:

## Slide 4: Proposed Solution
Constrain the residual magnitude for intra SDC mode within a range N (N is an non-negative integer)
The codeword (TU) for the residual magnitude (N=5)
When N=1, only use the sign flag to indicate “+1” or “-1”
When N=0, the intra SDC mode is intra Skipped

## Slide 5: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with proposed constraint (N=5)
  Under CTC
  Almost no change to the coding results (0.0%)

## Slide 6: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with proposed constraint (N=1)
  Under CTC
  Almost no change to the coding results (0.0%)

## Slide 7: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with proposed constraint (N=0)
  Under CTC
  0.2% coding performance drop

## Slide 8: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with proposed constraint (N=5)
  Under All-Intra
  Almost no change to the coding results (0.0%)

## Slide 9: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with proposed constraint (N=1)
  Under All-Intra
  0.1% coding performance drop

## Slide 10: Simulation Results
Anchor : HTM-8.0
Test : HTM-8.0 with proposed constraint (N=0)
  Under All-Intra
  0.4% coding performance drop

## Slide 11: Conclusions
Propose to constrain the SDC residual magnitude within a range N
Truncated unary (TU) is used to generate the codeword
  The context coded bins are reduced from 200 to N-1
  Negligible coding losses are observed for N = 1 and 5
  0.2% (CTC) and 0.4% (AI) coding losses are observed for N = 0
Recommend to adopt the proposed simplification into 3D-HEVC

## Slide 12: Thank you for your attention!

## Slide 13: Backup