## Slide 1: 3D-CE2.h related: Problem fix of the DV derivation in 3D-HEVC
Yi-Wen Chen, Jian-Liang Lin, Yu-Wen Huang, Shawmin Lei
Presented by Jian-Liang Lin
6th JCT3V Meeting in Geneva
25 Oct. – 1 Nov., 2013

## Slide 2: Problem Statement
In current text, a default DV with zero vector pointing to the base view (with a view index equal to 0) is used as a default output for NBDV when no DV could be derived from the neighbor blocks
However, in the IBP test conditions, there are cases that the base view reference picture is not included in the reference picture list of current slice
  Result in encoder/decoder mismatch or crash

## Slide 3: A Fix to The Problem
A fix to this issue has been integrated into HTM-8.0 during the software migration from HTM-7.0 to HTM-8.0
The fix is to use a zero vector pointing to the inter-view reference picture with the smallest view index instead of with a view index equal to 0 as a default output for NBDV
  Encoder/decoder mismatch without this fix
  No impact on CTC
In this proposal, the text of this fix is provided to align with the software

## Slide 4: The Text
The modifications are highlighted in green color

## Slide 5: Thank you for your attention!

## Slide 6: Backup