## Slide 1: 3D-CE2 related: Simplification on NBDV derivation in 3D-HEVC
Jian-Liang Lin, Yi-Wen Chen, Yu-Wen Huang, Shawmin Lei
JCT3V-F0116
Presented by Jian-Liang Lin
6th JCT-3V Meeting in Geneva
25 Oct. – 1 Nov. 2013

## Slide 2: Overall Summary
In the neighboring block disparity vector (NBDV) derivation, it needs to access the left and above spatial neighboring blocks and the collocated blocks to find an available disparity vector.
In order to reduce the complexity, it is proposed to remove the above block in the NBDV derivation process.
The experimental results reportedly show no coding efficiency loss.

## Slide 3: Introduction
In 3D-HEVC, the NBDV derivation process needs to access two spatial neighboring blocks, and collocated blocks to find an available DV:
  Search collocated block: Ctr
  Search spatial block: A1 and B1
  Search DV-MCP block: A1 and B1
    Check whether B1 is located in current CTU. If B1 is located in the above CTU, it is considered as not available.
 |  |  |  | B1
A1 |  |  |  | 
 |  | Ctr |  | 
Current block
Collocated block

## Slide 4: Proposed Simplification
In order to further reduce the complexity of the NBDV, it is propose to remove the above neighboring block
The simplified NBDV derivation process:
  Search collocated block: Ctr
  Search spatial block: A1 and B1
  Search DV-MCP block: A1 and B1
    Check whether B1 is located in current CTU. If B1 is located in the above CTU, it is considered as not available.
 |  |  |  | B1
A1 |  |  |  | 
 |  | Ctr |  | 
Current block
Collocated block

## Slide 5: Experiment Results – Test 1
Anchor : HTM-8.0 under CTC
Test1: Remove the above neighboring block
No BD-rate increase
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.1% | 0.3% | 0.1% | 0.1% | 0.1% | 98.4% | 97.0% | 97.8%
Kendo | 0.0% | 0.1% | -0.2% | 0.0% | 0.0% | 0.0% | 99.8% | 101.2% | 100.2%
Newspaper_CC | 0.0% | 0.2% | 0.2% | 0.1% | 0.1% | 0.1% | 99.1% | 100.7% | 99.4%
GT_Fly | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 97.2% | 101.9%
Poznan_Hall2 | 0.0% | 0.2% | -0.2% | 0.0% | 0.0% | -0.1% | 99.0% | 100.0% | 104.2%
Poznan_Street | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 99.9% | 100.4% | 102.7%
Undo_Dancer | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 98.9% | 98.9% | 95.6%
1024x768 | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% | 99.1% | 99.6% | 99.1%
1920x1088 | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.4% | 99.1% | 101.1%
average | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.3% | 99.3% | 100.2%
Shark | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 99.5% | 96.5% | 101.6%

## Slide 6: Experiment Results – Test 2
Anchor : HTM-8.0 under CTC
Test2: Test1 + replace default zero DV with the DV converted from middle depth value (128)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 101.4% | 102.7% | 102.3%
Kendo | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 101.8% | 95.5% | 96.2%
Newspaper_CC | 0.0% | -0.2% | -0.1% | -0.1% | 0.0% | -0.1% | 101.6% | 107.4% | 103.6%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 102.2% | 107.5% | 101.0%
Poznan_Hall2 | 0.0% | 0.4% | -0.2% | 0.0% | 0.0% | 0.0% | 99.4% | 95.2% | 99.5%
Poznan_Street | 0.0% | 0.2% | 0.1% | 0.0% | 0.0% | 0.0% | 99.7% | 99.6% | 104.3%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 95.1% | 101.7%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.6% | 101.9% | 100.7%
1920x1088 | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.4% | 99.3% | 101.6%
average | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.9% | 100.4% | 101.2%
Shark | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 100.1% | 101.1% | 100.2%

## Slide 7: Conclusions
It is proposed to further simply the NBDV derivation process by removing the above neighboring block.
The experimental results show this simplification brings no coding loss while the complexity of NBDV could be reduced.

## Slide 8: Thanks for your attention!
www.mediatek.com