## Slide 1
3D-CE5.h Fast depth lookup table application method
to intra modes for Depth data
(JCT3V-F0159)
Oct. 2013
LG Electronics
Jin Heo (jin78.heo@lge.com)
Jie Jia (jie.jia@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Introduction
JCT3V-E0157
  Apply DLT to all intra modes of depth map
  Performance
    CTC: 0.3% coding gain, enc/dec time: 96.6%/98.8%
    AI: 0.5% coding gain, enc/dec time: 149.9%/103.7%
  Increment of encoding time
Proposed method
  Fast DLT application method to all intra modes of depth map
Crosscheck
  F0207 (by Samsung)

## Slide 3: JCT3V-E0157
Basic idea
  Generate residual as the difference of DLT index of original and prediction pixel value
Encoder
  Check two different residues
    Residue by the original method: Resi[x] = org[x] – pred[x]
    Residue by the proposed method: Resi[x] = DLT[org[x]] – DLT[pred[x]]
  All intra modes excluding SDC are tested twice

## Slide 4: Proposed Method
Method I: applying DLT to 2Nx2N block size
  Apply DLT to all intra modes of depth map only in 2Nx2N block size
Method II: Method I + reduction of the number of candidate modes
  Simplified RDO: select 8 modes among 35 modes
  Proposed method: select 4 modes among 35 modes in simplified RDO
Method III: applying DLT to particular modes
  Replace original residual generation method with applying DLT method in particular intra modes; DMM, RBC, DC, vertical, and horizontal
    Without interpolation process
  Advantage
    Unnecessariness of a flag bit
    Less complexity compared to Method I and Method II

## Slide 5: Method I: applying DLT to 2Nx2N block size
CTC
AI
Notes: <number>

## Slide 6: Method II: Method I + reduction of the number of candidates
CTC
AI

## Slide 7: Method III: applying DLT to particular modes
CTC
AI

## Slide 8: Conclusion
Proposed method
  Fast DLT application to all intra modes excluding SDC modes
Performance
  Method I
    CTC: -0.1% gain, Encoding time: 102.9%
    AI: -0.3% gain, Encoding time: 110.2%
  Method II
    CTC: -0.1% gain, Encoding time: 101.0%
    AI: -0.2% gain, Encoding time: 107.1%
  Method III
    CTC: -0.1% gain, Encoding time: 100.4%
    AI: -0.2% gain, Encoding time: 100.5%