## Slide 1
Non-CE: Illumination compensation flag coding
(JCT3V-F0160)
Oct. 2013
LG Electronics
Jin Heo (jin78.heo@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Introduction
Proposed method
  Select the proper context model among several context models adaptively
Performance
  0.2% coding gain under CTC
Crosscheck
  JCT3V-F0208 (by Samsung)

## Slide 3: Proposed Method
Context modeling
  Use three context models for IC flag coding
  Select the IC context model from the presence of the IC flag of the neighboring blocks
Initial value setting
Current
block
B1
A1
ctxIdx = (ic_flag(A1) != 0) ? 1 : 0 + (ic_flag(B1) != 0) ? 1 : 0
Initialization variable | ctxIdx of ic_flag | 
initValue | 0 | 1
 | 197 | 197
Initialization variable | ctxIdx of ic_flag |  |  |  |  | 
initValue | 0 | 1 | 2 | 3 | 4 | 5
 | 154 | 154 | 154 | 154 | 154 | 154

## Slide 4: Experimental Results
CTC

## Slide 5: Conclusion
Proposed method
  Use an adaptive context model selection method for illumination compensation
  Change the initial value of each context model
Performance
    0.2% coding gain under CTC