## Slide 1
CE4 related: Coding of weighting factor of
advanced residual prediction
(JCT3V-F0161)
Oct. 2013
LG Electronics
Jin Heo (jin78.heo@lge.com)
Sunmi Yoo (sunmi.yoo@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Introduction
Proposed method
  Modify initial value of CABAC context model of ARP weighting factors
Performance
  0.3% coding gain under CTC
Crosscheck
  JCT3V-F0206 (by Samsung)

## Slide 3: Proposed Method
Syntax elements of ARP
  iv_res_pred_flag: indicate whether inter-view residual prediction is used
    Use three contexts decided by the presence of the iv_res_pred_flag in the above and the left CU
    ctxIdx: 0~2
  iv_res_pred_weight_idx: specify the index of the weighting factor
    Use one context
    ctxIdx: 3
Initialization variable | ctxIdx of iv_res_pred_weight_idx |  |  |  |  |  |  | 
initValue | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 154 | 154 | 154 | 154 | 154 | 154 | 154 | 154
Initialization variable | ctxIdx of iv_res_pred_weight_idx |  |  |  |  |  |  | 
initValue | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 162 | 153 | 154 | 162 | 162 | 153 | 154 | 162

## Slide 4: Experimental Results
CTC

## Slide 5: Conclusion
Proposed method
  Change initial value of CABAC context model of ARP weighting factors
Performance
  0.3% coding gain under common test condition