## Slide 1
CE2 related: Derivation of motion-aware temporal disparity vector (JCT3V-F0163)
October 2013
LG Electronics
Junghak Nam (junghak.nam@lge.com)
Sehoon Yea (sehoon.yea@lge.com)

## Slide 2: Summary
Derivation of motion-aware temporal disparity vector
Proposed method
  The position of corresponding block in temporal picture is derived by spatial neighboring block motion vector
Experimental results
  0.1% coding gain on synthesized view
Crosscheck
  JCT3V-F0200 (by Samsung)
<number>

## Slide 3: Problem statements
In current 3D-HEVC, corresponding block of temporal disparity vector derivation is always co-located block (C’)
  There is no consideration of whether current block has any motion
<number>
L
A
C
C’
Base view
DVc’
Dependent view
t
t-1

## Slide 4: Proposed method
A disparity (DVc") is derived from motion-aware corresponding block (C") which is shifted by a motion vector of neighboring left or above blocks.
<number>
L
A
C
C’
Base view
DVc’
DVc”
L”
C”
Dependent view
t
t-1
MVL

## Slide 5: Experimental results
<number>
<The proposed method vs. HTM 8.0 on CTC>

## Slide 6: Conclusion
Derivation of motion-aware temporal disparity vector are proposed
0.1% coding gain for synthesized views
It is recommended to adopt proposed method into 3D-HEVC
<number>