## Slide 1
www.hisilicon.com
The Right silicon for your next BIG idea
3D-CE3.h related: On Split Flag Prediction
Huanbang Chen1, Jianhua Zheng2, Fan Liang1
JCT3V-F0174
Sun Yat-sen University1, HiSilicon Technologies2

## Slide 2: Summary of the contribution
The proposal introduces a modified CU splitting strategy in both encoder and decoder for split_cu_flag prediction, to reduce the split flag signalling for dependent texture views.
Implemented based on HTM8.0, results under CTC,
- 0.36% , 0.36% gain for texture views (video1 and video2),
- 0.28% gain for overall video, and 0.15% gains for synthesized views
Thanks MediaTek for crosscheck (JCT3V-F0228)

## Slide 3: Proposed method
  Split flag prediction
  The following conditions are applied in both encoder and decoder.
  - Condition 2.2.1: All the five inter-view neighbouring blocks (the corresponding block of the current CU and the four direct adjacent blocks of the corresponding block) in the reference view are coded as merge modes.
  - Condition 2.2.2: The CU splitting depth of the current CU is equal to or larger than the maximum depth of the CU splitting depths of the five inter-view neighboring blocks.

## Slide 4: Proposed method
  Split flag signaling and Parsing
-Encoder: if both conditions 2.2.1 and 2.2.2 are true, no further CU splitting is need for the current CU, hence split_cu_flag is not signaled in bitstream, else split_cu_flag is still be signaled in bitstream.
-Decoder: examine the same conditions 2.2.1 and 2.2.2. If both conditions 2.2.1 and 2.2.2 are true, it is decided no further CU splitting for the current CU.

## Slide 5: Experimental results
Page 5
  Implemented based on HTM8.0
Results of prediction of split flag under CTC condition
No Change under All Intra condition

## Slide 6: Spec. Changes

## Slide 7: Conclusions
Proposes a simple CU splitting strategy in both encoder and decoder for split_cu_flag prediction, to reduce the split flag signalling for dependent texture views.
Achieves 0.36% gain for texture views, 0.28% gain for overall video, and 0.15% for synthesized views.
Suggest to adopt the proposal in HTM9.

## Slide 8
Thank you!
www.hisilicon.com