## Slide 1: MV-HEVC/SHVC HLS: Syntax clean-up of profile, tier, and level information (JCTVC-P0048, JCT3V-G0045)
JCT-VC 16th Meeting: San José, US, 9–17 Jan. 2014
JCT-3V 7th Meeting: San José, US, 11–17 Jan. 2014
Takeshi Tsukuba, Tomoyuki Yamamoto, Tomohiro Ikai
SHARP Corporation

## Slide 2: Summary
Motivation
  “profile_ref_minus1[i]” is used to select profile/tier/level info. to be referred
  It constantly uses 6 bits, but it introduces redundant flexibility
  Proposal
    Remove profile_ref_minus1
    When profile info is not present, it’s inferred from the previous one
  Benefits
    Clean-up profile/tier/level syntax without losing any functionality
    Reduce bit amount of profile_ref_minus1[i]
      It is recommended to adopt the proposal to next SHVC/MV-HEVC.
Notes:   Avoid the improper removal of sharing parameter set in bitstream extraction.
  Enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
  Enhance SPS sharing capability for Extended Spatial Scalability.

## Slide 3: Profile / tier / level signalling (current WD)
Profile/Tier/Level syntax structure
pRef=#2 (signalled)
#1
#2
#3
#4
#5
#6
A
B
C
B
C
F
C
pRef=#1 (signalled)
Layer Set A
Layer Set B
Layer Set C
#0
profile_level_tier_idx
pRef=#2 (signalled)
profile = A

## Slide 4: Profile / tier / level signalling (proposed)
Profile/Tier/Level syntax structure
#1
#2
#3
#4
#5
#6
A
B
B
C
C
C
F
pRef = #1 (inferred)
Layer Set A
Layer Set B
Layer Set C
#0
profile_level_tier_idx
pRef = #3 (inferred)
pRef = #4 (inferred)

## Slide 5: Text changes on proposal
vps_extension( ) { | Descriptor
…snipped… | 
vps_number_layer_sets_minus1 | u(10)
vps_num_profile_tier_level_minus1 | u(6)
for( i = 1; i <= vps_num_profile_tier_level_minus1; i ++ ) { | 
vps_profile_present_flag[ i ] | u(1)
if( !vps_profile_present_flag[ i ] ) | 
profile_ref_minus1[ i ] | u(6)
profile_tier_level( vps_profile_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
} | 
…snipped… | 
} | 
Note : The text is based on the attached one of the SHVC WD bug ticket #9.
https://hevc.hhi.fraunhofer.de/trac/shvc/attachment/ticket/9/JCTVC-O1008_v3_suggested_editorial_fix_r1.docx
Notes: The proposal adds the following restriction.
F.7.4.2.4 Order of VPS, SPS and PPS RBSPs and their activation
It is a requirement of bitstream conformance that, when an SPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.
It is a requirement of bitstream conformance that, when a PPS with nuh_layer_id equal to nuhLayerIdA is active for a layer with nuh_layer_id equal to nuhLayerIdB, the layer with nuh_layer_id equal to nuhLayerIdA shall be a direct or indirect reference layer of the layer with nuh_layer_id equal to nuhLayerIdB.

## Slide 6: (Info) SHVC WD bug ticked #9
Regarding Profile, tier and level semantics in subclause F.7.4.4, there exist several editorial bugs as follows: 1) Expression of inferring rule for profile_tier_level() syntax structure in VPS extension is incorrect. 2) syntax name "profile_layer_set_ref_minus1" should be "profile_ref_minus1". 3) Variable "lsIdx" should not be used for referring elements of "profile_ref_minus1[]".

## Slide 7
Thank you!