## Slide 1: 3D-HEVC HLS: On ARP reference picture signaling
Jian-Liang Lin, Yi-Wen Chen, Yu-Wen Huang, Shawmin Lei
Presented by Jian-Liang Lin
7th JCT3V Meeting in San Jose
11–17 Jan. 2014

## Slide 2: Overall Summary
To ease the burden of memory access, in current ARP, only the first temporal ref. picture is allowed to be used to generate predicting residual.
However, ref. picture reorder of the slices within a picture may still cause the first temporal ref. picture to change
  Frequent changing the ref. picture breaks the pipeline design
  Cause a burden for decoders due to the DRAM access limitations
Propose to prohibit changes to the ref. picture for ARP within a picture
An additional benefit of more flexibility in the reference picture selection for ARP is also provided

## Slide 3: Illustration of ARP
ARP needs to access the reference picture of the reference view.
The first temporal reference picture of each reference list.

## Slide 4: ARP in HTM-9.0
Ref. list reordering between slices in a same picture could cause the first temporal reference picture to change.
However, ref. picture reorder of the slices within a picture may still cause the first temporal ref. picture to change
  Frequent changing the ref. picture breaks the pipeline design
  Cause a burden for decoders due to the DRAM access limitations

## Slide 5: Solutions
Propose to prohibit changes to the ref. picture for ARP within a picture
An additional benefit of more flexibility in the reference picture selection for ARP is also provided

## Slide 6: Proposed Solution 1
Add one new syntax element to the slice header
  The new syntax element simply gives the reference picture index for ARP
  The new syntax element is semantically restricted to always point to a same reference picture for all slices within a picture
For CTC, only 1 bit is needed to code the first temporal reference picture, and therefore having negligible impact on the coding efficiency.
Moreover, this syntax could also provide the flexible of reference picture selection for ARP

## Slide 7: The modified Syntax for the Proposed Solution 1

## Slide 8: Proposed Solution 2
The reference picture for ARP is derived at the encoder and decoder through an identical derivation process.
Instead of selecting the first temporal reference picture, it is proposed to select the reference picture closest to current coding picture (has smallest POC distance) as the reference picture for ARP.
With this simply modification, all slices within a picture will have a same reference picture for ARP and will not be affected by the reference picture reordering.

## Slide 9: Simulation Results Under CTC
Anchor : HTM-9.0r1
Test : HTM-9.0r1 with the proposed solution2

## Slide 10: Conclusions
In current 3D-HEVC, the reference picture for ARP may change within a picture due to the ref. picture reordering
Two solutions are proposed to prohibit changes to the reference picture for ARP within a picture.
Solution 1 could solve the issue by sending new syntax
  Provide the flexible of reference picture selection for ARP
Solution 2 could solve the issue by deriving the ref. picture for ARP using the modified procedure

## Slide 11: Thank you for your attention!

## Slide 12: Backup

## Slide 13: The modified Syntax for the Proposed Solution 2