## Slide 1: 3D-CE1 related: VSP combining inter-view ARP
Yi-Wen Chen, Jian-Liang Lin, Yu-Wen Huang, Shawmin Lei
Presented by Jian-Liang Lin
7th JCT3V Meeting in San Jose
11–17 Jan. 2014

## Slide 2: Overall Summary
In current 3D-HEVC, the combination of VSP and ARP is not allowed.
  VSP merging candidates will not be inserted into the merge candidate list for a PU with ARP enabled
Since Inter-view residual prediction was adopted, the combination of VSP and ARP becomes possible.
Propose to enable the combination of VSP and ARP
  1.3%, 1.1% and 0.3% BD-rate reduction to sequence “UndoDancer” for video 1, video2 and overall results
  Overall 0.1% BD-rate reduction
  No increase to the worst case memory bandwidth

## Slide 3: Proposed VSP combining inter-view ARP
VSP merging candidates could still be inserted into the merge candidate list for an ARP enabled PU
VSP performs inter-view residual prediction on a sub-block basis
No increase to the worst
case memory bandwidth

## Slide 4: Simulation Results
Anchor : HTM-9.0r1
Test : HTM-9.0r1 with VSP combining inter-view ARP

## Slide 5: Conclusions
Propose to enable the inter-view ARP on VSP
Bring 0.1% overall BD-rate reduction
Bring 1.3%, 1.1% and 0.3% BD-rate reduction on “UndoDancer” for video1, video2 and synthesis results
No increase to the worst case memory access bandwidth

## Slide 6: Thank you for your attention!

## Slide 7: The Modified Syntax (1)
Remove the constraint that VSP candidate is not allowed to be added into the merge candidate list when ARP is enabled

## Slide 8: The Modified Syntax (2)
VSP with inter-view ARP