## Slide 1: 3D-AHG8: Simplification on CABAC contexts for IC and ARP Flags
Yi-Wen Chen, Kai Zhang, Jicheng An, Jian-Liang Lin, Xianguo Zhang, Shawmin Lei
Presented by Jian-Liang Lin
7th JCT3V Meeting in San Jose
11–17 Jan. 2014

## Slide 2: Overall Summary
In the current 3D-HEVC, two neighboring blocks are accessed to select one of the three CABAC context models for ic_flag and iv_res_pred_weight_idx.
Propose to simplify the CABAC for ic_flag and iv_res_pred_weight_idx
For ic_flag, the context number is reduced from 3 to 1 without coding loss
For iv_res_pred_weight_idx, the context number is reduced from 3 to 2 without coding loss
The line buffers for for ic_flag and iv_res_pred_weight_idx could also be removed

## Slide 3: CABAC for ic_flag and iv_res_pred_weight_idx
In current 3D-HEVC, for both ic_flag and iv_res_pred_weight_idx, two neighboring blocks are accessed to select one of the 3 context models
Line buffers for ic_flag and iv_res_pred_weight_idx of upper CTU row are required

## Slide 4: Simplified CABAC for ic_flag
Only one context is used for the CABAC of ic_flag without referring any information from neighboring blocks
The number of context is reduced from 3 to 1
The line buffer for ic_flag of upper CTU row could be removed
X
X

## Slide 5: Simulation Results
Anchor : HTM-9.0r1
Test : HTM-9.0r1 with simplified CABAC for ic_flag

## Slide 6: Simplified CABAC for iv_res_pred_weight_idx
Only the left neighboring block A are accessed to derive the CABAC context models
The number of context is reduced from 3 to 2
The line buffer for iv_res_pred_weight_idx of upper CTU row could be removed
X

## Slide 7: Simulation Results
Anchor : HTM-9.0r1
Test : HTM-9.0r1 with simplified CABAC for iv_res_pred_weight_idx

## Slide 8: Conclusions
Propose to simplify the context model derivation for the CABAC of ic_flag and iv_res_pred_weight_idx
Remove 3 context models as well as remove the line buffers without causing coding efficiency loss for the synthesized views

## Slide 9: Thank you for your attention!