## Slide 1: JCT3V-G0062 3D-AHG8 related: A simplified method on DMM mode coding
Kai Zhang, Yi-Wen Chen, Jicheng An, Xianguo Zhang, Jian-Liang Lin, Shawmin Lei2

## Slide 2: Overall Summary
The Problem
  The table index in DMM1 is binarizied as a fixed-length code.
    All bins in the code share one context model.
    These bins can hardly obey the same distribution.
Proposed
  Code these bins in the by-pass way
  One context models can be removed.
Results
  Cause no BD-rate loss in the common test condition

## Slide 3: The problem
The table index in DMM1 is binarizied as a fixed-length code, all bins in which share one context model.
  It may be inefficient to code them according to a single context model since these bins can hardly obey the same distribution.

## Slide 4: Proposed
  Code bins of the table index in DMM1 in the by-pass way.
  One context model can be removed
  The simplification does not cause a BD-rate loss under CTC
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | 0.02% | -0.14% | -0.03% | -0.05% | -0.03% | 99.6% | 86.0% | 102.6%
Kendo | 0.00% | -0.05% | -0.11% | -0.03% | 0.01% | -0.05% | 98.8% | 104.4% | 100.8%
Newspaper_CC | 0.00% | -0.18% | 0.00% | -0.02% | -0.05% | -0.05% | 97.9% | 106.8% | 101.0%
GT_Fly | 0.00% | 0.06% | 0.06% | 0.00% | 0.01% | -0.06% | 98.4% | 93.2% | 99.2%
Poznan_Hall2 | 0.00% | 0.36% | -0.21% | 0.02% | 0.02% | 0.12% | 99.3% | 107.4% | 97.4%
Poznan_Street | 0.00% | -0.03% | -0.01% | 0.00% | 0.01% | 0.00% | 99.2% | 106.1% | 96.9%
Undo_Dancer | 0.00% | -0.03% | 0.00% | 0.00% | 0.01% | -0.07% | 98.6% | 86.8% | 96.4%
Shark | 0.00% | 0.07% | -0.10% | -0.01% | -0.02% | 0.04% | 97.1% | 88.0% | 98.0%
1024x768 | 0.00% | -0.07% | -0.09% | -0.03% | -0.03% | -0.04% | 98.8% | 99.1% | 101.5%
1920x1088 | 0.00% | 0.08% | -0.05% | 0.00% | 0.00% | 0.00% | 98.5% | 96.3% | 97.6%
average | 0.00% | 0.03% | -0.07% | -0.01% | -0.01% | -0.01% | 98.6% | 97.3% | 99.0%

## Slide 5: Conclusion
One context models is removed with no loss
Suggest to be adopted

## Slide 6: Thank you for your attention!