## Slide 1: JCT3V-G0063 3D-CE2: Results on additional merging candidates for depth coding
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
Background
  In texture coding
    Depth values are used to predict disparity vectors.
    An additional inter-view merging candidates are adopted.
Proposed
  A disparity derived depth (DDD) coding method
  An additional texture merging candidate
Results
  Achieve 0.3% BD-rate saving for the synthesized views

## Slide 3: Background
Samples in the depth component are used to derive disparity vectors for texture coding. (BVSP)
  A disparity vector (DVx, 0) can be derived from its corresponding depth value (dep) by a linear relationship as
  where w and b are two camera parameters
Equ. (1) is implemented in an integer form so w and b can be transmitted from the encoder to the decoder as integers.
Can we use disparity vectors to predict depth values?
(1)

## Slide 4: Proposed
  A disparity derived depth (DDD) coding method is proposed.
  A depth value can also be derived from its corresponding disparity vector (DVx, DVy)
    dep can be calculated with operations of integer multiplication and shift approximately.
    No division operations.
  When the collocated texture block employs DCP
    A DDD candidate will be inserted into the merging candidate list right after the texture candidate.
    In a DDD candidate, all prediction samples in the current block are set to the approximated dep

## Slide 5: Proposed

## Slide 6: Proposed
  Similar to texture coding, an additional texture merging candidate is proposed in depth coding
    Inherits motion parameters from the right bottom position of the collocated PU in the reference texture picture
    The additional texture merging candidate is also inserted into the merging candidate list before TMVP
      pruning with the first merging candidate

## Slide 7: Results
Only the DDD candidate
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.1% | 89.0% | 98.1%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.3% | 102.3% | 99.3%
Newspaper_CC | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 97.6% | 106.1% | 100.2%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.8% | 100.4% | 89.9% | 98.7%
Poznan_Hall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 100.1% | 102.4% | 98.0%
Poznan_Street | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.2% | 101.7% | 94.5%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 100.3% | 89.4% | 96.8%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.4% | 98.0% | 97.4% | 99.8%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 98.7% | 99.1% | 99.2%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | 99.6% | 96.1% | 97.6%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | 99.3% | 97.3% | 98.2%

## Slide 8: Results
Only the additional texture candidate
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 98.7% | 94.6% | 99.8%
Kendo | 0.0% | -0.2% | -0.1% | 0.0% | 0.0% | -0.1% | 100.6% | 93.6% | 100.8%
Newspaper_CC | 0.0% | -0.1% | 0.1% | 0.0% | -0.1% | -0.1% | 98.5% | 106.5% | 101.3%
GT_Fly | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 99.7% | 99.5% | 99.4%
Poznan_Hall2 | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 100.8% | 101.9% | 98.0%
Poznan_Street | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.1% | 100.5% | 109.1% | 99.6%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 101.0% | 92.7% | 101.1%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 98.1% | 99.3% | 101.9%
1024x768 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 99.3% | 98.2% | 100.6%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 100.0% | 100.5% | 100.0%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 99.7% | 99.6% | 100.2%

## Slide 9: Results
The combination of DDD and the additional texture candidate
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 98.8% | 93.2% | 101.4%
Kendo | 0.0% | -0.2% | -0.1% | 0.0% | -0.1% | -0.2% | 99.9% | 105.1% | 102.7%
Newspaper_CC | 0.0% | -0.1% | 0.1% | 0.0% | -0.1% | -0.2% | 99.4% | 101.5% | 101.3%
GT_Fly | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.9% | 98.8% | 88.8% | 99.4%
Poznan_Hall2 | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 109.8% | 99.4%
Poznan_Street | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.2% | 98.5% | 107.5% | 95.5%
Undo_Dancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | 99.1% | 79.4% | 94.4%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.5% | 96.0% | 91.1% | 98.0%
1024x768 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.2% | 99.4% | 99.9% | 101.8%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | 98.4% | 95.3% | 97.3%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | 98.8% | 97.1% | 99.0%

## Slide 10: Conclusion
Two additional merging candidates are proposed
  A disparity derived depth coding candidate
  An additional texture merging candidate
The combination achieves an average BD-rate saving of 0.3% for the synthesized views
Suggest to be adopted

## Slide 11: Thank you for your attention!