## Slide 1: JCT3V-G0064 3D-CE4: Results on adaptive ARP
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  In ARP, NBDV and DMV is used as estimated DV/MV
  May be not accurate enough
Proposed
  Adaptive ARP (AdpARP)
Results
  Achieve 0.22% BD-rate saving for the synthesized views

## Slide 3: The problem
In ARP, NBDV is used as the estimated DV in the MCP case
  NBDV is the first encountered DV from a neighbouring block.
DMV is used as the estimated MV in the DCP case
  DMV is the MV in the corresponding block in the base view.
The estimated DV/MV may be not so accurate, which harms the similarity between the pseudo residue and the real one.

## Slide 4: Proposed
  Adaptive ARP
    3 DV/MV candidates are derived from neighbouring blocks.
    The encoder can find the best DV/MV candidate in ARP according to RDO criterion and signal the index to the decoder.
    DMV is inserted as the first MV candidate in MCP case.
    Aligned temporal DV (ATDV) is proposed as a new DV candidate in DCP case
      ATDV is obtained from the aligned block, which is located by a scaled MV to the collocated picture.
      Two collocated pictures are utilized, as in the NBDV derivation.
      ATDV is put into the candidate list first in DCP case

## Slide 5: Proposed
ATDV

## Slide 6: Results
AdpARP with ½ weighting
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.25% | -0.40% | -0.18% | -0.17% | -0.14% | 111.7% | 93.3% | 99.8%
Kendo | 0.00% | -1.27% | -1.44% | -0.64% | -0.61% | -0.39% | 111.4% | 98.8% | 97.4%
Newspaper_CC | 0.00% | -0.28% | -0.15% | -0.13% | -0.14% | -0.08% | 109.8% | 100.7% | 97.4%
GT_Fly | 0.00% | 0.05% | -0.03% | -0.07% | -0.06% | -0.04% | 107.8% | 100.8% | 100.4%
Poznan_Hall2 | 0.00% | -0.16% | -0.03% | -0.09% | -0.13% | 0.10% | 110.0% | 104.7% | 96.5%
Poznan_Street | 0.00% | -0.46% | -0.37% | -0.20% | -0.20% | -0.12% | 110.1% | 104.4% | 98.8%
Undo_Dancer | 0.00% | -0.41% | -0.44% | -0.18% | -0.17% | -0.16% | 113.0% | 94.0% | 96.5%
Shark | 0.00% | -0.22% | 0.04% | -0.11% | -0.12% | -0.03% | 104.8% | 95.3% | 98.1%
1024x768 | 0.00% | -0.60% | -0.66% | -0.32% | -0.30% | -0.20% | 111.0% | 97.6% | 98.2%
1920x1088 | 0.00% | -0.24% | -0.17% | -0.13% | -0.14% | -0.05% | 109.1% | 99.9% | 98.1%
average | 0.00% | -0.38% | -0.35% | -0.20% | -0.20% | -0.11% | 109.8% | 99.0% | 98.1%

## Slide 7: Results
AdpARP without ½ weighting
  ½ weighting introduces additional overhead bits.
  But it is not so useful when the estimated DV is accurate enough.
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -0.82% | -0.60% | -0.28% | -0.25% | -0.29% | 102.7% | 95.6% | 103.8%
Kendo | 0.00% | -1.11% | -1.22% | -0.45% | -0.38% | -0.40% | 104.2% | 99.8% | 101.9%
Newspaper_CC | 0.00% | -0.33% | -0.15% | -0.09% | -0.08% | -0.09% | 102.6% | 108.7% | 101.5%
GT_Fly | 0.00% | -0.14% | -0.19% | -0.08% | -0.07% | -0.08% | 101.9% | 102.4% | 102.4%
Poznan_Hall2 | 0.00% | -0.12% | -0.23% | -0.05% | -0.04% | 0.03% | 103.6% | 99.8% | 96.8%
Poznan_Street | 0.00% | -0.30% | -0.38% | -0.07% | -0.06% | -0.09% | 103.0% | 104.8% | 100.9%
Undo_Dancer | 0.00% | -0.70% | -0.72% | -0.22% | -0.20% | -0.16% | 104.4% | 91.3% | 96.5%
Shark | 0.00% | -0.39% | -0.18% | -0.13% | -0.12% | -0.05% | 100.9% | 97.4% | 96.6%
1024x768 | 0.00% | -0.75% | -0.66% | -0.27% | -0.24% | -0.26% | 103.2% | 101.4% | 102.4%
1920x1088 | 0.00% | -0.33% | -0.34% | -0.11% | -0.10% | -0.07% | 102.7% | 99.1% | 98.7%
average | 0.00% | -0.49% | -0.46% | -0.17% | -0.15% | -0.14% | 102.9% | 100.0% | 100.1%

## Slide 8: Results
ADVD+ ATDV without ½ weighting
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.00% | -1.28% | -1.16% | -0.44% | -0.38% | -0.44% | 102.6% | 91.5% | 102.0%
Kendo | 0.00% | -1.35% | -1.40% | -0.56% | -0.51% | -0.50% | 103.5% | 98.6% | 99.6%
Newspaper_CC | 0.00% | -0.64% | -0.45% | -0.20% | -0.18% | -0.23% | 102.2% | 101.1% | 100.7%
GT_Fly | 0.00% | -0.27% | -0.32% | -0.11% | -0.09% | -0.06% | 104.1% | 100.0% | 102.6%
Poznan_Hall2 | 0.00% | -0.45% | -0.57% | -0.20% | -0.18% | -0.16% | 103.0% | 103.5% | 102.6%
Poznan_Street | 0.00% | -0.42% | -0.46% | -0.10% | -0.08% | -0.11% | 103.1% | 112.3% | 100.8%
Undo_Dancer | 0.00% | -0.61% | -0.75% | -0.22% | -0.19% | -0.21% | 104.8% | 86.6% | 97.7%
Shark | 0.00% | -0.42% | -0.29% | -0.15% | -0.13% | -0.08% | 100.0% | 91.7% | 99.5%
1024x768 | 0.00% | -1.09% | -1.00% | -0.40% | -0.36% | -0.39% | 102.8% | 97.0% | 100.8%
1920x1088 | 0.00% | -0.43% | -0.48% | -0.15% | -0.14% | -0.12% | 103.0% | 98.8% | 100.6%
average | 0.00% | -0.68% | -0.67% | -0.25% | -0.22% | -0.22% | 102.9% | 98.2% | 100.7%

## Slide 9: Conclusion
AdpARP is proposed to improve ARP
0.22% BD-rate saving for the synthesized views
Recommend to be adopted

## Slide 10: Thank you for your attention!