## Slide 1
CE3 : AMVP candidate list construction for DCP blocks
January 2014
LG Electronics

## Slide 2: Introduction
Two prediction modes for 3D-HEVC
  Merge : Additional candidates for inter-view prediction
    Inter-view motion vector predictor (IVMP)
    Depth-refined DCP candidate
    VSP
    Combined candidates
  AMVP
    IVMP used to be one of candidates
    Currently no inter-view candidate
But we still have a chance to improve the AMVP for inter-view prediction, for DCP blocks.

## Slide 3: Proposed method
The proposed method is to reuse a refined disparity used in merge process for AMVP DCP blocks.
  The idea is identical to JCT3V-E0189 and F0121.
  If a current reference picture is an inter-view picture and the number of candidates is not sufficient, the refined disparity is added as one of candidates.
  If none of candidates is available, the AMVP candidate list are filled with the refined disparity and a zero vector.

## Slide 4: Proposed method
The proposed method only checks whether the number of candidates is less than 2.
The proposed method is invoked only when the NBDV of current CU is available.
if refPic.viewId != currPic.viewId
if numCand < 2
if currCu.bNBDVavailable
mvpList[numCand] = currCu.DoNBDV
numCand += 1
The proposed method 1
if refPic.viewId != currPic.viewId
if numCand < 2
if currCu.bNBDVavailable
mvpList[numCand] = currCu.NBDV
numCand += 1
The proposed method 2

## Slide 5: Complexity analysis
HTM9.0r1 | Method Proposed in G0065
A0, A1, B0, B1, B2 (spatial candidates) | A0, A1, B0, B1, B2 (spatial candidates)
Temporal candidate | Temporal candidate
Zero candidate | DoNBDV (NBDV)/ Zero candidate
Method Proposed in G0065 | Note
Additional comparisons : 3 additional checks | Num. of candidates check View index of reference frame check NBDV availability check
Additional memory accesses: 1 access for DoNBDV(NBDV) (could be loaded in one time) | Depending on implementation, DoNBDV(NBDV) is available without memory access

## Slide 6: Experimental results
Experimental result shows that the coding efficiency can be improved by the proposed method.
  When the refine disparity, DoNBDV, is inserted as a candidate

## Slide 7: Experimental results
Experimental result shows that the coding efficiency can be improved by the proposed method.
  When the disparity from neighbor blocks or temporal blocks, NBDV, is inserted as a candidate
  If the NBDV is inserted as a candidate, coding gains are observed in most of sequences.

## Slide 8: Conclusion
The proposed method is to reuse DoNBDV as supplements if the number of AMVP candidates for the inter-view reference is not maximal.
It can be implemented with reusing of current AMVP module.
  Whether HEVC AMVP is reusable or not is an implemental issue.
Since the DoNBDV is obtained at CU-level,
  Additional refined disparity calculation for DCP AMVP is not necessary.
  It is free from the memory cost issue.
We recommend this proposal is adopted for the next version.