## Slide 1: JCT3V-G0066 Syntax redundancy removal for illumination compensation
Kai Zhang, Jicheng An, Xianguo Zhang, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  There is syntax redundancy for IC in merge blocks.
Proposed
  Remove such redundancy without imposing parsing dependency
Results
  Achieve 0.1% BD-rate saving for the synthesized views

## Slide 3: The problem
IC only takes effects to DCP
An ic_flag is always signaled when the merge index !=0.
  To avoid parsing dependency
Therefore, there is syntax redundancy when ic_flag is sent but the selected merging candidate does not employ DCP

## Slide 4: Proposed
  It is proposed to remove the syntax redundancy by modifying the merging candidate construction process
    When an ic_flag equal to 1 is received, a candidate that does not employ DCP is considered as unavailable.
    When an ic_flag equal to 0 is received, the original merging candidate construction applies.
  There is no parsing dependency or syntax redundancy

## Slide 5: Results
Achieve 0.1% gain in CTC.
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.4% | -0.3% | -0.2% | -0.1% | -0.1% | 96.3% | 89.4% | 96.6%
Kendo | 0.0% | -0.9% | -0.8% | -0.3% | -0.3% | -0.2% | 97.5% | 90.1% | 96.8%
Newspaper_CC | 0.0% | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 96.1% | 100.1% | 97.0%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 95.4% | 86.9% | 95.6%
Poznan_Hall2 | 0.0% | -0.2% | -0.2% | -0.1% | -0.1% | 0.0% | 96.6% | 101.4% | 96.1%
Poznan_Street | 0.0% | -0.1% | -0.3% | -0.1% | -0.1% | 0.0% | 95.9% | 102.0% | 94.3%
Undo_Dancer | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 98.2% | 88.5% | 94.7%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 95.6% | 96.3% | 96.6%
1024x768 | 0.0% | -0.5% | -0.4% | -0.2% | -0.2% | -0.1% | 96.6% | 93.2% | 96.8%
1920x1088 | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 96.3% | 95.0% | 95.5%
average | 0.0% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | 96.5% | 94.3% | 96.0%

## Slide 6: Conclusion
Proposed to remove the syntax redundancy by modifying the merging candidate construction process.
0.1% BD-rate saving for the synthesized view without increasing parsing dependency
Suggest to be adopted

## Slide 7: Thank you for your attention!