## Slide 1: Availability checking of temporal inter-view MV candidate and VSP candidate
Jicheng An, Yi-Wen Chen, Kai Zhang, Jian-Liang Lin, and Shawmin Lei

## Slide 2: Overall Summary
Problem definition
  When the inter-view picture is not in the reference lists, the inter-view MV and VSP candidates will use an unavailable reference view
Proposed method
  When there is no inter-view picture in the current reference lists, the inter-view MV and VSP candidate are disabled.
  No BD-rate change in CTC
<number>

## Slide 3: Unavailable inter-view reference picture
When there is no inter-view picture in current reference lists,
  The reference view of derived DV is unavailable,
  The temporal inter-view MV candidate (including sub-PU temporal inter-view MV candidate and shifted temporal inter-view MV candidate) and VSP candidate should not be used anymore.
  But in current 3D-HEVC, the temporal inter-view MV candidate and VSP candidate are still be used, which will result in an unpredictable behavior because an improper reference view index value of derived DV is used
<number>

## Slide 4: Proposed method
When there is no inter-view picture in the current reference lists
  Disable the temporal inter-view MV candidate and VSP candidate, that is to say, the two kinds of candidates cannot be inserted into the merge candidate list.
  That case can be identified by checking whether the derived DV has reference view index equal to -1 in the draft text and HTM software.
No performance change under CTC.
<number>

## Slide 5: Conclusion
When the inter-view picture is not in the reference lists, the inter-view MV and VSP candidates uses an unavailable reference view
Proposed method
  When there is no inter-view picture in the current reference lists, the inter-view MV and VSP candidate are disabled.
  No BD-rate change in CTC
<number>

## Slide 6: Thank you!