## Slide 1: 3D-CE1 related: Restricted bi-prediction for sub-PU
Jicheng An, Jian-Liang Lin, Kai Zhang, Yi-Wen Chen, and Shawmin Lei

## Slide 2: Overall Summary
Disable the bi-prediction for sub-PU smaller than 8x8
Suggestion 1
  Only disable bi-prediction for small sub-PU in inter-view motion prediction
Suggestion 2
  Disable bi-prediction for small Sub-PU in both inter-view motion prediction and VSP
Aligned with HEVC
Results
  0.02% BD-rate saving for synthesized views.
<number>

## Slide 3: Sub-PU size in HTM
Sub-PU inter-view motion prediction
  For CTC, the sub-PU can be smaller than 8x8
    When PU=16x4/4x16, the sub-PU=8x4/4x8
VSP
  The sub-PU size always 8x4 or 4x8
In HEVC, the bi-prediction in small PU sizes (8x4, 4x8) is disabled.
  To reduce the memory bandwidth
However, the sub-PU related methods in 3D-HEVC miss the restriction.
  The worst case memory bandwidth could be unacceptable
<number>

## Slide 4: Proposed suggestion 1
Disable the bi-prediction for sub-PU smaller than 8x8 in inter-view motion prediction
  Bi-prediction for VSP is kept since only horizontal interpolation is used for VSP
  Prediction in list1 is disabled
<number>

## Slide 5: Proposed suggestion 2
Disable the bi-prediction for sub-PU smaller than 8x8 in both inter-view motion prediction and VSP
  Prediction in list1 is disabled
<number>

## Slide 6: Experimental Results
Implemented on HTM9.0r1
<number>

## Slide 7: Conclusion
Disable the bi-prediction for sub-PU smaller than 8x8
Suggestion 1
  Only disable bi-prediction for small sub-PU in inter-view motion prediction
Suggestion 2
  Disable bi-prediction for small Sub-PU in both inter-view motion prediction and VSP
Aligned with HEVC
Results
  0.02% BD-rate saving for synthesized views.
<number>

## Slide 8: Thank you!