## Slide 1
Page <number>
Improvement on Do-NBDV derivation
Xu Chen, Yongbin Lin, Xiaozhen Zheng and Jianhua Zheng
Notes: 26/7/28
<number>

## Slide 2: Summary
Page <number>
In 3D-HEVC, Do-NBDV needs a depth-to-DV conversion to extract disparity vector from a depth block
  The depth-to-DV conversion in Do-NBDV uses a maximum among four points scheme within a PU.
Proposed simplification and refinement of depth-to-DV conversion by maximum among four corners for Do-NBDV
  Simplification from maximum among two or three corners
  Do-NBDV refinement with calculated Do-NBDV
Thanks for cross-check by SHARP

## Slide 3: Summary
Page <number>
  Use an estimated disparity vector (NBDV) to locate the corresponding block in the coded texture view, then use the associated depth block in the coded view as the virtual depth for the current block (coding unit).
  Extract a derived disparity vector from the depth block by maximum among four points scheme for each PU.
CB
T1
Coded D0
Collocated depth
Estimated disparity vector
Virtual depth

## Slide 4: Method 1- Do-NBDV Simplification
Page <number>
Extract a derived disparity vector from the depth block by maximum among two or three corners scheme for each PU
CB
T1
Coded D0
Collocated depth
Estimated disparity vector
Virtual depth

## Slide 5: Method 2- Do-NBDV Refinement
Page <number>
Base on Simplification, we can do more improvement on Do-NBDV
Get information of Hor value to relocate the associated depth block and maximum the corners (Add)
………
maxDepthVal = std::max( maxDepthVal, depthTL[ (depthEndPosY) * depStride + depthEndPosX ]);
/////////add maximum two corners case
mv->setHor( aiShiftLUT[ maxDepthVal ] );
depthStartPosX = Clip3(0, iPictureWidth - 1, iBlkX + ((mv->getHor()+2)>>2));
depthEndPosX = Clip3(0, iPictureWidth - 1, iBlkX + iBlkWidth - 1 + ((mv->getHor()+2)>>2));
maxDepthVal = 0;
maxDepthVal = std::max( maxDepthVal, depthTL[ (depthEndPosY) * depStride + depthStartPosX ]);
maxDepthVal = std::max( maxDepthVal, depthTL[ (depthEndPosY) * depStride + depthEndPosX ]);
//////////add

## Slide 6: Results
Page <number>
HTM9.0r1 Test condition: CTC
Table 1. Coding results for the contribution
average | video1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Simplified (two corners) | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 99.4% | 99.0% | 100.0%
Simplified (three corners) | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.4% | 98.2% | 96.3%
Refinement (four corners) | -0.2% | -0.2% | -0.1% | -0.1% | 0.0% | 99.4% | 99.1% | 100.0%
Refinement with simplified (three corners) | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | 99.6% | 99.8% | 99.9%
Refinement with simplified (two corners) | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 99.4% | 99.9% | 99.9%

## Slide 7: Conclusions
Page <number>
Simplified depth-to-DV conversion
  Use the maximum among two or three corners of the depth samples to extract a disparity vector from the virtual depth block in Do-NBDV, less computation and save memory space without coding impact.
Refined depth-to-DV conversion
  Minor complexity improve, also bring small BD rate reduction (0.1 or 0 coding gain with simplification).
Suggest to adopt this proposal.

## Slide 8
Page <number>
Thank you!
www.hisilicon.com

## Slide 9: Supplement
Page <number>
HTM9.0r1 Test condition: CTC
Table 1. Coding results for enabling maximum among two corners in Do-NBDV
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.2% | 0.2% | 0.00% | -0.02% | -0.07% | 100.2% | 97.3% | 101.1%
Kendo | 0.0% | -0.2% | 0.2% | 0.01% | 0.00% | -0.01% | 97.9% | 100.1% | 99.9%
Newspaper_CC | 0.0% | -0.4% | 0.1% | -0.04% | -0.04% | -0.01% | 98.2% | 98.5% | 99.0%
GT_Fly | 0.0% | -0.2% | -0.1% | -0.02% | -0.01% | -0.02% | 99.7% | 98.8% | 100.2%
Poznan_Hall2 | 0.0% | -0.3% | 0.0% | -0.06% | -0.06% | 0.07% | 99.6% | 100.7% | 100.2%
Poznan_Street | 0.0% | -0.1% | 0.0% | 0.00% | 0.01% | 0.02% | 100.1% | 98.9% | 99.7%
Undo_Dancer | 0.0% | 0.0% | 0.0% | -0.01% | -0.02% | -0.02% | 99.7% | 99.2% | 99.5%
Shark | 0.0% | 0.9% | 1.0% | 0.16% | 0.13% | 0.15% | 99.4% | 98.4% | 100.5%
1024x768 | 0.0% | -0.3% | 0.2% | -0.01% | -0.02% | -0.03% | 98.8% | 98.7% | 100.0%
1920x1088 | 0.0% | 0.1% | 0.2% | 0.02% | 0.01% | 0.04% | 99.7% | 99.2% | 100.0%
average | 0.0% | 0.0% | 0.2% | 0.01% | 0.00% | 0.01% | 99.4% | 99.0% | 100.0%

## Slide 10: Supplement
Page <number>
HTM9.0r1 Test condition: CTC
Table 1. Coding results for enabling maximum among three corners in Do-NBDV
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.1% | 0.00% | -0.02% | -0.03% | 99.5% | 98.3% | 98.5%
Kendo | 0.0% | -0.1% | -0.2% | -0.06% | -0.04% | -0.07% | 99.8% | 100.1% | 100.7%
Newspaper_CC | 0.0% | -0.1% | 0.1% | -0.01% | -0.02% | 0.03% | 99.0% | 95.6% | 97.0%
GT_Fly | 0.0% | 0.0% | -0.1% | -0.01% | -0.02% | -0.01% | 99.6% | 99.9% | 93.1%
Poznan_Hall2 | 0.0% | -0.2% | -0.1% | -0.04% | -0.02% | 0.05% | 99.0% | 99.4% | 94.1%
Poznan_Street | 0.0% | -0.1% | -0.1% | -0.03% | -0.01% | -0.03% | 99.5% | 100.8% | 94.9%
Undo_Dancer | 0.0% | -0.2% | 0.0% | -0.04% | -0.04% | -0.02% | 99.4% | 93.5% | 94.3%
Shark | 0.0% | 0.4% | 0.3% | 0.05% | 0.04% | 0.04% | 99.1% | 97.9% | 97.9%
1024x768 | 0.0% | -0.1% | 0.0% | -0.02% | -0.03% | -0.03% | 99.4% | 98.0% | 98.7%
1920x1088 | 0.0% | 0.0% | 0.0% | -0.02% | -0.01% | 0.01% | 99.3% | 98.3% | 94.9%
average | 0.00% | -0.05% | 0.00% | -0.02% | -0.02% | -0.01% | 99.4% | 98.2% | 96.3%

## Slide 11: Results-Refinement-four corners
Page <number>
HTM9.0r1 Test condition: CTC
Table 2. Coding results for Do-NBDV refinement with maximum among four corners in Do-NBDV
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.2% | 0.0% | -0.04% | -0.03% | -0.07% | 100.4% | 98.2% | 100.2%
Kendo | 0.0% | -0.1% | -0.4% | -0.10% | -0.07% | -0.11% | 98.5% | 101.8% | 100.3%
Newspaper_CC | 0.0% | -0.4% | -0.4% | -0.14% | -0.12% | -0.02% | 98.3% | 97.3% | 99.2%
GT_Fly | 0.0% | 0.0% | -0.2% | -0.03% | -0.03% | -0.02% | 99.4% | 99.4% | 100.1%
Poznan_Hall2 | 0.0% | -0.2% | -0.1% | -0.06% | -0.08% | 0.02% | 99.6% | 99.6% | 100.4%
Poznan_Street | 0.0% | -0.3% | -0.2% | -0.08% | -0.06% | -0.05% | 100.1% | 98.0% | 99.6%
Undo_Dancer | 0.0% | 0.0% | -0.3% | -0.04% | -0.05% | -0.05% | 99.7% | 99.8% | 99.8%
Shark | 0.0% | -0.2% | -0.2% | -0.04% | -0.04% | -0.02% | 99.3% | 98.3% | 100.5%
1024x768 | 0.0% | -0.3% | -0.3% | -0.09% | -0.07% | -0.07% | 99.1% | 99.1% | 99.9%
1920x1088 | 0.0% | -0.1% | -0.2% | -0.05% | -0.05% | -0.02% | 99.6% | 99.0% | 100.1%
average | 0.0% | -0.2% | -0.2% | -0.06% | -0.06% | -0.04% | 99.4% | 99.1% | 100.0%

## Slide 12: Results-Refinement-three corners
Page <number>
HTM9.0r1 Test condition: CTC
Table 3. Coding results for Do-NBDV refinement with maximum among three corners in Do-NBDV
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.2% | -0.2% | -0.06% | -0.06% | -0.09% | 100.3% | 100.1% | 100.3%
Kendo | 0.0% | -0.2% | -0.4% | -0.10% | -0.07% | -0.13% | 98.0% | 103.2% | 100.1%
Newspaper_CC | 0.0% | -0.7% | -0.4% | -0.18% | -0.17% | -0.12% | 98.6% | 97.6% | 99.6%
GT_Fly | 0.0% | -0.2% | -0.1% | -0.03% | -0.04% | -0.05% | 99.9% | 99.9% | 100.1%
Poznan_Hall2 | 0.0% | -0.2% | -0.1% | -0.06% | -0.07% | 0.03% | 100.1% | 100.5% | 99.8%
Poznan_Street | 0.0% | -0.2% | -0.1% | -0.06% | -0.05% | -0.06% | 100.5% | 99.1% | 99.4%
Undo_Dancer | 0.0% | -0.1% | -0.1% | -0.04% | -0.05% | -0.02% | 99.8% | 99.6% | 99.3%
Shark | 0.0% | 0.2% | 0.0% | 0.01% | 0.00% | 0.02% | 99.4% | 98.6% | 100.4%
1024x768 | 0.0% | -0.3% | -0.3% | -0.12% | -0.10% | -0.11% | 99.0% | 100.3% | 100.0%
1920x1088 | 0.0% | -0.1% | -0.1% | -0.04% | -0.04% | -0.02% | 99.9% | 99.5% | 99.8%
average | 0.0% | -0.2% | -0.2% | -0.07% | -0.06% | -0.05% | 99.6% | 99.8% | 99.9%

## Slide 13: Results-Refinement-two corners
Page <number>
HTM9.0r1 Test condition: CTC
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | -0.2% | 0.0% | -0.01% | 0.00% | -0.02% | 100.0% | 99.4% | 100.0%
Kendo | 0.0% | -0.2% | -0.1% | -0.05% | -0.02% | -0.07% | 97.7% | 101.5% | 100.7%
Newspaper_CC | 0.0% | -0.6% | -0.3% | -0.16% | -0.15% | -0.09% | 98.5% | 98.4% | 99.2%
GT_Fly | 0.0% | -0.2% | 0.0% | -0.03% | -0.03% | -0.03% | 99.4% | 98.7% | 99.9%
Poznan_Hall2 | 0.0% | -0.4% | -0.2% | -0.12% | -0.12% | -0.09% | 99.9% | 100.2% | 99.8%
Poznan_Street | 0.0% | -0.2% | -0.1% | -0.06% | -0.04% | -0.03% | 100.1% | 99.2% | 99.5%
Undo_Dancer | 0.0% | 0.0% | 0.0% | -0.02% | -0.03% | 0.02% | 100.1% | 103.3% | 99.3%
Shark | 0.0% | 0.8% | 1.0% | 0.13% | 0.12% | 0.13% | 99.6% | 98.6% | 100.3%
1024x768 | 0.0% | -0.3% | -0.1% | -0.07% | -0.06% | -0.06% | 98.7% | 99.8% | 100.0%
1920x1088 | 0.0% | 0.0% | 0.1% | -0.02% | -0.02% | 0.00% | 99.8% | 100.0% | 99.8%
average | 0.0% | -0.1% | 0.0% | -0.04% | -0.03% | -0.02% | 99.4% | 99.9% | 99.9%
Table 3. Coding results for Do-NBDV refinement with maximum among two corners in Do-NBDV