## Slide 1: CE3 related: Results on Limitation of the Range of NBDV (JCT3V-G0082)
Peng Lu and Lu Yu (yul@zju.edu.cn)

## Slide 2: Backgroud
Neighboring Block Disparity Vector (NBDV) is a estimated disparity vector used for IVMP, VSP and ARP. NBDV is also used to generate the DoNBDV when depth_refinement_flag is equal to 1.
NBDV is derived from the disparity vectors of DCP-coded neighboring blocks.

## Slide 3: Problem Statement (1)
Disparity vector represents the distance of the same object in different views. While the disparity vector of DCP neighboring blocks is derived by motion estimation, which takes both rate and distortion under consideration. Therefore, the disparity vector of DCP neighboring blocks may not be accurate.

## Slide 4: Problem Statement (2)
NBDV is used to fetch the texture and depth maps of the reference view.

## Slide 5: Problem Statement (2)
NBDV is used to fetch the texture and depth maps of the reference view.
In current design, the range of NBDV is not limited. However, the range of all the possible disparity among two views is limited and is often much smaller.
Therefore, in hardware implementation, the current design brings more cache miss and may request more bandwidth or on-chip memory than it really needs, especially for the coded depth map, which will only be accessed by NBDV.

## Slide 6
Proposed method
To solve the above problems, we propose to limit the range of NBDV when depth_refinement_flag equals to 1 under the following considerations:
  The range of all the possible disparity among two views is limited. This range can be calculated by assuming the depth map of the current view contains all possible depth values, e.g. from 0 to 255 when bit depth is 8.
  The disparity vectors derived by motion estimation are not very accurate, even fall out of the possible disparity range sometimes.

## Slide 7
Method 1
Assuming the depth map of the current texture view contains all possible depth values. Find a maximum disparity (DispMax) and a minimum disparity (DispMin) between the current view and reference view. Note that DispMax and DispMin can be calculated once per slice.
Derive a NBDV using current method.
If a NBDV can be derived, clip the horizontal component of NBDV to [DispMin, DispMax] and clip the vertical component of NBDV to [-CtbSizeY, CtbSizeY], where CtbSizeY is the size of LCU.
If no NBDV is derived, use the defualt DV with horizontal component equal to (DispMin+DispMax)>>1 and vertical component equal to 0.

## Slide 8
Method 1
By applying Method 1, the range of NBDV and the possible accessed area in reference view can be limited into a rectangle area, as the green rectangle area shown below.

## Slide 9
Method 1
 | Before Limitation |  |  | After Limitation |  |  | Ratio
 | Width | Height | Size | Width | Height | Size | 
Balloons | 1024 | 768 | 786432 | 112 | 192 | 21504 | 2.7%
Kendo | 1024 | 768 | 786432 | 112 | 192 | 21504 | 2.7%
Newspaper_CC | 1024 | 768 | 786432 | 134 | 192 | 25728 | 3.3%
GT_Fly | 1920 | 1088 | 2088960 | 110 | 192 | 21120 | 1.0%
Poznan_Hall2 | 1920 | 1088 | 2088960 | 166 | 192 | 31872 | 1.5%
Poznan_Street | 1920 | 1088 | 2088960 | 143 | 192 | 27456 | 1.3%
Undo_Dancer | 1920 | 1088 | 2088960 | 144 | 192 | 27648 | 1.3%
Shark | 1920 | 1088 | 2088960 | 97 | 192 | 18624 | 0.9%
Average | 1584 | 968 | 1600512 | 127.25 | 192 | 24432 | 1.9%

## Slide 10
Method 1
Such a limitation can reduce the cache miss when fetching the reference views and save the bandwidth or on-chip memory for hardware design.
If the derived NBDV is out of the possible disparity range, it can be improved by the above clipping process. Therefore, the accuracy of NBDV can be improved.

## Slide 11
Method 1
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.00% | -0.15% | -0.12% | -0.04% | -0.05% | -0.08%
Kendo | 0.00% | -0.22% | -0.18% | -0.08% | -0.06% | -0.07%
Newspaper_CC | 0.00% | -0.23% | -0.11% | -0.05% | -0.06% | -0.03%
GT_Fly | 0.00% | -0.14% | -0.09% | -0.02% | -0.02% | -0.02%
Poznan_Hall2 | 0.00% | 0.17% | -0.02% | 0.03% | 0.00% | 0.06%
Poznan_Street | 0.00% | -0.03% | -0.08% | -0.01% | -0.01% | 0.00%
Undo_Dancer | 0.00% | -0.10% | -0.03% | -0.02% | -0.02% | -0.09%
Shark | 0.00% | -0.06% | -0.23% | -0.03% | -0.04% | -0.03%
1024x768 | 0.00% | -0.20% | -0.14% | -0.05% | -0.06% | -0.06%
1920x1088 | 0.00% | -0.03% | -0.09% | -0.01% | -0.02% | -0.02%
average | 0.00% | -0.09% | -0.11% | -0.03% | -0.03% | -0.03%
Notes: <number>

## Slide 12
Method 2
(Assuming the depth map of the current texture view contains all possible depth values. Find a maximum disparity (DispMax) and a minimum disparity (DispMin) between the current view and reference view. This is as the same as Method 1.
Derive the NBDV. During this process, if a candidate DV is out of the range [DispMin, DispMax], it will be ignored and the derivation process continues, otherwise, clip the vertical component of this candidate DV to [-CtbSizeY, CtbSizeY] and use this candidate DV as the final NBDV, where CtbSizeY is the size of LCU.
If no NBDV is derived, use the defualt DV with horizontal component equal to (DispMin+DispMax)>>1 and vertical component equal to 0.

## Slide 13
Method 2
Method 2 is similar to Method 1, the range of NBDV and the possible accessed area in reference view can also be limited into a same rectangle area. Thus method 2 can also bring the benefits in hardware implementation as method 1.
Method 2 also eliminates those candidate DVs that fall out of the disparity range, thus a more accurate NBDV may be found.

## Slide 14
Method 2
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate
Balloons | 0.00% | -0.06% | -0.03% | -0.02% | -0.02% | -0.08%
Kendo | 0.00% | -0.28% | -0.22% | -0.09% | -0.07% | -0.06%
Newspaper_CC | 0.00% | -0.34% | -0.02% | -0.05% | -0.05% | -0.04%
GT_Fly | 0.00% | -0.08% | 0.03% | -0.01% | 0.00% | -0.05%
Poznan_Hall2 | 0.00% | -0.02% | -0.19% | -0.04% | -0.04% | -0.04%
Poznan_Street | 0.00% | -0.15% | -0.01% | -0.02% | -0.01% | 0.00%
Undo_Dancer | 0.00% | -0.06% | -0.09% | -0.02% | -0.02% | -0.03%
Shark | 0.00% | -0.17% | -0.24% | -0.04% | -0.05% | -0.05%
1024x768 | 0.00% | -0.23% | -0.09% | -0.05% | -0.05% | -0.06%
1920x1088 | 0.00% | -0.09% | -0.10% | -0.02% | -0.02% | -0.03%
average | 0.00% | -0.14% | -0.10% | -0.03% | -0.03% | -0.04%
Notes: <number>

## Slide 15: Conclusion
This proposal gives two methods to limit the range of NBDV.
Both of the two methods can limit the range NBDV into a rectangle area. Such a limitation can reduce the cache miss when fetching the reference views and save the bandwidth or on-chip memory for hardware design.
This proposal can also improve the accuracy of NBDV and has some coding performance improvement.
We recommend adopting the Method 1 because method 1 is simpler and without degradation of coding efficiency compared to Method 2.

## Slide 16
Thanks ZTE for crosscheck!
Q & A