## Slide 1: JCT3V-F0104 CE3 related: Result on clean ups of VSP merging candidates
Yichen Zhang, Lu Yu
Zhejiang University

## Slide 2: Introduction
HEVC v1 merge candidate list contruction
3D-HEVC candidate insertion

## Slide 3: Problem
Identical VSP candidates except merge index
DV for virtual depth block = NBDV
Same DV for virtual depth block fetching for all VSP candidates
  Same VSP prediction samples

## Slide 4
Method 1

## Slide 5: Proposed Method
Method 1
Current:
Proposed:

## Slide 6: Proposed Method
Method 1
Proposed:
Only 1 VSP candidate in MCL
Other VSP candidates are converted to DCP candidates
VspFlag of A0 & B2 are always set equal to 0
Default VSP inserted only when A1, B1, B0 are not VSP candidate

## Slide 7: Proposed Method 1
VspFlagA1 = VspFlagA1
VspFlagB1 = !VspFlagA1 & VspFlagB1
VspFlagB0 = !(VspFlagA1 | VspFlagB1) & VspFlagB0
VspFlagA0 = 0
VspFlagB2 = 0

## Slide 8
Method 3

## Slide 9: Proposed Method
Method 3
Current:
Proposed:

## Slide 10: Proposed Method
Method 3
VSP flag storage of coded blocks can be totally removed
Position of VSP candidate in MCL is fixed (mrgIdx = 3)
When mrgIdx is equal to 3, VSP mode is selected, which means the whole MCL construction procedure can be skipped.
Proposed:

## Slide 11: Conclusion
Method | First VSP Candidate | A0/B2 VSP Candidate | Other VSP Candidate(s) | Default VSP Position | Video PSNR/ Video Bitrate | Video PSNR/ Total Bitrate | Synth PSNR/ Total Bitrate
1 | VSP | DCP | DCP | After IvDC | -0.02% | -0.03% | -0.01%
2 | VSP | Remove | Remove | After IvDC | -0.03% | -0.03% | -0.01%
3 | DCP | DCP | DCP | 3 | 0.02% | 0.01% | 0.03%

## Slide 12: Experimental results
 | Video 0 | Video 1 | Video 2 | Video PSNR / Video bitrate | Video PSNR / Total bitrate | Synth PSNR / Total bitrate | Encoding Time | Decoding Time
Balloons | 0.00% | -0.03% | 0.06% | 0.00% | -0.01% | -0.03% | 100.4% | 97.2%
Kendo | 0.00% | -0.10% | -0.16% | -0.05% | -0.04% | -0.06% | 95.2% | 111.7%
Newspaper_CC | 0.00% | -0.02% | 0.04% | 0.00% | -0.02% | 0.03% | 97.1% | 96.0%
GT_Fly | 0.00% | -0.12% | -0.12% | -0.03% | -0.03% | 0.00% | 101.9% | 98.0%
Poznan_Hall2 | 0.00% | -0.10% | -0.01% | -0.01% | -0.02% | 0.03% | 100.2% | 100.5%
Poznan_Street | 0.00% | -0.04% | -0.14% | -0.03% | -0.02% | -0.02% | 99.6% | 108.4%
Undo_Dancer | 0.00% | -0.16% | -0.17% | -0.05% | -0.05% | -0.03% | 102.4% | 95.2%
Shark | 0.00% | -0.17% | -0.15% | -0.04% | -0.04% | -0.02% | 97.4% | 89.4%
1024x768 | 0.00% | -0.05% | -0.02% | -0.02% | -0.02% | -0.02% | 97.5% | 101.6%
1920x1088 | 0.00% | -0.12% | -0.12% | -0.03% | -0.03% | -0.01% | 100.3% | 98.3%
average | 0.00% | -0.09% | -0.08% | -0.02% | -0.03% | -0.01% | 99.26% | 99.56%
Proposed method 1 vs Anchor (HTM-9.0r1)

## Slide 13: Experimental results
 | Video 0 | Video 1 | Video 2 | Video PSNR / Video bitrate | Video PSNR / Total bitrate | Synth PSNR / Total bitrate | Encoding Time | Decoding Time
Balloons | 0.00% | -0.05% | 0.02% | -0.01% | -0.02% | -0.04% | 97.3% | 96.1%
Kendo | 0.00% | -0.11% | -0.36% | -0.08% | -0.06% | -0.14% | 95.6% | 100.7%
Newspaper_CC | 0.00% | -0.10% | 0.07% | -0.01% | -0.01% | 0.07% | 96.5% | 98.3%
GT_Fly | 0.00% | 1.11% | 0.99% | 0.16% | 0.14% | 0.15% | 96.2% | 94.5%
Poznan_Hall2 | 0.00% | -0.05% | -0.01% | -0.02% | -0.04% | 0.05% | 95.7% | 99.2%
Poznan_Street | 0.00% | 0.04% | -0.04% | -0.02% | -0.01% | -0.01% | 97.1% | 103.5%
Undo_Dancer | 0.00% | 0.38% | 0.55% | 0.09% | 0.07% | 0.14% | 98.2% | 100.3%
Shark | 0.00% | 0.32% | 0.16% | 0.02% | -0.01% | 0.02% | 96.0% | 89.3%
1024x768 | 0.00% | -0.09% | -0.09% | -0.04% | -0.03% | -0.04% | 96.5% | 98.4%
1920x1088 | 0.00% | 0.36% | 0.33% | 0.05% | 0.03% | 0.07% | 96.7% | 97.3%
average | 0.00% | 0.19% | 0.17% | 0.02% | 0.01% | 0.03% | 96.59% | 97.74%
Proposed method 3 vs Anchor (HTM-9.0r1)

## Slide 14
Thanks ZTE (G0225) & Huawei (G0230) for cross-checking this proposal