## Slide 1: MV-HEVC/SHVC HLS: Clean-up for output layer sets (JCTVC-Q0165, JCT3V-H0053)
JCT-VC 17th Meeting: Valencia, ES, 27 Mar. – 4 Apr. 2014
JCT-3V 8th Meeting: Valencia, ES, 29 Mar. – 4 Apr. 2014
Takeshi Tsukuba*, Tomoyuki Yamamoto*, Tomohiro Ikai*, Sachin Deshpande**
*SHARP Corporation
**Sharp Labs of America, Inc.

## Slide 2: Summary
Three proposals:
  Restrictions on output layer set:
    Prohibit 1) output layer set with no output layers, 2) duplicated output layer sets with the same output layers.
  Signal num_add_output_layer_sets / default_target_output_layer_set when vps_num_layer_sets_minus1 > 0
  Add a flag indicating whether or not to explicitly signal profile_level_tier_idx/DPB parameters for additional output layer sets
  Benefits
    Avoid the case:
      no output layers in the target output layer set
      two or more output layer sets having the same output layers/AltOptLayerFlag/profile_level_tier_idx
    Simplify the signaling condition for num_add_output_layer_sets / default_target_output_layer_set
    Required bits of profile_level_tier_idx/DPB parameters for additional output layer sets could be reduced with low costs.
      It is recommended to adopt proposals to next SHVC/MV-HEVC.
Notes:   Avoid the improper removal of sharing parameter set in bitstream extraction.
  Enable parameter sharing in case of pixel, motion or any other dependency is not utilized.
  Enhance SPS sharing capability for Extended Spatial Scalability.

## Slide 3: Proposal 1
Background:
  Output layer can be explicitly defined by output_layer_flag.
Problem :
  Output layer sets without any output layer
  Duplicated output layer set definition on the same layer set
Solution: add the following restrictions for semantics of output_layer_flag:
When LayerSetIdxForOutputLayerSet[iA] is equal to LayerSetIdxForOutputLayerSet[iB] for any iA and iB in the range of 0 to NumOutputLayerSets-1, inclusive, with iA not equal to iB, at least one of the following conditions shall be satisfied:
- the value of OutputLayerFlag[iA][n] shall not be equal to OutputLayerFlag[iB][n] for at least one value of n in the range of 0 to NumLayerInIdList[ LayerSetIdxForOutputLayerSet[iA] ] – 1, inclusive.
- the value of AltOuputLayerFlag[iA] shall not be equal to AltOutputLayerFlag[iB].
- the value of profile_level_tier_idx[iA] shall not be equal to profile_level_tier_level_idx[iB].
It is requirement of bitstream comformance that the i-th output layer set shall have one or more output layers.
Or
The sum of OutputLayerFlag[ i ][ j ] for j in the range of 0 to NumLayersInIdList[ LayerSetIdxForOutputLayerSet[ i ] ] − 1, inclusive shall be greater than 0.
For problem a)
For problem b)

## Slide 4: Proposal 2
Background:
  num_add_output_layer_sets is always signaled.
  default_target_output_layer_idc is signaled when NumOutputLayerSets >0.
Problem :
  When vps_num_layer_sets_minus1 is equal to 0 (only base layer), the additional output layer sets syntax doesn’t make sense.
Solution:
  Signal num_add_output_layer_sets and default_target_output_layer_idc when vps_num_layer_sets_minus1 is greater than 0.
vps_extension( ) { | Descriptor
… | 
if (vps_num_layer_sets_minus1 > 0) | 
{ | 
num_add_output_layer_sets | ue(v)
if( NumOutputLayerSets > 1 ) | 
default_target_output_layer_idc | u(2)
} | 
NumOutputLayerSets = num_add_output_layer_sets + vps_num_layer_sets_minus1 + 1 | 

## Slide 5: Proposal 3
Background:
  In the current spec., it is mandated to decode all layers in the target output layer set.
  If all layers are necessary to be decoded, all output layer sets associated with the same layer set may have the same DPB size and probably the same profile/level.
Problem :
  Signaling DPB parameters and profile_level_tier_idx of output layer sets associated with the same output layer is redundant.
Solution:
  Add a flag, ptl_dpb_info_present_flag, indicating whether or not to explicitly signal profile_level_tier_idx/DPB parameters for additional output layer sets

## Slide 6: Proposal 3
LS#A
Layer Set
OLS#A
OLS#X
OLS#Y
OLS#Z
Output layer set
LayerSetIdx = A
DPB_INFO#A
DPB_INFO#X
DPB_INFO#Y
DPB_INFO#Z
DPB Info.
ptl_dpb_info_present_flag[i]
1
1
0
0
When ptl_dpb_info_present_flag[i] is equal to 0,
DPB info. for i-th output layer sets, e.g., DPB_INFO#Y, DPB_INFO#Z, is inferred to be equal to the DPB_INFO#A for OLS#A.
Additional output layer set
Infer
Explicitly signal

## Slide 7: Text changes on Proposal 3 (1/3)
vps_extension( ) { | Descriptor
... | 
for( i = 1; i < NumOutputLayerSets; i++ ) { | 
… | 
if ( i >vps_num_layer_sets_minus1) | 
ptl_dpb_info_present_flag[ i ] | u(1)
if ( ptl_dpb_info_present_flag[ i ] ) | 
profile_level_tier_idx[ i ] | u(v)
… | 
} | 
... | 
dpb_size() | 
... | 
} | 
ptl_dpb_info_present_flag[ i ] equal to 1 specifies that the syntax profile_level_tier_level_idx[ i ] and sub_layer_flag_info_present_flag[ i ], max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ], max_vps_num_reorder_pics[ i ][ j ] max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are present for i-th output layer set. ptl_dpb_info_present_flag[ i ] equal to 0 specifies that the syntax profile_level_tier_level_idx[ i ] and sub_layer_flag_info_present_flag[ i ], max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ], max_vps_num_reorder_pics[ i ][ j ] max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are not present for i-th output layer set.
profile_level_tier_idx[ i ] specifies the index, into the list of profile_tier_level( ) syntax structures in the VPS, of the profile_tier_level( ) syntax structure that applies to i-th output layer set. The length of the profile_level_tier_idx[ i ] syntax element is Ceil( Log2( vps_num_profile_tier_level_minus1 + 1 ) ) bits. The value of profile_level_tier_idx[ 0 ] is inferred to be equal to 0. The value of profile_level_tier_idx[ i ] shall be in the range of 0 to vps_num_profile_tier_level_minus1, inclusive. For the i-th output layer set, when ptl_dpb_info_present_flag[ i ] is equal to 0, profile_level_tier_idx[ i ] is inferred to be equal to the value of profile_level_tier_idx[ output_layer_set_idx_minus1[ i ] + 1 ].

## Slide 8: Text changes on Proposal 3 (2/3)
dpb_size( ) { | Descriptor
for( i = 1; i < NumOutputLayerSets; i++ ) { | 
if( ptl_dpb_info_present_flag[ i ]){ | 
sub_layer_flag_info_present_flag[ i ] | u(1)
for( j = 0; j <= MaxSubLayersInLayerSetMinus1[ i ]; j++ ) { | 
… | 
} | 
} | 
} | 
} | 
The variable OlsIdx[i] is set to be equal to (output_layer_set_idx_minus1[ i ]+1) for i in the range of 1 to NumOutputLayerSets-1.
sub_layer_flag_info_present_flag[ i ] equal to 1 specifies that sub_layer_dpb_info_present_flag[ i ][ j ] is present for i in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive. sub_layer_flag_info_present_flag[ i ] equal to 0 specifies that, for each value of j greater than 0, sub_layer_dpb_info_present_flag[ i ][ j ] is not present and the value is inferred to be equal to 0.
sub_layer_dpb_info_present_flag[ i ][ j ] equal to 1 specifies that max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] is present for k in the range of 0 to NumSubDpbs[ LayerSetIdxForOutputLayerSet[ i ] ] − 1, inclusive, for the j-th sub-layer, and max_vps_num_reorder_pics[ i ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are present for the j-th sub-layer.
sub_layer_dpb_info_present_flag[ i ][ j ] equal to 0 specifies that, the values of max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] are equal to max_vps_dec_pic_buffering_minus1[ i ][ k ][ j − 1 ] for k in the range of 0 to NumSubDpbs[ LayerSetIdxForOutputLayerSet[ i ] ] − 1, inclusive, and that the values max_vps_num_reorder_pics[ i ][ j ] and max_vps_latency_increase_plus1[ i ][ j ] are set equal to max_vps_num_reorder_pics[ i ][ j ‑ 1 ] and max_vps_latency_increase_plus1[ i ][ j ‑ 1 ], respectively. The value of sub_layer_dpb_info_present_flag[ i ][ 0 ] for any possible value of i is inferred to be equal to 1.
When not present, the value of sub_layer_dpb_info_present_flag[ i ][ j ] for j greater than 0 and any possible value of i, is inferred to be equal to 0.

## Slide 9: Text changes on Proposal 3 (3/3)
max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] plus 1 specifies the maximum required size of the k-th sub-DPB for the CVS in the i-th output layer set in units of picture storage buffers when HighestTid is equal to j.
When j is greater than 0, max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] shall be greater than or equal to max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ‑ 1 ].
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, it is inferred to be equal to max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ‑ 1].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_dec_pic_buffering_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, max_vps_dec_pic_buffering_minus1[ i][ k][ j ] is inferred to be equal to the value of max_vps_dec_pic_buffering_minus1[ OlsIdx[i] ][ k][ j ].
max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] plus 1 specifies the maximum number of decoded pictures, of the k-th layer for the CVS in the i-th output layer set, that need to be stored in the DPB when HighestTid is equal to j.
When j is greater than 0, max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] shall be greater than or equal to max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ‑ 1 ].
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to vps_max_sub_layers_minus1 − 1, inclusive, it is inferred to be equal to max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ‑ 1].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] is not present for j in the range of 1 to vps_max_sub_layers_minus1 − 1, inclusive, max_vps_layer_dec_pic_buff_minus1[ i ][ k ][ j ] is inferred to be equal to the value of max_vps_layer_dec_pic_buff_minus1 [ OlsIdx[i] ][ k][ j ].

## Slide 10: Text changes on Proposal 3 (3/3)
max_vps_num_reorder_pics[ i ][ j ] specifies, when HighestTid is equal to j, the maximum allowed number of access units containing a picture with PicOutputFlag equal to 1 that can precede any access unit auA that contains a picture with PicOutputFlag equal to 1 in the i-th output layer set in the CVS in decoding order and follow the access unit auA that contains a picture with PicOutputFlag equal to 1 in output order.
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_num_reorder_pics[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, due to sub_layer_dpb_info_present_flag[ i ][ j ] being equal to 0, it is inferred to be equal to max_vps_num_reorder_pics[ i ][ j ‑ 1].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_num_reorder_pics[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, max_vps_num_reorder_pics[ i][ j ] is inferred to be equal to the value of max_vps_num_reorder_pics [ OlsIdx[i] ] [ j ].
max_vps_latency_increase_plus1[ i ][ j ] not equal to 0 is used to compute the value of VpsMaxLatencyPictures[ i ][ j ], which, when HighestTid is equal to j, specifies the maximum number of access units containing a picture with PicOutputFlag equal to 1 in the i-th output layer set that can precede any access unit auA that contains a picture with PicOutputFlag equal to 1 in the CVS in output order and follow the access unit auA that contains a picture with PicOutputFlag equal to 1 in decoding order.
When ptl_dpb_info_present_flag[ i ] is equal to 1 and max_vps_latency_increase_plus1[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, due to sub_layer_dpb_info_present_flag[ i ][ j ] being equal to 0, it is inferred to be equal to max_vps_latency_increase_plus1[ i ][ j ‑ 1 ].
When ptl_dpb_info_present_flag[ i ] is equal to 0 and max_vps_latency_increase_plus1[ i ][ j ] is not present for j in the range of 1 to MaxSubLayersInLayerSetMinus1[ i ], inclusive, max_vps_latency_increase_plus1 [ i][ j ] is inferred to be equal to the value of max_vps_latency_increase_plus1 [ OlsIdx[i] ] [ j ].

## Slide 11
Thank you!

## Slide 12: Bit amount analysis on proposal 3
Two use-cases are studied.
  Use-case#1: Two output layer sets associated with the same layer set, which have the same output layers and different AltOptLayerFlag values.
  Use-case#2: Three output layer sets associated with the same layer set, which have different output layers and the same AltOptLayerFlag.
Bit-savings are estimated on the condition that profile and DPB info can be inferred and omitted.
Bit-overhead are estimated on the condition that all profile and DPB info are signaled.
 | bit-saving scenario | bit-overhead scenario
Use-case#1 | 49.23 % | -0.77%
Use-case#2 | 66.61% | -0.53 %
Bit-saving ratio compared to ref.(SHVC/MV-HEVC)
100*(ref.- proposal)/ref. [%]

## Slide 13: Use-case#1 (bit-saving scenario)
Use-case#1:
1) There are two output layer sets (OLS#1,OLS#2) associated with the same layer set (LS#1), which have different AltOptLayerFlag (Alt) values. and the same output layers (OptLayer).
LS#1 = { Layer0, Layer1},
OLS#1 = { LS#1, OptLayer={Layer1}, Alt=1},
OLS#2 = { LS#1, OptLayer={Layer1}, Alt=0}
OLS#2 is an additional output layer set against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are inferred and omitted
( ptl_dpb_info_present_flag is 0 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#2 are the same so that DPB size of OLS#2 are inferred to be equal to OLS#1.
profile_level_tier_idx of OLS#1 to OLS#2 are the same so that profile_level_tier_idx of OLS#2 are inferred to be equal to OLS#1.
NumSubDpbs is equal to NumLayersInIdList[] since all layers's representaion format differ.
Use-case#1 (bit-saving case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 1 | 1 | N/A
Required bit-size on profile_level_tier_idx | 1 | 2 | 2 | 1 | 1 | 50.00%
Required bit-size on DPB Size syntax element | 64 | 2 | 128 | 1 | 64 | 50.00%
 |  | Total size | 130 |  | 66 | 49.23%

## Slide 14: Use-case#1 (bit-overhead scenario)
Use-case#1:
1) There are two output layer sets (OLS#1,OLS#2) associated with the same layer set (LS#1), which have different AltOptLayerFlag (Alt) values. and the same output layers (OptLayer).
LS#1 = { Layer0, Layer1},
OLS#1 = { LS#1, OptLayer={Layer1}, Alt=1},
OLS#2 = { LS#1, OptLayer={Layer1}, Alt=0}
OLS#2 is an additional output layer set against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are explicitly signaled
( ptl_dpb_info_present_flag is 1 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#3 are explicitly signaled although DPB sizes of OLS#1 to OLS#2 are the same
profile_level_tier_idx of OLS#1 to OLS#3 are explicitly signaled although profile_level_tier_idx of OLS#1 to OLS#2 are the same.
NumSubDpbs is equal to NumLayersInIdList[] since all layers's representaion format differ.
Use-case#1 (bit-overhead case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 1 | 1 | N/A
Required bit-size on profile_level_tier_idx | 1 | 2 | 2 | 2 | 2 | 0.00%
Required bit-size on DPB Size syntax element | 64 | 2 | 128 | 2 | 128 | 0.00%
 |  | Total size | 130 |  | 131 | -0.77%

## Slide 15: Use-case#2 (bit-saving scenario)
Use-case#2:
1)There are three output layer sets (OLS#1,2,3) associated with the same layer set (LS#1), which have the same AltOptLayerFlag and different output layers:
- LS#1 = { L#0, L#1, L#2},
- OLS#1 = { LS#1, OptLayer={L#0, L#1 L#2}, Alt=0} ,
- OLS#2 = { LS#1, OptLayer={L#1,L#2}, Alt=0} , - OLS#3 = { LS#1, OptLayer={L#0,L#2}, Alt=0}
OLS#2 and OLS#3 are additional output layer sets against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are inferred and omitted
( ptl_dpb_info_present_flag is 0 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#3 are the same so that DPB size of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
profile_level_tier_idx of OLS#1 to OLS#3 are the same so that profile_level_tier_idx of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
NumSubDpb is equal to 1 since all layers' representation formant are the same.
Use-case#2 (bit-saving case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 2 | 2 | N/A
Required bit-size on profile_level_tier_idx | 1 | 3 | 3 | 1 | 1 | 66.77%
Required bit-size on DPB Size syntax element | 124 | 3 | 372 | 1 | 124 | 66.77%
 |  | Total size | 375 |  | 127 | 66.13%

## Slide 16: Use-case#2 (bit-overhead scenario)
Use-case#2:
1)There are three output layer sets (OLS#1,2,3) associated with the same layer set (LS#1), which have the same AltOptLayerFlag and different output layers:
- LS#1 = { L#0, L#1, L#2},
- OLS#1 = { LS#1, OptLayer={L#0, L#1 L#2}, Alt=0} ,
- OLS#2 = { LS#1, OptLayer={L#1,L#2}, Alt=0} , - OLS#3 = { LS#1, OptLayer={L#0,L#2}, Alt=0}
OLS#2 and OLS#3 are additional output layer sets against OLS#1.
2) profile_level_tier_idx/DPB size for additional output layer sets are explicitly signaled
( ptl_dpb_info_present_flag is 1 for additional output layer sets)
Assumption:
num. of sub-layers is equal to 4.
DPB sizes of OLS#1 to OLS#3 are the same so that DPB size of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
profile_level_tier_idx of OLS#1 to OLS#3 are the same so that profile_level_tier_idx of OLS#2 to OLS#3 are inferred to be equal to OLS#1.
NumSubDpb is equal to 1 since all layers' representation formant are the same.
Use-case#2 (bit-saving case) |  |  |  |  |  | 
Required bit-size for OLS#1 to OLS#2 |  | Ref. (SHVC/MV-HEVC) |  | Proposal |  | bit-saving
 | bits/OLS | Counts | Total size (bits) | Counts | Total size (bits) | 
Required bit-size on ptl_dpb_info_present_flag | 1 | 0 | 0 | 2 | 2 | N/A
Required bit-size on profile_level_tier_idx | 1 | 3 | 3 | 3 | 3 | 0.00%
Required bit-size on DPB Size syntax element | 124 | 3 | 372 | 3 | 372 | 0.00%
 |  | Total size | 375 |  | 377 | -0.53%